## Slide 1: JCTVC-V0046 On the CU-level escape flag in the palette mode
Yao-Jen Chang, Jih-Sheng Tu, Chun-Lung Lin and Ching-Chieh Lin
Geneva Oct. 2015

## Slide 2: escape flag in palette mode(1/2)
In current HEVC-SCC:
if( CurrentPaletteSize != 0 )
palette_escape_val_present_flag
escape flag
  The condition check was added in HEVC SCC Draft Text 2
    To prevent getting the invalid syntax value while palette size
    and escape flag are equal to zero.
palette size
Notes: In this case the decoder behaviour is undefined, and the decoder may crash.
<number>

## Slide 3: escape flag in palette mode(2/2)
However, in current design(HEVC SCC Draft Text 4) :
  If the palette size is equal to zero
    code mode flag -> 0
    palette index -> 0
    palette run -> NxN-1
  There is no invalid syntax value!

## Slide 4: proposed parsing process
  The condition check is redundent
Remove the condition check while parsing the escape flag
Notes: The proposed change doesn’t affect the performance results. Therefore, it no needs to show the simulation results.
<number>

## Slide 5: Conclusions
The proposed syntax modification can remove one redundant condition check
Make the syntax simpler and cleaner
Notes: <number>

## Slide 6: Thank You!
<number>