## Slide 1: On bi-prediction restriction when intra block copy is enabled
JCTVC-V0048
K. Rapaka, V. Seregin, R. Joshi, M. Karczewicz (Qualcomm)

## Slide 2: Introduction
In the current WD, an 8x8 bi-prediction restriction is applied
  when IBC is enabled (i.e curr_pic_as_ref_enabled_flag is equal to 1) or
  adaptive motion vector resolution is enabled (i.e use_integer_mv equal to 1)
This restriction reduces worst-case memory accesses by 7-9% when IBC is used.
This proposal, proposes to relax existing 8x8 bi-prediction restriction based on the characteristic of the motion vector.

## Slide 3: Proposal
In this contribution, it is proposed to improve the current bi-prediction restriction for intra block copy as follows:
  The 8x8 bi-prediction is restricted when all of the following conditions are true:
    IBC is enabled for the current block based on slice, picture or sequence level IBC control
    use_integer_mv is equal to zero for the current slice
    Both MVs of an 8x8 bi-predicted block are
      not integer-pel (fractional-pel accuracy)
      not equal
      not from the same reference picture

## Slide 4: Experimental Results – 444 CTC
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.2% | -0.2%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.2%
RGB, Animation, 720p | -0.5% | -0.6% | -0.6%
RGB, camera captured, 1080p | -0.2% | -0.3% | -0.2%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.2% | -0.3% | -0.2%
YUV, Animation, 720p | -0.3% | -0.3% | -0.4%
YUV, camera captured, 1080p | -0.2% | -0.1% | -0.2%
Enc Time[%] | 102% |  | 
Dec Time[%] | 100% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.2% | -0.3%
RGB, mixed content, 1440p & 1080p | -0.6% | -0.5% | -0.5%
RGB, Animation, 720p | -0.6% | -0.7% | -0.7%
RGB, camera captured, 1080p | -0.3% | -0.3% | -0.3%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.2% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.3% | -0.4% | -0.6%
YUV, Animation, 720p | -0.4% | -0.5% | -0.4%
YUV, camera captured, 1080p | -0.1% | -0.1% | -0.2%
Enc Time[%] | 102% |  | 
Dec Time[%] | 100% |  | 
444 Lossy Full frame IBC CTC
 | Random Access |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.2% | -0.2% | -0.2%
RGB, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.2%
RGB, Animation, 720p | -0.5% | -0.6% | -0.6%
RGB, camera captured, 1080p | -0.2% | -0.2% | -0.2%
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.2% | -0.2% | -0.1%
YUV, Animation, 720p | -0.3% | -0.3% | -0.4%
YUV, camera captured, 1080p | -0.1% | -0.1% | -0.2%
Enc Time[%] | 83% |  | 
Dec Time[%] | 84% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
RGB, text & graphics with motion, 1080p & 720p | -0.3% | -0.2% | -0.2%
RGB, mixed content, 1440p & 1080p | -0.6% | -0.5% | -0.4%
RGB, Animation, 720p | -0.6% | -0.8% | -0.8%
RGB, camera captured, 1080p | -0.2% | -0.3% | -0.3%
YUV, text & graphics with motion, 1080p & 720p | -0.3% | -0.2% | -0.3%
YUV, mixed content, 1440p & 1080p | -0.3% | -0.3% | -0.4%
YUV, Animation, 720p | -0.3% | -0.4% | -0.4%
YUV, camera captured, 1080p | -0.1% | -0.2% | -0.2%
Enc Time[%] | 95% |  | 
Dec Time[%] | 92% |  | 
444 Lossy local search IBC CTC

## Slide 5: Experimental Results – 420 CTC
 | Random Access |  | 
 | G/Y | B/U | R/V
YUV, text & graphics with motion, 1080p & 720p | -0.1% | -0.1% | -0.1%
YUV, mixed content, 1440p & 1080p | -0.1% | -0.2% | -0.1%
YUV, Animation, 720p | -0.2% | -0.4% | -0.2%
Enc Time[%] | 100% |  | 
Dec Time[%] | 102% |  | 
 | Low delay B |  | 
 | G/Y | B/U | R/V
YUV, text & graphics with motion, 1080p & 720p | -0.2% | -0.1% | -0.3%
YUV, mixed content, 1440p & 1080p | -0.3% | -0.1% | -0.1%
YUV, Animation, 720p | -0.2% | 0.1% | 0.0%
Enc Time[%] | 102% |  | 
Dec Time[%] | 103% |  | 
420 Lossy full frame IBC CTC

## Slide 6: On SW and WD mismatch
A mismatch between WD and the software is reported related to adoption of JCTVC-U0078 that was discovered during an offline discussion in the 22nd JCTVC meeting in Geneva.
The SCM 5.2 (as well as CE software) performs 8x8 bi-to-uni conversion of the final candidate list when 8x8 bi-prediction restriction is applied. This is in similar lines to HEVC v1 which also converts bi-to-uni for 8x4 bi-prediction merge candidates.
The WD text specification, however, does not apply bi-to-uni conversion of merge candidates resulting in mismatch with SCM 5.2.
We would like to bring this issue to the attention of experts to decide which way to proceed
  Align WD with software :- Bi-to-Uni conversion of merge candidates
  Align Software with WD: - No conversion and disallow usage of the merge candidate.

## Slide 7: Conclusion
It is reported that the proposed approach provides objective bit rate reductions of 0.5 % and 0.3% for Random access 720p Animation RGB and YUV categories, respectively over SCM-5.0 anchor. It is reported that the proposed approach provides objective bit rate reductions of 0.6 % and 0.4% for Low delay B 720p Animation RGB and YUV categories, respectively over SCM-5.2 anchor.
The worst case memory accesses of the proposed method based on JCTVC-U0175 are not increased over the current WD.
We would like to Thank MediaTek for cross-checking the proposal