## Slide 1: JCTVC-V0061 Simplification for the index of the MSB in the paletteRun binarization
Yao-Jen Chang , Ching-Chieh Lin , Chun-Lung Lin and Jih-Sheng Tu
Geneva, Switzerland
October, 2015

## Slide 2: Summary
In Warsaw meeting, there were comments
  Performance results for another modification, modifying one context-coded bin in palette_run_msb_id_plus1 as one bypass-coded bin, were not provided.
  No analyzing results were provided to evaluate whether the method has measurable benefit in the overall complexity of the decoding process.
Four experimental results and the percentage of the reduced context coded bins are provided
  By removing three context coded bins, it can save up to 10.5% context coded bins
    with 0.1% BD-rates change on average

## Slide 3: Index map coding in palette mode
Palette run type flag and palette run value are signalled for index map coding.
Palette run value is derived by the most significant bit(MSB) index and the refinement bits.
  palette_run_msb_id_plus1
  palette_run_refinement_bits

## Slide 4: Issues on coding the palette run value
The first five bins of MSB index are context coded.
If the context-coded bins are getting less, the processing time could be getting shorter in hardware implementation.
binIdx | 0 | 1 | 2 | 3 | 4 | > 4
palette_run_type_flag = COPY_ABOVE_MODE | 5 | 6 | 6 | 7 | 7 | bypass
palette_run_type_flag = COPY_INDEX_MODE | 0,1,2 | 3 | 3 | 4 | 4 | bypass
Table 9-50

## Slide 5: Proposed Modifications(1/2)
Modification 1:
Modification 2:
<number>
Table 9-50
binIdx | 0 | 1 | 2 | 3 | > 3
copy_above_palette_indices_flag = = 1 | 5 | 6 | 7 | 7 | bypass
copy_above_palette_indices_flag = = 0 | 0,1,2 | 3 | 4 | 4 | bypass
Table 9-50
binIdx | 0 | 1 | 2 | > 2
copy_above_palette_indices_flag = = 1 | 5 | 6 | 7 | bypass
copy_above_palette_indices_flag = = 0 | 0,1,2 | 3 | 4 | bypass

## Slide 6: Proposed Modifications(2/2)
Modification 3:
Modification 4:
<number>
Table 9-50
Table 9-50
binIdx | 0 | 1 | > 1
copy_above_palette_indices_flag = = 1 | 6 | 7 | bypass
copy_above_palette_indices_flag = = 0 | 0,1,2,3 | 4,5 | bypass
binIdx | 0 | > 0
copy_above_palette_indices_flag = = 1 | 7 | bypass
copy_above_palette_indices_flag = = 0 | 0,1,2,3,4,5,6 | bypass

## Slide 7: Y-BD-rate comparisons for four modifications
 | Y-BD-rate results for modifications |  |  | 
 | Mod. 1 | Mod. 2 | Mod. 3 | Mod. 4
RGB, text & graphics with motion, 1080p & 720p | 0.0% | 0.1% | 0.1% | 0.5%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.1% | 0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, text & graphics with motion, 1080p & 720p | 0.1% | 0.1% | 0.3% | 0.7%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.1% | 0.2%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 100% | 100% | 100% | 100%
Dec Time[%] | 100% | 100% | 100% | 101%
<number>

## Slide 8: Analysis for our modifications
<number>
The bins changed from context mode to bypass mode over all context-coded bins of all coding modes
 | 5th bit (Mod. 1) | 4th – 5th bit (Mod. 2) | 3rd – 5th bit (Mod. 3) | 2nd – 5th bit (Mod. 4)
RGB, text & graphics with motion, 1080p | 1.4% | 4.0% | 7.8% | 13.1%
RGB, text & graphics with motion, 720p | 0.6% | 1.8% | 3.6% | 6.3%
YUV, text & graphics with motion, 1080p | 2.0% | 5.4% | 10.5% | 17.6%
YUV, text & graphics with motion, 720p | 1.0% | 2.6% | 5.2% | 9.0%
Average | 1.2% | 3.4% | 6.8% | 11.5%

## Slide 9: Conclusions
Four modifications for coding the MSB id of the palate run value are evaluated to clarify the proposed method.
For Modification 3, our analysis shows that it could save up to 10.5% context coded bins, with small BD-rate changes.
Thank Nokia for cross check
Notes: Still need some improvements for the third bullet.
<number>

## Slide 10: Thank You
<number>