## Slide 1: [JCTVC-V088] Tile level rate control for multi-core platform
Ismail Marzuki, Yong-Jo Ahn, Woong Lim, and Donggyu Sim
KWU (Kwangwoon University)

## Slide 2: Introduction
R-lambda model was defined for current rate control framework of HM
However, the rate control method does not consider the tile level rate control yet
Even though the rate control algorithm achieves target bitrates, the tile level rate control should be considered to complete the functionality of tile
This contribution proposes a tile level rate control for HEVC

## Slide 3: Rate control of HEVC reference model (HM)
Multi-level bit allocation for rate control of HM
  GOP-level, Picture-level, CTU-level
  In each level, model parameters are updated after encoding

## Slide 4: Motivation
Motivation
  The current R-lambda model rate control of HM is designed without any consideration of the tile level rate control for multi-core platform.
  Practically, tile partition for multicore degrades the video quality
    It might be due to the number of the encoder output bits abnormally changed degrading the video quality
The proposed method
  Investigates tile level rate control for multi-core platform for HEVC

## Slide 5: Tile level rate control for HEVC
Proposed RC is based on the leaky bucket model same as well
  GOP level
    Budget control for a GOP
  Picture level
    Budget control for a picture
    Decide QP based R-Lambda model
  Tile level
    Budget control for a tile estimated from the frame level
  Coding tree unit (CTU) level
    Decide QP based R-Lambda model

## Slide 6: Block-diagram of the proposed method

## Slide 7: Details of the proposed method
For GOP, picture, and CTU level bit allocation
  There is no any changing for each level
  They are the same with the current rate control framework
For tile level bit allocation:
  The bit allocation of each tile is based on the predetermined weight form the picture level rate control
  The target bit of the current tile is determined by:

## Slide 8: Conclusion
This contribution proposes a tile level rate control for HEVC.
For further works:
  this contribution will be further studied with complete reports and performance evaluations altogether under the common test condition for HEVC