## Slide 1: Request for the creation of additional profiles inside HEVC V0098（Originally M36981）
G.Barroux, K.Kazui, and K.Takeuchi
FUJITSU LABORATORIES LTD.
Oct. 2015

## Slide 2: Summary
Proposal on new HEVC profiles for Extended Range Scalable coding
Based on the lossless profiles first required in the past meetings
Less constrains for a broader usage

## Slide 3: Technical details
Basic copy of format range extension profiles with scalable constraints
Various scalabilities supported
  Quality, Spatial, Temporal
No additional constrain on the number of layers
  But more than 4 does not seem to meet any need
Chroma format ranging from 4:0:0 to 4:4:4
Bit depth ranging from 8 to 16 bits
No scalable still picture
No scalable intra only profiles

## Slide 4: Market needs
Video conferencing already uses such profiles in AVC
Medical imaging has non 4:2:0 8bits content and needs scalability
  Lossless can be better encoded if scalability can be used
    9.3% gain for 4:0:0/12-bit and 4:0:0/16-bit medical images from OsiriX
    9.0% gain for 4:0:0/12-bit and 4:0:0/16-bit medical images from Siemens
    0.8% gain for 4:4:4/10-bit RExt sequences
    -0.4% gain for 4:2:0/8-bit HM sequences
  Medical image archiving
  Video production
  Remote sensing
  Patient data sharing
    E.g. facilities in remote locations with bad network coverage

## Slide 5: Support
Last meeting:
  Fujitsu proposed
  Vidyo orally supported
  Vitech orally supported
  Thales said they may be interested but need to make some tests
This meeting
  Fujitsu still proposes
  Vidyo has made a written statement to add more visibility to their support

## Slide 6: time constrained from DICOM
Fujitsu is standardizing HEVC inside DICOM
Scalability is a big addition to the set of additional capabilities offered
If this proposal is not accepted at this meeting
  No Scalable + Range Ext in the next HEVC standard in February
  No possible standardization of the tools in DICOM
  => Either no HEVC in DICOM (low chances though)
  Or small support but with a big missed opportunity for greater tools
Fujitsu requests the acceptance of this profile at this meeting
  We are ready to put in the necessary hours to write the specs

## Slide 7: Conclusion
Markets need Scalable + Range Extension
Additional functionalities and enhanced lossless coding
There will be Scalable + Range Extension profiles
  Now or in 2 years?
DICOM standardization pushes us to act fast to offer the best of HEVC
Support from market leaders