## Slide 1: JCTVC-W0042 SCC Encoder Improvement
Yao-Jen Chang, Po-Han Lin, Chun-Lung Lin, Jih-Sheng Tu and Ching-Chieh Lin
San Diego, USA
Feb. 2016
Notes: <number>

## Slide 2: HEVC-SCC
<number>
Adaptive color transform (ACT) is adopted into HEVC-SCC to convert one color-space to another one
  Improve the coding efficiency by reducing the correlations among three color components
  Applied to intra prediction mode, inter prediction mode
  Effective to 444 chroma format
Notes: <number>

## Slide 3: Intra prediction mode
<number>
444 chroma format
  Intra Prediction Mode without ACT
  Intra Prediction Mode with ACT
Non-444 chroma formats
  Intra Prediction Mode without ACT
Notes: <number>

## Slide 4: Adopted method in JCTVC-U0095
<number>
  JCTVC-U0095 was adopted to skip the checking of the smaller TU sizes for Intra Prediction Mode with ACT if the CU sizes are greater than 16x16
  Substantially improve the encoder complexity
  Effective to 444 chroma format only
The checking of the smaller TU sizes is also complicated for Intra Prediction Mode in non-444 chroma formats
This contribution applies the adopted method in JCTVC-U0095 to Intra Prediction Mode in non-444 chroma formats
Notes: <number>

## Slide 5: The proposed modification in non-444 chroma formats
<number>
If the CU size is greater than 16x16, then skips the checking of the smaller TU sizes for Intra Prediction Mode without ACT in non-444 chroma formats
  A large CU coded by intra prediction mode usually implies the content in the area is not complex
Notes: <number>

## Slide 6
On top of SCM 6.0 anchor
Compared to SCM6.0 anchor, up to 3.2% encoding time is saved with 0.1 coding gain
Thank xxxxx for crosscheck!
<number>
 | All Intra |  |  | Enc time [%]
 | G/Y | B/U | R/V | 
YUV, TGM, 1080p & 720p | -0.1% | -0.1% | -0.1% | 96.8%
YUV, mixed, 1440p & 1080p | 0.0% | 0.0% | 0.1% | 97.5%
YUV, Animation, 720p | 0.0% | 0.1% | 0.1% | 97.3%
Enc Time[%] | 97% |  |  | 
Dec Time[%] | 100% |  |  | 
Results of AI Lossy, 420 chroma format
Notes: <number>

## Slide 7
On top of SCM 6.0 anchor
Compared to SCM6.0 anchor, up to 1.6% encoding time is saved without any coding change
Thank xxxxx for crosscheck!
<number>
 | Random Access |  |  | Enc time [%]
 | G/Y | B/U | R/V | 
YUV, TGM, 1080p & 720p | 0.0% | 0.0% | 0.0% | 98.4%
YUV, mixed, 1440p & 1080p | 0.0% | -0.1% | 0.4% | 99.0%
YUV, Animation, 720p | 0.0% | 0.3% | 0.2% | 99.0%
Enc Time[%] | 99% |  |  | 
Dec Time[%] | 100% |  |  | 
Results of RA Lossy, 420 chroma format
Notes: <number>

## Slide 8
On top of SCM 6.0 anchor
Compared to SCM6.0 anchor, up to 1.5% encoding time is saved with 0.2% coding change
Thank Microsoft for crosscheck!
<number>
 | Low delay B |  |  | Enc time [%]
 | G/Y | B/U | R/V | 
YUV, TGM, 1080p & 720p | 0.2% | 0.4% | 0.3% | 98.5%
YUV, mixed, 1440p & 1080p | 0.0% | 0.3% | 0.4% | 99.1%
YUV, Animation, 720p | 0.0% | 0.0% | -0.5% | 98.6%
Enc Time[%] | 99% |  |  | 
Dec Time[%] | 100% |  |  | 
Results of LB Lossy, 420 chroma format
Notes: <number>

## Slide 9
Adopted method: If the CU size ≥ NxN, then skips the checking of the smaller TU
On top of SCM 6.0 anchor (N = 32)
<number>
Re-tests of adopted method in JCTVC-U0095 (1)
 | Disabled |  |  | N = 64 |  |  | N = 16 |  |  | N = 8 |  | 
AI-lossy coding, 444 format | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, TGM, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.2% | 0.1% | 0.1%
RGB, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% | 0.2% | 0.2% | 0.2%
RGB, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1% | 0.2% | 0.2% | 0.2%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0% | 0.1%
YUV, TGM, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.3% | 0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
Enc Time[%] | 105% |  |  | 104% |  |  | 97% |  |  | 95% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 
Notes: <number>

## Slide 10
Adopted method: If the CU size ≥ NxN, then skips the checking of the smaller TU
On top of SCM 6.0 anchor (N = 32)
<number>
Re-tests of adopted method in JCTVC-U0095 (2)
 | N = 16, AI |  |  | N = 16, RA |  |  | N = 16, LB |  | 
Lossy coding, 444 format | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, TGM, 1080p & 720p | 0.1% | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1%
RGB, mixed content, 1440p & 1080p | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 0.1%
RGB, Animation, 720p | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, TGM, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% | -0.1% | -0.1% | 0.2% | -0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.3% | 0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Enc Time[%] | 97% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 99% |  |  | 100% |  | 
Notes: <number>

## Slide 11: Summary (1)
<number>
This contribution applies the adopted method of JCTVC-U0095 to Intra Prediction Mode without ACT in non-444 chroma formats
  JCTVC-U0095: skip the checking of the smaller TU sizes in Intra Prediction Mode with ACT in 444 chroma format
The simulation results show that there are 3% / 1% / 1% encoding time saving compared to SCM6.0 anchor in AI / RA / LB conditions, respectively, with -0.1% ~ 0.2% coding change
Notes: <number>

## Slide 12: Summary (2)
<number>
This contribution re-tests the adopted method of JCTVC-U0095 for different CU sizes
  JCTVC-U0095: skip the checking of the smaller TU sizes in Intra Prediction Mode with ACT in 444 chroma format if CU size ≥ NxN
The simulation results show that there are 3% / 1% / 1% encoding time saving compared to SCM6.0 anchor in AI / RA / LB conditions, respectively, with -0.1 ~ 0.1% coding change
Notes: <number>

## Slide 13: Thank you.
Notes: <number>