## Slide 1: JCTVC-W0042 SCC Encoder Improvement
Yao-Jen Chang, Po-Han Lin, Chun-Lung Lin, Jih-Sheng Tu and Ching-Chieh Lin
San Diego, USA
Feb. 2016
Notes: <number>

## Slide 2: HEVC-SCC
<number>
Adaptive color transform (ACT) is adopted into HEVC-SCC to convert residues from one color-space to another one
  Improve the coding efficiency by reducing the correlations among three color components
  Applied to intra prediction mode, inter prediction mode
  Enabled in 444 chroma format
Notes: <number>

## Slide 3: Intra prediction mode
<number>
444 chroma format
  Intra Prediction Mode without ACT
  Intra Prediction Mode with ACT
Non-444 chroma formats
  Intra Prediction Mode without ACT
Notes: <number>

## Slide 4: Adopted method in JCTVC-U0095
<number>
  JCTVC-U0095: it was adopted to skip the checking of the smaller TU sizes for Intra Prediction Mode with ACT if CU sizes ≥ 32x32
  Substantially reduce the encoder complexity
  Effective to 444 chroma format only
The checking of the smaller TU sizes is also complicated for Intra Prediction Mode in non-444 chroma formats
This contribution applies the same method to Intra Prediction Mode in non-444 chroma formats
Notes: <number>

## Slide 5: The proposed modification in non-444 chroma formats
<number>
If CU size ≥ 32x32, then skips the checking of the smaller TU sizes for Intra Prediction Mode in non-444 chroma formats
Notes: <number>

## Slide 6
On top of SCM 6.0 anchor
Up to 3.2% encoding time is saved with 0.1% coding gain
Thank Microsoft for crosscheck!
<number>
 | All Intra |  |  | Enc time [%]
 | G/Y | B/U | R/V | 
YUV, TGM, 1080p & 720p | -0.1% | -0.1% | -0.1% | 96.8%
YUV, mixed, 1440p & 1080p | 0.0% | 0.0% | 0.1% | 97.5%
YUV, Animation, 720p | 0.0% | 0.1% | 0.1% | 97.3%
Enc Time[%] | 97% |  |  | 
Dec Time[%] | 100% |  |  | 
Results of AI Lossy, 420 chroma format
Notes: <number>

## Slide 7
On top of SCM 6.0 anchor
Up to 1.6% encoding time is saved without any BD-rate change
Thank Microsoft for crosscheck!
<number>
 | Random Access |  |  | Enc time [%]
 | G/Y | B/U | R/V | 
YUV, TGM, 1080p & 720p | 0.0% | 0.0% | 0.0% | 98.4%
YUV, mixed, 1440p & 1080p | 0.0% | -0.1% | 0.4% | 99.0%
YUV, Animation, 720p | 0.0% | 0.3% | 0.2% | 99.0%
Enc Time[%] | 99% |  |  | 
Dec Time[%] | 100% |  |  | 
Results of RA Lossy, 420 chroma format
Notes: <number>

## Slide 8
On top of SCM 6.0 anchor
Up to 1.5% encoding time is saved with 0.2% BD-rate change
Thank Microsoft for crosscheck!
<number>
 | Low delay B |  |  | Enc time [%]
 | G/Y | B/U | R/V | 
YUV, TGM, 1080p & 720p | 0.2% | 0.4% | 0.3% | 98.5%
YUV, mixed, 1440p & 1080p | 0.0% | 0.3% | 0.4% | 99.1%
YUV, Animation, 720p | 0.0% | 0.0% | -0.5% | 98.6%
Enc Time[%] | 99% |  |  | 
Dec Time[%] | 100% |  |  | 
Results of LB Lossy, 420 chroma format
Notes: <number>

## Slide 9
Current SCM6.0: If CU size ≥ NxN (N=32), then skips the checking of the smaller TU sizes for ACT-enabled intra prediction mode in 444 format
If N=16: 1% ~ 3% coding time saving with -0.1% ~ 0.1% BD-rate change
<number>
Supplemental test results for the current SCM6.0 (1/2)
 | N = 16, AI |  |  | N = 16, RA |  |  | N = 16, LB |  | 
Lossy coding, 444 format | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, TGM, 1080p & 720p | 0.1% | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | -0.1%
RGB, mixed content, 1440p & 1080p | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 0.1%
RGB, Animation, 720p | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1%
RGB, camera captured, 1080p | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, TGM, 1080p & 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.0% | 0.0% | 0.0% | -0.1% | 0.1% | -0.1% | -0.1% | 0.2% | -0.1%
YUV, Animation, 720p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.3% | 0.2%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0%
Enc Time[%] | 97% |  |  | 99% |  |  | 99% |  | 
Dec Time[%] | 100% |  |  | 99% |  |  | 100% |  | 
Notes: <number>

## Slide 10
Current SCM6.0: If CU size ≥ NxN (N=32), then skips the checking of the smaller TU sizes for ACT-enabled intra prediction mode in 444 format
If N is set to the other values:
<number>
Supplemental test results for the current SCM6.0 (2/2)
 | N = 8 |  |  | N = 16 |  |  | N = 64 |  |  | Disable U0095 |  | 
AI-lossy coding, 444 format | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V | G/Y | B/U | R/V
RGB, TGM, 1080p & 720p | 0.2% | 0.1% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, mixed content, 1440p & 1080p | 0.2% | 0.2% | 0.2% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, Animation, 720p | 0.2% | 0.2% | 0.2% | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
RGB, camera captured, 1080p | 0.1% | 0.0% | 0.1% | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, TGM, 1080p & 720p | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, mixed content, 1440p & 1080p | 0.1% | 0.1% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, Animation, 720p | 0.1% | 0.3% | 0.2% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
YUV, camera captured, 1080p | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Enc Time[%] | 95% |  |  | 97% |  |  | 104% |  |  | 105% |  | 
Dec Time[%] | 100% |  |  | 100% |  |  | 100% |  |  | 100% |  | 
Notes: <number>

## Slide 11: Summary (1/2)
<number>
This contribution applies the adopted method of JCTVC-U0095 to non-444 chroma formats
  JCTVC-U0095: skip the checking of the smaller TU sizes in Intra Prediction Mode with ACT in 444 chroma format
3% / 1% / 1% encoding time saving compared to SCM6.0 anchor in AI / RA / LB conditions with -0.1% / 0.0% / 0.2% BD-rate change, respectively
Notes: <number>

## Slide 12: Summary (2/2)
<number>
This contribution tests the adopted method of JCTVC-U0095 for different CU sizes
  JCTVC-U0095: skip the checking of the smaller TU sizes in Intra Prediction Mode with ACT in 444 chroma format if CU size ≥ NxN
CU size ≥ 16x16: 3% / 1% / 1% encoding time saving compared to SCM6.0 anchor in AI / RA / LB conditions with -0.1 ~ 0.1% BD-rate change, respectively
Notes: <number>

## Slide 13: Thank you.
Notes: <number>