## Slide 1: JCTVC-W0062 Non-normative HM encoder improvements Note: Results for SAME CHANGES on JEM in JVET-B0039
K. Andersson, P. Wennersten, R. Sjöberg, J. Samuelsson, J. Ström, P. Hermansson, M. Pettersson

## Slide 2: Summary
It’s proposed to fix the misalignment between lambda and QP in HM for random access and low delay configurations. Doing that gives BD rate improvements of 1.8% for RA and 1.7% for LD. No effect on all intra since that already have good alignment. Bit allocation between temporal layers after the fix is roughly the same.
A second aspect is to increase the hierarchy for random access from 8 to 16 pictures. For that together with the fix of the misalignment its reported BD rate improvements of 7.1%. On a set of difficult sequences BD rate improvements of 4.8% is reported. In JVET-B0039 extension to a GOP of 32 pictures gives 9.7% BD rate improvements for HM.
It is also reported that subjective quality improvements have been seen by the authors. Planned to have a viewing on HM encodings using Samsung TV
The contribution proposes that both the fix to the misalignment between QP and lambda and the extension to a hierarchy of 16 pictures are included in the reference software for HEVC and used in the common test conditions.
Thanks to Microsoft for cross-check in JCTVC-W0117.

## Slide 3: Background
The reference software for HEVC (HM) uses a fixed QP setting while adjusting lambda according to the hierarchy length, the picture position in hierarchy and the QP value. For all intra coding the lambda is given by
0.57*2^(QP-12)/3 (Eq. 1)
It has previously been observed that the adjustment of lambda as in HM is suboptimal for for random access and low delay configurations in JCTVC-J0242 and HM therefore has a configuration file parameter “RecalculateQPAccordingToLambda” that when turned on recalculates QP for the given lambda.
A hierarchical coding structure with length of 8 for random access coding has been used during HEVC development. In JVT-P014 it was shown that performance can be improved by increasing the length of the hierarchy to 16, 32 and even 64.

## Slide 4: Fix QP to better correspond to lambda
Currently HM punishes pictures higher up in the hierarchy by using a higher lambda than what would correspond to the used QP. This produces a lot of skips since it is too expensive RD-wise to correct the distortion even if the distortion could have been corrected using a higher QP.
Numerical example for top layer for highest and lowest QP:
 | QP=26 | QP=41
HM random access | 471 | 3372
HM all intra | 415 | 2152
Value 1 de-quantized | 408 | 2304

## Slide 5: Fix QP to better correspond to lambda
We therefore suggest fix the misalignment between QP and lambda for random access and low delay configuration by recalculating the QP according to the given lambda using same relation between lambda and QP as for all intra coding.
The suggested fix or “RecalculateQPAccordingToLambda” in HM both produces average value close to the expected value:
 | QP=30 | QP=48
HM with QP fix | 640 | 4732
Value 1 de-quantized | 640 | 5120
 | QP=29 | QP=46
HM with “RecalculateQPAccordingToLambda” | 594 | 4204
Value 1 de-quantized | 576 | 4096

## Slide 6: PSNR Differences per temporal layer
Below it is shown how much the PSNR increases after fixing the misalignment between QP and lambda using same lambda as HM at an bitrate increase of 1.7%.
Temporal layer | 0 | 1 | 2 | 3
class D | 0.43 | 0.04 | 0.07 | 0.11
class C | 0.37 | 0.04 | 0.07 | 0.12
class B | 0.33 | 0.02 | 0.06 | 0.10
class A | 0.41 | -0.11 | -0.09 | 0.00
class F | 0.56 | 0.33 | 0.34 | 0.37
avg all | 0.42 | 0.06 | 0.09 | 0.14

## Slide 7: Bit allocation per temporal layer
As can be seen below the bit allocation is similar between HM and the proposal, its just that the QP better correspond to the used lambda in the proposal.
 | HM-16.6 |  |  |  |  | HM-16.6 with QP fix |  |  | 
Temporal layer | 0 | 1 | 2 | 3 |  | 0 | 1 | 2 | 3
avg ratio D | 0,59468 | 0,143634 | 0,164933 | 0,096754 |  | 0,616322 | 0,134696 | 0,155322 | 0,09366
avg ratio C | 0,555455 | 0,15144 | 0,180888 | 0,112217 |  | 0,578248 | 0,141851 | 0,17032 | 0,109581
avg ratio B | 0,632887 | 0,139896 | 0,152328 | 0,074889 |  | 0,665012 | 0,125985 | 0,138015 | 0,070988
avg ratio A | 0,559449 | 0,141515 | 0,177901 | 0,121136 |  | 0,591776 | 0,129919 | 0,164132 | 0,114173
avg ratio F | 0,659582 | 0,101889 | 0,132372 | 0,106158 |  | 0,675232 | 0,096302 | 0,1253 | 0,103167
avg all | 0,601957 | 0,135876 | 0,161239 | 0,100929 |  | 0,627208 | 0,125762 | 0,150018 | 0,097012

## Slide 8: RESULTS for fix and for “RecalculateQPAccordingToLambda”
Fix according to proposal
“RecalculateQPAccordingToLambda=1”
 | Random Access Main 10 |  | 
 | Y | U | V
Class A | -1,9% | -10,3% | -10,5%
Class B | -1,6% | -7,7% | -8,8%
Class C | -2,0% | -8,3% | -8,9%
Class D | -1,7% | -7,9% | -8,8%
Class E |  |  | 
Overall (Ref) | -1,8% | -8,5% | -9,2%
Class F (optional) | -1,6% | -5,6% | -5,4%
Enc Time[%] | 103% |  | 
Dec Time[%] | 98% |  | 
 | Low delay B Main 10 |  | 
 | Y | U | V
Class A |  |  | 
Class B | -1,6% | -4,9% | -5,0%
Class C | -1,8% | -5,5% | -6,1%
Class D | -1,4% | -4,7% | -5,1%
Class E | -2,2% | -3,9% | -4,3%
Overall (Ref) | -1,7% | -4,8% | -5,2%
Class F (optional) | -1,8% | -4,2% | -4,0%
Enc Time[%] | 84% |  | 
Dec Time[%] | 88% |  | 
 | Random Access Main 10 |  | 
 | Y | U | V
Class A | -1,9% | -6,7% | -8,2%
Class B | -1,7% | -5,3% | -6,3%
Class C | -2,2% | -5,1% | -5,2%
Class D | -1,8% | -5,3% | -5,6%
Class E |  |  | 
Overall (Ref) | -1,9% | -5,6% | -6,3%
Class F (optional) | -1,6% | -3,7% | -3,5%
Enc Time[%] | 103% |  | 
Dec Time[%] | 105% |  | 
 | Low delay B Main 10 |  | 
 | Y | U | V
Class A |  |  | 
Class B | -1,1% | -2,8% | -2,7%
Class C | -1,2% | -2,7% | -2,3%
Class D | -1,1% | -2,8% | -2,7%
Class E | -2,4% | -4,8% | -6,2%
Overall (Ref) | -1,4% | -3,1% | -3,3%
Class F (optional) | -1,3% | -2,2% | -2,5%
Enc Time[%] | 84% |  | 
Dec Time[%] | 97% |  | 

## Slide 9: Extending hierarchy for random access
It’s proposed to increase the hierarchy to 16 pictures instead of 8.
Impact:
  5 temporal layers instead of 4
  One additional frame store
  DPB size increased from 5 to 6 compared to a GOP 8 hierarchy
  Latency increase 8/60 second for a frame rate of 60 Hz and 8/24 second for a frame rate of 24 Hz
Results for JEM is presented in JVET-B0039. There also results for GOP 32 is presented.
 | Random Access Main 10 |  | 
 | Y | U | V
Class A | -5,7% | -12,9% | -14,1%
Class B | -7,1% | -13,6% | -17,3%
Class C | -8,3% | -13,0% | -13,1%
Class D | -7,4% | -14,4% | -15,0%
Class E |  |  | 
Overall (Ref) | -7,1% | -13,5% | -15,0%
Class F (optional) | -8,5% | -10,3% | -10,1%
Enc Time[%] | 96% |  | 
Dec Time[%] | 93% |  | 
 | Random Access Main 10 |  | 
 | Y | U | V
RedKayak | -6,1% | -19,1% | -15,1%
DuckTakeOff | -4,1% | -9,5% | -3,4%
Riverbed | -5,6% | -21,1% | -13,1%
Crowdrun | -3,4% | -7,2% | -7,7%
Overall | -4,8% | -14,2% | -9,8%
Enc Time[%] | 101% |  | 
Dec Time[%] | 100% |  | 

## Slide 10: Summary
It’s proposed to fix the misalignment between lambda and QP in HM for random access and low delay configurations. Doing that gives BD rate improvements of 1.8% for RA and 1.7% for LD. No effect on all intra since that already have good alignment. Bit allocation between temporal layers is roughly the same.
A second aspect is to increase the hierarchy for random access from 8 to 16 pictures. For that together with the fix of the misalignment its reported BD rate improvements of 7.1%. On a set of difficult sequences BD rate improvements of 4.8% is reported. . In JVET-B0039 extension to a GOP of 32 pictures gives 9.7% BD rate improvements for HM.
It is also reported that subjective quality improvements have been seen by the authors. Planned to have a viewing on HM encodings using Samsung TV
The contribution proposes that both the fix to the misalignment between QP and lambda and the extension to a hierarchy of 16 pictures are included in the reference software for HEVC and used in the common test conditions.
Thanks to Microsoft for cross-check in JCTVC-W0117.