## Slide 1
Robert Brondijk / Wiebe de Haan
Research
February 19, 2016
HDR CE7:
Philips cross check results

## Slide 2
CE7 cross checks and observations by Philips
Purpose:
Evaluate visual quality of SDR and HDR video from Hybrid Log-Gamma (HLG) in the following cases
CE7.1a: System gamma value of 1.6, OOTF only affects luminance
CE7.1b: Same, but both the color and the luminance may change
CE7.2a: Investigate effect of a system gamma of 1.2 and 1.4 (System of CE7.1a)
CE7.2b: Investigate effect of a system gamma of 1.2 and 1.4 (System of CE7.1b)
Additional observations are provided

## Slide 3
CE7 cross check results
CE7.1 sequences produced by BBC were easily replicated by Philips
  “High Bit Depth” macro in HM 16.7 had to be disabled
CE7.2 sequences produced by Philips were both cross checked by BBC
  MD5 sums and the metrics results were found OK
  Because the latest CE3 software was used, there were some slight differences in some of the objective numbers.

## Slide 4
Observations on CE7.1 (gamma = 1.6)
SDR quality impressions
CE7.1a (OOTF only affects luminance)
  SDR looks over-saturated
  Some color shifts (changing relation between R, G and B components)
CE7.1b (color and the luminance may change)
  SDR looks “washed out”
  Even more color shifts than with CE7.1a
Comparing HDR coding quality of CE7.1a and CE7.1b
For sequences like EBU Starting, the HDR was clearly not as good as the anchors: more blocking artifacts and the “lines over the stadium” disappeared much more than in the anchors, also there were color errors in the clouds
In Garage exit: the “power lines” in the background disappeared completely, unlike in the anchor.
In WarmNight, there are more blocking artifacts and there are visibly more color errors than in the Anchor.
The first impression was that the sequences seem to have a lower subjective quality than the anchors.

## Slide 5
CE7.1a and CE7.1b
CE7.1b
Gamma 1.6
CE7.1a
Gamma 1.6

## Slide 6
CE7.2 compared with CE7.1a and CE7.1b
SDR quality impressions
In general the test pictures with gamma 1.4 looked better than those with gamma 1.6
For some content a gamma of 1.2 looks better than gamma 1.4
Overall a gamma of 1.2 shows better SDR pictures than with a gamma of 1.6. The oversaturation that is seen with gamma 1.6 is much less or absent.
Comparing HDR coding quality of CE7.1a and CE7.1b
When comparing 7.2a with 1.2 and 1.6, sequences with 1.6 seem to be better than 1.2.
When comparing 7.2a to 7.2b, 7.2b seem to have less coding errors.
The first impression was that the sequences seem to have a lower subjective quality than the anchors.

## Slide 7
Comparison of 4 versions
CE7.1b
Gamma 1.6
CE7.1a
Gamma 1.6
CE7.2b
Gamma 1.4
CE7.2a
Gamma 1.2

## Slide 8
Further experiments
Some “HDR” still images were generated by Philips
  400 nit peak to be encoded in a “4000 nit HLG” container
  Allows for evaluation of the rendering of large areas
  Input images created as linear-light .exr files, converted from BT.709 to BT.2020 color space
  Images processed by the “type a HLG” chain with an OOTF gamma of 1/1.45 and output peak brightness set to 100 nit
  Rendered on a 100 nit “legacy” virtual display with a BT.1886 EOTF
  Converted back from BT.2020 to BT.709 color space

## Slide 9
HDR input
400 nit = 1.0

## Slide 10
SDR output
100 nit = 1.0

## Slide 11
HDR input, 400 nit = 1.0
HDR input, 970 nit = 1.0
SDR output, 100 nit = 1.0
Same “white” level
Note the “fluorescence”