## Slide 1
Results of CE5 3.1
R.Brondijk
Philips
februari 19, 2016

## Slide 2
High Level Functional Diagram of the Pre- and Post Processing for Y”u”v”

## Slide 3
Issues of a Color Space
 | Y”u”v” | Y”CbCr | Y”FbFr | IPT-PQ
Color space | Contains all visible colors | Restricted to a BT.2020 gamut | Restricted to a BT.2020 gamut | Contains all visible colors
Luminance in Color | Uncoupled: except for low luminance to avoid coding of dark noise | Coupled: non-constant luminance | Coupled: non-constant luminance | Y is luminance, but the chroma correlates with the luminance
Constant-luminance issues due to 4:2:0 | No problem, almost 4:4:4 quality | Major problem near the edge of BT.2020 gamut | Major problem near the edge of BT.2020 gamut | Minor problem due to larger color gamut
Chromaticity for gamut mapping | Very easy to make (u’,v’) for gamut mapping | Not easy, must go through linear-light | Not easy, must go through linear-light | Not easy, must go through linear-light
Representation | 10 bits gives highest quality. Not more is needed and is independent of the luminance range. For lower bit-rates, less bits may be used, in trade of to avoid blocking artifacts at low bit-rates. | Depends on the luminance range: all three equal 10 bits, later 12 as luminance level increases | Depends on the luminance range: all three equal 10 bits, and 12 as luminance level increases | Depends on the luminance range: color may now be 9 bits, benefits from “re-shaping” = a form of dynamic tone mapping
Transmitter complexity | Medium, high bit-widths are needed to support linear light operations, but the operations themselves are of low complexity | Low, traditional processing with OETF replaced by ST.2084 PQ | Low, just a variation of Y”CbCr | Medium, just re-programming of existing matrices, but dynamic re-shaping is needed
Receiver complexity | Can be low, no linear-light needed, mostly lookup tables | Can be low, unless color space conversion is needed | Can be low, unless color space conversion is needed | High, always re-shaping and color space conversion needed

## Slide 4
Objective Metrics

## Slide 5
Subjective Observations
- In some sequences 9 bits Y outperforms 10 bits Y
Y
10 bits
Y
9 bits

## Slide 6
HM Issues
When setting U and V to 9 bits, the YUV output of the HM encoder was often corrupt: the picture was incorrect. A correct YUV file could only be reproduced by the HM decoder.
When setting Y to 9 bits, both the HM encoder and HM Decoder failed to produced a correct output (Perhaps coupled to “main 10”??)

## Slide 7
Conclusions
When using YCbCr, 10 bits is needed for all three components in order to reach the quality seen in the anchors.
For the low bit-rates, like those used for the anchors, when using Y”u”v”, the u”v” need only be 9 bits and in some cases, even the Y can also be 9 bits, to lower the quantization effects so as to match the quality of the anchor.
Open Question:
  Could an HM encoder optimization significantly increase the coding efficiency, and thereby lift the quality of Y”u”v” above that of anchors?