## Slide 1: Bottom-up hash value calculation and validity check
Wei Xiao, Bin Li and Jizheng Xu
Xidian Univ. and Microsoft Corp.

## Slide 2: Background
Hash-based motion estimation is used in SCM
  Hash value is generated for every possible block (8x8, 16x16, 32x32 and 64x64)
  Except for blocks that are simple (horizontally or vertically uniform)
    A validity check is used to tell if a block is simple or not
Computation for hash table generation
  Calculations for different block sizes are independent
  W*H*4 CRC
  W*H*4 validity check

## Slide 3: Hierarchical hash design
B: 2Nx2N
SB0-SB3: NxN
Original: Hash(B)=CRC[p(0,0), p(0,1), …, p(2N-1,2N-1)]
Proposed: Hash(B)=CRC[Hash(SB0), Hash(SB1), Hash(SB2), Hash(SB3)]

## Slide 4: Complexity reduction analysis
SCM
  4*W*H
Proposed
  2x2 CRC – W*H
  4x4 CRC – W/2*H/2
  8x8 CRC – W/4*H/4
  16x16 CRC – W/8*H/8
  32x32 CRC – W/16*H/16
  64x64 CRC – W/32*H/32
  Total: 1.33*W*H

## Slide 5: Bottom-up validity test
A 2Nx2N block’s result can be derived from 6 NxN blocks’ results

## Slide 6: Results – 4:4:4

## Slide 7: Results – 4:2:0