## Slide 1: JCTVC-W0129: SCC Level Limits Based on Chroma Format
Sachin Deshpande, Seung-Hwan Kim

## Slide 2
Introduction
HEVC SCC Draft: MaxDpbSize is calculated based on PicSizeInSamplesY to take advantage of available memory capacity
Proposal: MaxDpbSize is to be calculated considering the chroma format (Screen-Extended Main 10 4:4:4 profile)
Changes from previous contribution: MaxDpbSize is modified based only on chroma format (and not bit-depth)

## Slide 3
Results for MaxDpbSize from our proposal
Table 1- MaxDpbSize for various Scale Factors when sps_curr_pic_ref_enabled_flag=0
Proposed change allows to use larger DPB size
  Maximize the usage of available memory
  Support higher GOP structure where large DPB size is required (coding gain)

## Slide 4
Conclusion
Modification is proposed for MaxDpbSize calculation for Screen-Extended Main 10 4:4:4 profile to account for chroma format.
We propose to adopt the proposed approach in HEVC SCC Draft.

## Slide 5
Backup slide: Proposed Text Changes
A.4.2 Profile-specific level limits for the video profiles
…
The variable BrNalFactor, which represents the NAL bit rate scale factor, is set equal to CpbNalFactor * HbrFactor.
The variable MinCr is set equal to MinCrBase * MinCrScaleFactor ÷ HbrFactor.
The variable SFactor is defined as follows:
-If the bitstream or sub-layer representation is indicated to conform to the Screen-Extended Main 10 4:4:4 profile,
and if chroma_format_idc is equal to 1, SFactor is set equal to (1  2)
-Otherwise, SFactor is set equal to 1
When the specified level is not level 8.5, the value of
sps_max_dec_pic_buffering_minus1[ HighestTid ] + 1 shall be less than or equal to MaxDpbSize, which
is derived as follows:
if( PicSizeInSamplesY <= ( MaxLumaPs >> 2 ) ) MaxDpbSize = Min( 4 * maxDpbPicBuf/SFactor, 16 ) else if( PicSizeInSamplesY <= ( MaxLumaPs >> 1 ) ) MaxDpbSize = Min( 2 * maxDpbPicBuf/SFactor, 16 ) (A‑1) else if( PicSizeInSamplesY <= ( ( 3 * MaxLumaPs ) >> 2 ) ) MaxDpbSize = Min( ( 4 * maxDpbPicBuf/SFactor) / 3, 16 ) else MaxDpbSize = maxDpbPicBuf/SFactor

## Slide 6
Backup slide: MaxDpbSize from our proposal
Table 2- MaxDpbSize for various Scale Factors when sps_curr_pic_ref_enabled_flag!=0