## Slide 1: HLG issues
prepared by Jack Holm
liaison from the ICC to SC29
21 February 2016
<number>

## Slide 2: Ambiguities in reference display specifications
<number>
Minimum luminance upper limit is specified but then not required to be met
No upper limit on peak luminance
Definitions cited for background and surround specifications are not applicable
Ambient lighting tolerances are impractical

## Slide 3: Normative specification of OETF, EOTF and OOTF
<number>
Is overly restrictive and creates potential for conflict
Only EOTF should be normatively specified
Reference OETFs and OOTFs may be provided informatively, but should not be required
Content creators need to be able to control the look of the content communicated

## Slide 4: OOTF is simple Y gamma with RGB ratio preservation
generally, applying tone curves to RGB channels produces results that are preferred to applying gamma to luminance and preserving RGB ratios
<number>
Simple Y gamma with RGB ratio preservation
ACES system OOTF

## Slide 5: Confusion regarding purpose of OOTF
Says OOTF accounts for differences between scene and display viewing environment
ACES system OOTF
Scene-referred image in display environment

## Slide 6: Unclear where scene and artistic adjustments are done
Says HLG images are scene-referred and display independent
  If they are scene-referred, the only camera control allowed is exposure
    but exposure choices may depend on expected display dynamic range
Says all that is needed to match images on displays with different dynamic ranges and viewing environments is a simple gamma adjustment

## Slide 7: EOTF specification variable
OOTF incorporated in EOTF
OOTF gamma prescribed to change with peak luminance change
OOTF gamma allowed to change additionally with viewing environment, but no prescription
How to create content with unknown EOTF?
  Must be scene-referred, but this precludes creative control
How to convert to and from other HDR encodings with unknown HLG EOTF?

## Slide 8: Display compensation experiments flawed
Overly constrained
  Images presented to subjects from same exposure range with only simple gamma difference
    no extension of exposure range, the defining characteristic of HDR
  Subjects only allowed to adjust gamma
    forces tradeoff between mid-tone luminance and contrast
  Need to redo experiments with proper subject controls
More appropriate display compensation method is presented in same document as HLG
  Why not use it?

## Slide 9: Backward compatibility questionable
You can see an image if the 1886 EOTF is used, but it won’t look like the HLG image or the 2020 OETF - 1886 EOTF image
While the backward compatible result might be useful in a video truck to see where a camera is pointed or if there is a clipping problem, presenting it to end-users would be a huge step backwards in image quality
  Do we want this kind of “backward” compatibility?

## Slide 10
SDR reference image on SDR display
HLG image on SDR display, exposure 0-1
HLG image on SDR display, exposure 0-3
HLG image on SDR display, exposure 0-12

## Slide 11: OETF exposure scaling incorrect
Graphs presented use different exposure scaling for 2020 and HLG OETFs
  As if exposure has no effect on image appearance
Best HLG exposure range scaling for backward compatibility is approximately 0-3
  Not much HDR capability in highlights