## Slide 1: On profiles and per-feature Flags
Stephan Wenger Vidyo, Inc.

## Slide 2: Outline of Proposal
Enable dial-down of coding tool-set from established profile
Decide early to use only subset of coding tools allowed in profile
  Early: cap-exchange (when available), high-level standard, …
Indicate use (or non-use) of coding tools in SPS/VUI or similar
Encode using only indicated subset of coding tools
Decoder needs only to implement subset of coding tools indicated in SPS/VUI

## Slide 3: Motivation for profile dial-down
Business need for “Profile” with feature set below max abilities of standard
Can’t expect ITU/MPEG to create such new Profile quickly in many cases
  Technical concerns: Limited numbering space, etc.
  Slow acting committees, too much politics, last century approval processes, …
  Niche industry demands cannot be addressed in standards applicable to many/broader industries
  Result: non-compliant use of standard
RAND commitment and other licensing issues bound to (substantial) compliance with standard as set by ITU/MPEG
  Motivation for standard compliance beyond interop constraints (which are not relevant in many environments, including but certainly not limited to walled garden)
Not trying for perfect solution, but for a “better” one compared to today

## Slide 4: Profile Alternative: dial-up
H.263, as an example, has a fully functional video codec as baseline, plus
  13 optional modes, most (but not all) of which are known or suspected to be compatible with each other
  Some of the optional modes have submodes and parameters. Some of the submodes and parameters are mutually exclusive, others not
  In H.245, 7 pages of definitions of codepoints, 3 pages of examples
  Interop and implementation nightmare
  Therefore, profiling through
    H.263++ Annex X, IMTC, cross-vendor agreements, …
Not Viable

## Slide 5: Profile dial-down
In H.264/AVC baseline, 3 flags are used to constrain baseline
  Introduced to facilitate (HW-) decoder implementation
  Effectively created a profile “Constrained Baseline”
  Allowed creating a compliant Baseline decoder without implementing FMO, ASO, RS
  Even with this mechanism, patent holdup over minor features of standard has happened, but not AFAIK over FMO, ASO, RS.
In HEVC, no such flags
  Main profile is main profile is main profile; need to implement everything for full compliance

## Slide 6: Proposal 1/2
Assign a flag indicating non-use of an encoder-optional tool
  Fine granularity: accepted proposal, accepted syntax element, …
    shouldn’t allow too many additional decisions in pixel-oriented or bit-oriented ops
    But too coarse granularity defeats purpose
  Probably need to keep syntax unchanged—some syntax elements become fixed value or don’t care when mechanism is not used
    Otherwise flags would need to be in normative syntax
    Opens loopholes for smart lawyers :-(
  Expect hundreds of Flags
  Put flags, suitably entropy-coded, into VUI
    Flags describe whole bitstream, so no SEI
Encoder sets flags based on stream properties it created

## Slide 7: Proposal 2/2
The following applies at the time when a system has to decide whether or not to handle a bitstream
  Handle == Decode, forward, etc. Could be cap-exchange in a middlebox. Could also be set-top-box decoder chip level
If a decoder implements all of a profile, it does not have to look at VUI flags
If a decoder implements only parts of a profile, it has to look at VUI flags and decode only if it includes all the tools the dialed-down bitstream uses

## Slide 8: Outlook/Options
In the standard, need to define a compliant decoder as a decoder that either implements the full profile, or those parts of the profile that are used as indicated by the flags in the bitstream VUI
In the standard, could define a Profile by “dialing down” from full standard
  That’s what most of the profile definition does today anyway, flags would probably simplify the definition language of profiles