## Slide 1: JCTVC-X0062: Regional nesting SEI message
A. K. Ramasubramonian, J. Sole, Y.-K. Wang, D. Rusanovskyy, D.B. Sansli, M. Karczewicz (Qualcomm)
P. Andrivon, E. Francois (Technicolor)
W. de Haan, R. Brondijk (Philips)

## Slide 2: Motivation
Specify regions of pictures for application of SEIs/metadata
Carriage of SMPTE ST 2094-1 requires signalling of regions to which metadata would be applicable
  It would be good to not re-define region-related syntax elements for metadata/potential SEI for each of the applications in ST 2094-related applications
Existing SEI message (CRI) can be re-usable for SMPTE ST 2094-30 with some additional syntax elements
Existing SEI messages could also be used on a region-specific basis:
  Colour remapping SEI message
  Filter hint SEI message
  Tone mapping SEI message

## Slide 3: Design of regional nesting SEI message
Motivated by the scalable nesting SEI message
  A list of bitstream subsets: output operation points or a list of layers and max. temporal ID
  A set of SEI messages applicable to all the bitstream subsets specified in the SEI
Regional nesting SEI message
  List of regions in the picture
  A set of SEI messages applicable to all the regions in the SEI message

## Slide 4: Syntax
regional_nesting( payloadSize ) { | Descriptor
rns_id | u(16)
rns_num_rect_regions | u(8)
for( i = 0; i < rns_num_rect_regions; i++) { | 
rns_rect_region_id[ i ] | u(8)
rns_rect_left_offset[ i ] | u(16)
rns_rect_right_offset[ i ] | u(16)
rns_rect_top_offset[ i ] | u(16)
rns_rect_bottom_offset[ i ] | u(16)
} | 
num_seis_in_rns_minus1 | u(8)
for( i = 0; i <= num_seis_in_rns_minus1; i++ ) { | 
sei_message( ) | 
rns_num_data_bytes[ i ] | u(8)
for( j = 0; j < rns_num_data_bytes[ i ]; j++ ) | 
rns_data_byte[ i ][ j ] | u(8)
} | 
} | 
Regions
SEIs
Addn. syntax elements

## Slide 5: Example
There are 3 regions in a picture.
  Regions 1 and 2 has a set of applicable SEI messages (SEI_A, SEI_B, SEI_C, SEI_D)
  Region 3 has a different set of SEI messages (SEI_E, SEI_F, SEI_G)
Region 1
Region 2
List of regions
SEI_A SEI_B SEI_C SEI_D
List of SEI mesages
Region 3
List of regions
SEI_E SEI_F SEI_G
List of SEI messages
First instance of RNS SEI
Second instance of RNS SEI

## Slide 6: Additional syntax elements
In SMPTE ST 2094-1, applications (including SMPTE ST 2094-30) generally require signaling of application identifier, application version, targeted display characteristics.
It is proposed to have this flexibility so that an application standard may be able to define these accordingly.
… | 
num_seis_in_rns_minus1 | u(8)
for( i = 0; i <= num_seis_in_rns_minus1; i++ ) { | 
sei_message( ) | 
rns_num_data_bytes[ i ] | u(8)
for( j = 0; j < rns_num_data_bytes[ i ]; j++ ) | 
rns_data_byte[ i ][ j ] | u(8)
} | 

## Slide 7: An example of how SMPTE could specify rns_data_byte[ ]
… | 
num_seis_in_rns_minus1 | u(8)
for( i = 0; i <= num_seis_in_rns_minus1; i++ ) { | 
sei_message( ) | 
rns_num_data_bytes[ i ] | u(8)
for( j = 0; j < rns_num_data_bytes[ i ]; j++ ) | 
rns_data_byte[ i ][ j ] | u(8)
} | 
rns_num_data_bytes[ i ] | u(8)
for( i = 0; i < rns_num_data_bytes[ i ]; i++ ) | 
rns_data_byte | u(8)
application_identifier[ i ] | u(8)
application_version[ i ] | u(8)
for( c = 0; c < 4; c++ ) { | 
targeted_system_prim_chromaticity_x[ i ][ c ] | u(16)
targeted_system_prim_chromaticity_y[ i ][ c ] | u(16)
} | 
targeted_display_max_luminance[ i ] | u(16)
targeted_display_min_luminance[ i ] | u(16)
rns_num_data_bytes[ i ] = 22

## Slide 8: Conclusion
Proposed to specify the regional nesting SEI message for regions
  Can include existing SEI message, new SEI messages, and also user-data registered SEI messages
  We may avoid redefinition of region-related syntax elements in SEI messages
  Provides a carriage means for ST 2094-1
    Existing SEI (e.g. CRI) can be re-used for ST 2094-30