## Slide 1: Suggestion for a Technical Recommendation on HDR/WCG technology for SDR backward compatibility and display adaptation
D. Rusanovskyy (Qualcomm), A . Segall (Sharp), E. Francois (Technicolor)

## Slide 2: Motivations
HDR deployment being happening
  UHD Blu-Ray
  DVB UHD Phase2
  ATSC 3.0
  Proprietary solutions
Need for technologies offering SDR backward compatibility and display adaptivity
  Cf MPEG doc. N15084, “Reqts and Use Cases for HDR and WCG Content Coding”
  SDR devices widely deployed
  Proliferation of new display technologies, with various colour volume rendering capabilities
DVB liaison m38351
  Backwards compatibility to Standard Dynamic Range (SDR) UHD decoders
  Ask for inputs from MPEG and VCEG on HDR technologies

## Slide 3: Motivations
Document “Conversion and Coding Practices for HDR/WCG Video” focused on HDR BT.2020, YCbCr, ST 2084, NCL video JCTVC-W1017 does not addresses these features

## Slide 4: Technologies already investigated in JCTVC (not exhaustive list)
SHVC for purposes of HDR/WCG coding with backward compatibility
  HEVC version 2
  SHVC verification test results (CGS, SDR709-to-HDR2020), JCTVC-W0095
  Supplement to SHVC Verification Test (SDR2020-to-HDR2020), JCTVC-X0080
Responses to CfE addressing SDR BC
  m36263, m36266
SDR BC solutions investigated in CEs
  Core Experiment 2 on 4:2:0 YCbCr NCL fixed point for HDR Video Coding m15795, m37497, JCTVC-W0022
  Core Experiment 6 on non-normative post processing m15799, JCTVC-W0025, m37499
Exploratory Test Model (ETM)
  Description of the Exploratory Test Model (ETM) for HDR/WCG extension of HEVC, JCTVC-W0092
  Description of the reshaper parameters derivation process in ETM reference software, JCTVC-W0031

## Slide 5: Proposal
Provide guidance for non-normative pre- / post-processing, for purpose of backward compatibility and display adaptation, using signaling specified in HEVC standard
Produce a Technical Recommendation (TR) on HDR/WCG technology for backward compatibility and display adaptation
  Include technologies investigated by JCTVC, based on HEVC specification, and identified as relevant to address these features

## Slide 6: Tentative strawman
1. SDR backward compatibility
1.1 Single-layer solutions with metadata
1.2 Multi-layer solutions
2. Display adaptation
1.1 Display SDR compatibility
1.2 Display EDR compatibility

## Slide 7: Suggested timeline
June 2016 (Geneva)
  First draft version
Oct 2016 (Chengdu)
  Updated draft version
Jan 2017 (Geneva)
  Final version for approval