## Slide 1: Production Workflow
Note: Use of “1,000” nits is close to an optimal interop point. Let displays tonemap up or down from there.
HLG
“Raw” or
“Camera Log”
Hybrid Log Gamma (HLG) OETF
Mastering Reference Monitor
1,000 cd/m2
PQ
Rendering
(“DI”)
“Raw” or
“Camera Log”
PQ
Coding
System Gamma 1.2
For 1,000 cd/m2
(OOTF)

## Slide 2: HLG to PQ Conversion
HLG/2100 defines shaping scene light (OETF) & display processing (OOTF).
For a given reference display (e.g. 1000 cd/m2, 2000 cd/m2 4000 cd/m2) display light can be calculated.
Results in transparent conversion from HLG to PQ
We’re not going to demonstrate this since the math is reversible.
HLG
PQ
Display RGB Light values
Display RGB Light values
Direct PQ encoding

## Slide 3: PQ to HLG Conversion
Easy case: PQ content mastered at 1,000 nits
  Clear math for conversion to HLG 1,000 nits (with some edge of gamut adjustments)
More challenging case: PQ content mastered at 4,000 nits
  Common for MANY existing PQ-based studio titles
  BT.2100 & BBC say to convert with System Gamma of 1.45 for display on a 4,000 nit HLG display, but that won’t look right on the more common 1,000 nit HLG display
  Recommend doing a trim grade to 1,000 nits and converting at System Gamma of 1.2
HLG
PQ
Linear
RGB Display
Light
BT.2100 method
Preserve
relative R/G/B
Ratios
(via Y ratio)
HLG OETF
HLG Shaped
Scene Light
HLG Gamma Invert
Applies
Gamma-Log shape
4K -> 1K
(Invert PQ)
“Approved conversion”
from 4000 to 1000 nits
(HLG Inverse EOTF
system gamma = 1.2)
LW = 1000 nits
Clamp
RGB Range

## Slide 4: HLG Limitations on Saturated Colors
Translating from PQ back to scene light through HLG system gamma (in the HLG inverse EOTF) results in R/G/B scene light values out of range for HLG transfer function.
Dependent on amount of system gamma and whether PQ display referred content uses full 2020 color volume (extremely saturated).
There are modest examples of where saturated P3 begins to go out which may be possible to compensate for during format conversion.
4000 cd/m2 100% Rec2020 PQ volume
HLG Gamma 1.45 Representation
Y - Linear
u’
v’
Y - Linear
u’
v’

## Slide 5: Mapping to Display Luminance (log)
BT.2100 defines different system gammas for different HLG displays (footnote 5e)
BT.2390 describes adjusting EOTF for different displays by applying an EETF that tone maps prior to display (section 5.4.1)
PQ - Highlights affected by EETF
HLG - Entire image affected
by display system gamma
(w/EETF)

## Slide 6: Mapping to Display Luminance (stops)
HLG with system gamma mapping applies significant level shifts throughout the signal range (with dark detail shifting the opposite direction of bright detail):
PQ with EETF mapping preserves mids with steep highlight roll off. When ST 2086 metadata is available, could adjust the roll off to better match.
(EETF)
(system gamma)
Critical Region: flesh tones and diffuse whites

## Slide 10: Percentage of ICAS pixels exceeding HLG ɣ=1.2

## Slide 11: average value exceeding HLG ɣ=1.2