## Slide 1: Essential Omni-directional/360° video indication for AVC, HEVC elementary bitstreams
JCTVC-Y0023 / MPEG m38965

## Slide 2: Current use of Omni/360 video in AVC
Possible oversight: Unlike 3D/stereo-vision, currently no means to indicate that the coded video stream is intended for omni/360 presentation
Current omni/360 video applications apply AVC to code equi-rectangular (ERP) and cubic (CMP) video.
Most products assume ERP.
No metadata required for ERP in current applications other than what is already provided in sequence, VUI, and user_data bar data.
Demonstrations of omni/360 HEVC

## Slide 3: Example current devices that understand equi-rectangular projection (ERP) for 360-degree video playback
Platform | Since | How to engage
Sony Playstation 4 (PS4) | 14 Oct 2016 firmware update | User selects “VR mode” in Media Player. File formats supported for ERP: .mkv, .avi, .mp4, .m2ps, .m2ts, AVCHD, JPEG, BMP, PNG
GoPro player (JVET-D0177) | 2016 | Manual selection of VR type.
FaceBook | 2016 | Player under control of FaceBook. No metadata
YouTube VR | 2015 | Player under control of Google. No metadata

## Slide 4: 2D Frame (rectangle) to sphere…
..project to equally spaced spherical longitude lines only on the equator.
By classic map definition: longitude and latitude lines are equally spaced on the 2D rectangle.
Longitude (α)
Latitude (β)
β =0
α=0
+90°
(+π/2 radians)
-90°
(-π/2 radians)
-180° (-π)
+180° (+π)
Projection
mapping

## Slide 5: Why does 2:1 aspect ratio?
It’s the ratio between the circumference (along equator) and the half-circumference (pole-to-pole).
Sphere: radius = 1 radian

## Slide 6
void cart_to_sph(double x, double y, double z, S360_SPH_COORD * coord){
coord->lat = (float)RAD2DEG(acos(z));
if (coord->lat > 180) coord->lat = 180;
if (x < 0)
coord->lng = 180.0f - (float)RAD2DEG(-atan(y / x));
else if (x == 0){
if (y < 0)
coord->lng = 270;
else if (y == 0)
coord->lng = (z < 0 ? 270.0f : 90.0f);
else
coord->lng = 90;
} else /* x>0 */ {
coord->lng = (float)RAD2DEG(atan(y / x));
if (coord->lng < 0) coord->lng += 360;
}
if (coord->lng == 0) coord->lng = 0.01f;
if (coord->lng == 360) coord->lng = 359.99f;
}
https://github.com/Samsung/360tools/blob/master/src/360tools.c

## Slide 7: SEI syntax: AVC, HEVC static indicator for 360 degree video
vr_info (payloadSize) { | Descriptor
vr_info_type | ue(v)
} | 

## Slide 8: SEI semantics
vr_info_type | Projection map format
0 | undefined
1 | Equi-rectangular: Legacy
2.. | Reserved
This SEI message identifies the virtual reality projection mapping of the pictures of the CLVS.
vr_info_type, when not equal to 0, indicates the virtual reality projection mapping of the coded pictures of the CLVS.
NOTE: The presence of frame_packing_arrangement SEI and other indicators in the bitstream provide information for 3D (stereo view) presentation.

## Slide 9: SEI semantics continued…
croppedWidth
croppedHeight
pic_width_in_luma_samples
pic_height_in_luma_samples
0° horizontal
0° vertical
The output frame is centered at the 0-degree horizontal (α) and 0-degree vertical (β) virtual sphere location. Nominally, the full 360 degree sphere is mapped to the croppedWidth and croppedHeight portions of the coded pictures.
16:9 frame for UHD transport (over SDI)
Bar_info user_data SEI (as used in DVB) can distinguish active 2:1 picture area from the discarded letterboxes area

## Slide 10: Converting sample coordinates to spherical
Compute conformance window size:
  croppedWidth = pic_width_in_luma_samples − SubWidthC * ( conf_win_right_offset + conf_win_left_offset ) [HEVC spec. eq. D-28]
  croppedHeight = pic_height_in_luma_samples − SubHeightC * ( conf_win_bottom_offset + conf_win_top_offset ) [HEVC spec. eq. D-29]
To calculate the projected radian-unit longitude (α) and latitude (β) of sample location x,y in the decoded picture:
  α = ((x - SubWidthC * conf_win_left_offset)/croppedWidth - 0.5)*2*π;
  β = ((y - SubHeightC * conf_win_top_offset)/croppedHeight - 0.5)*π;

## Slide 11: Possible solutions…
Registered user data
new SEI, carry entries from CICP (Codec Independent Code Points) / OMAF (Omni-Directional Application Format),
  Define entry now with basic ERP entry now to close open issue with existing applications.
Extend existing structure (VUI or SEI)

## Slide 12: Equi-rectangular projection (ERP)
invented by Marinus of Tyre ~AD 100. (*)
(*): document number unavailable due library fire in Alexandria. Referred in [1].
Based on spherical to cube coordinate trigonometry [2]
-----------------------------------------------------------------
References
[1] Cladius Ptolmey, Geography, AD 150.
[2] Archimedes of S.., “Liaison statement to Babylonian royal court of standards.”, Doc. MCMXCVIII.