## Slide 1: [JCTVC-Y0026] Tile-Level Rate Control for Multi-core Platform on HM
Ismail Marzuki, Yong-Jo Ahn, Wahyu Wiratama, and Donggyu Sim
KWU (Kwangwoon University)

## Slide 2: Introduction
HEVC is introduced to significantly improve coding efficiency for higher video quality (FHD and UHD video contents)
  To meet this goal:
    HEVC has been developed with high computation load and memory requirements compared with H.264/AVC
  To cover the complexity issues:
    Tile-level parallelism has been widely considered to accelerate HEVC system, especially for real-time video applications
    However, tile partition defined in the entire sequence breaks all the dependencies
      Degrade the visual quality: Solved by in-loop filtering
      Degrade the compression rate: None
    In the tile-level multi-core platform case:
      Each tile must be independently encoded in different cores
      Rate control must also be separately executed on each core
      The total bits generated from each core must be taken into consideration to satisfy transmission environment constraints on the bitrate and video quality

## Slide 3: Motivation
R-λ model has been defined as the current rate control framework for HM
  However, this rate control model does not benefit the tile partition effects in losing coding efficiency
  R-λ model rate control cannot facilitate tile-level parallelism fashion
This contribution proposes a tile level rate control for HM on multi-core platform
  To maximize compression performance (i.e., better coding efficiency and/or better visual quality),
  It is important to consider tile-level rate control to control encoding processes for each tile
  Integrated with the current R-λ model rate control

## Slide 4: Rate control of HEVC reference model (HM)
Multi-level bit allocation for rate control of HM
  GOP-level, Picture-level, CTU-level
  In each level, model parameters are updated after encoding

## Slide 5: Block-diagram of the proposed method

## Slide 6: Proposed algorithm
For GOP, picture, and CTU level bit allocation
  They are kept the same as the current rate control framework
For the proposed tile level bit allocation:
  The bits allocation of each tile is designed based on the R-Lambda model rate control of HM 16.12
  Both Intra and Inter Picture are treated with different manners:
    Intra picture:
      we consider sum of SATD values of all CTUs in tile as tile complexity to adjust the number of bits
    Inter picture:
      tile-level bit allocation organizes bits for the tiles based on a weight ratio of the bits derived at the picture level.
      we also employ the actual generated bit of collocated tiles in the recently coded pictures (under random access configuration) when allocating bits for the current tile of the inter pictures.

## Slide 7: Details of the Proposed Algorithm
For intra picture:
  Each tile allocation bit is budgeted according to ratio of complexity measure and total remaining bits :
  Complexity ratio is calculated based on SATD of CTUs within a tile:

## Slide 8: Details of the Proposed Algorithm
For inter picture:
  Allocation bit for each tile in inter picture is estimated based on predefined weighting factor and :
  is priory estimated according to parameters of picture level rate control:

## Slide 9: Experimental conditions
Based on HM-16.12
Anchor: HM-16.12 without Tile-level rate control
Follow the common test condition of HM-16.12
  Use three tile configurations (4, 6, and 8 tile partitions)
  Tile configurations are set uniformly
  Class D is excluded
  Hierarchical bit is set adaptive for ratio bit allocation
  Configuration test: Random access and Low delay B

## Slide 10: Experimental results

## Slide 11: Experimental results
Table 3 Rate control accuracy of the proposed Tile-level rate control algorithm
Test case/ Tile partition | Sequence | Average of bitrate accuracy |  | Delta bitrate accuracy | Y-PSNR improvement
 |  | RC in HM-16.12 without tile-level RC | Proposed tile-level RC |  | 
RA-Main/ 4 Tiles | Class A | 0.54% | 0.73% | 0.19% | 0.00 dB
 | Class B | 0.78% | 1.05% | 0.27% | 0.12 dB
 | Class C | 0.36% | 0.60% | 0.23% | 0.11 dB
Average |  | 0.59% | 0.82% | 0.23% | 0.08 dB
RA-Main/ 6 Tiles | Class A | 0.56% | 0.73% | 0.17% | 0.01 dB
 | Class B | 0.79% | 1.06% | 0.27% | 0.12 dB
 | Class C | 0.36% | 0.61% | 0.25% | 0.11 dB
Average |  | 0.59% | 0.82% | 0.23% | 0.09 dB
RA-Main/ 8 Tiles | Class A | 0.55% | 0.75% | 0.20% | 0.02 dB
 | Class B | 0.78% | 1.07% | 0.29% | 0.12 dB
 | Class C | 0.36% | 0.61% | 0.25% | 0.11 dB
Average |  | 0.58% | 0.83% | 0.25% | 0.08 dB
LB-Main/ 4 Tiles | Class B | 0.06% | 0.12% | 0.06% | 0.03 dB
 | Class C | 0.15% | 0.18% | 0.04% | 0.02 dB
 | Class E | 0.24% | 0.28% | 0.03% | -0.05 dB
Average |  | 0.10% | 0.15% | 0.04% | 0.03 dB
LB-Main/ 6 Tiles | Class B | 0.07% | 0.13% | 0.03% | 0.05 dB
 | Class C | 0.15% | 0.18% | 0.02% | 0.01 dB
 | Class E | 0.66% | 0.66% | 0.06% | 0.06 dB
Average |  | 0.24% | 0.28% | 0.04% | 0.03 dB
LB-Main/ 8 Tiles | Class B | 0.07% | 0.13% | 0.06% | 0.05 dB
 | Class C | 0.15% | 0.18% | 0.03% | 0.01 dB
 | Class E | 0.24% | 0.29% | 0.03% | -0.05 dB
Average |  | 0.10% | 0.15% | 0.05% | 0.03 dB

## Slide 12: Conclusion
This contribution proposes a tile-level bit allocation of rate control to favour multi-core platform in HM
It is reported that the proposed tile-level rate control model can achieve:
  Coding gain, visual quality, and bitrate accuracy improvements in both random-access and low-delay configurations with negligible encoding time increased

## Slide 13: End of Presentation
Q&A