## Slide 1
JCTVC-Y0031: On MCTS extraction
Fraunhofer HHI
R. Skupin, Y. Sánchez, K.Grüneberg, C. Hellge, T. Schierl

## Slide 2: Motivation
Typically only subset of High-Res, high-FoV video is presented, e.g. on Phone, Tablet or TV
HEVC motion constrained tile sets (MCTS) do not constitute conformant HEVC bitstreams themselves
System specifications cannot rely on presence of “advanced” MCTS decoders
Joint MPEG Requirements & JCT-VC meeting at MPEG #115 decided to have JCT-VC work towards enabling extraction of MCTS to conformant HEVC bitstreams.

## Slide 3: System Examples
File Format (ISO/IEC FDIS 14496-15)
Implements sub-NALU extractors
Ability to re-assemble NALUs into new bitstream
Example:
Full video is stored as HEVC conformant track
Further tracks allow reading MCTS as HEVC conformant video
MPEG2 Transport Stream
Full video is broadcasted, individual ES per MCTS
ES buffer (i.e. CPB) is filled with selected ESs

## Slide 4: Proposal
To allow systems to use MCTS for derivation of HEVC conformant bitstreams, the following is proposed:
Add syntax for
    carriage of MCTS specific Parameter Sets
    carriage of MCTS specific SEI messages
add a MCTS extraction process based on the proposed syntax

## Slide 5: Proposal – MCTS_extraction SEI
Carriage of Parameter Sets: In-band variant

## Slide 6: Proposal – MCTS_extraction SEI
num_extraction_information_sets_minus1 indicates the number of information sets contained in the present mcts_extraction SEI to be applied in the mcts extraction process.
num_applicable_tile_set_identifiers_minus1 indicates the number of values of mcts_id of the tile sets that the following i-th information set applies to for the mcts extraction process.
mcts_identifier[ i ][ k ] indicates all num_applicable_tile_set_identifers_minus1 plus 1 values of mcts_id of the tile sets that the following i-th information set applies to for the mcts extraction process.
num_mcts_pps_replacements[ i ] indicates the number of pps identifier replacements signaling in the mcts_extraction SEI for the tile set with mcts_id equal to mcts_id_map[ i ].
mcts_pps_id_in[ i ][ j ] indicates the j-th value of the num_mcts_pps_replacements[ i ] pps identifiers in slice header syntax structures of the tile set with mcts_id equal to mcts_id_map[ i ] to be replaced in the mcts extraction process.
mcts_pps_id_out[ i ][ j ] indicates the j-th value of the num_mcts_pps_replacements pps identifiers in slice header syntax structures of the tile set with mcts_id equal to mcts_id_map[ i ] to replace pps identifiers equal to the value mcts_pps_id_in[ i ][ j ] in the mcts extraction process.

## Slide 7: Proposal – MCTS_extraction SEI
Carriage of Parameter Sets:
Nested variant

## Slide 8: Proposal – MCTS_extraction SEI
num_vps_in_message_minus1 indicates the number of vps syntax structures in the given mcts_extraction_nesting SEI to be used in the mcts extraction process.
num_sps_in_message_minus1 indicates the number of sps syntax structures in the given mcts_extraction_nesting SEI to be used in the mcts extraction process.
num_pps_in_message_minus1 indicates the number of pps syntax structures in the given mcts_extraction_nesting SEI to be used in the mcts extraction process.
mcts_pps_id_in[ i ][ j ] indicates the j-th value of the num_mcts_pps_replacements[ i ] pps identifiers in slice header syntax structures of the tile set with mcts_id equal to mcts_id_map[ i ] to be replaced in the mcts extraction process.
mcts_pps_idx_out[ i ][ j ] indicates that the picture Parameter Set with pps identifier equal to mcts_pps_id_in[ i ][ j ] is to be replaced with the mcts_pps_idx_out[ i ][ j ]-th signaled picture Parameter Set in the mcts_extraction_nesting SEI during the mcts extraction process.

## Slide 9: Proposal – mcts_nesting SEI
Carriage SEI messages:

## Slide 10: Proposal – mcts_nesting SEI
all_tile_sets_flag equal to 0 specifies that the mcts_identifier list is specified by mcts_identifier[ i ] for all tile sets defined within the bitstream. all_tile_sets_flag equal to 1 specifies that the list mcts_identifier[ i ] consists of all values of mcts_id[] of the temporal_motion_constrained_tile_sets SEI messages present in the current access unit.
tile_sets_max_temporal_id_plus1 minus 1 indicates the maximum temporal level to be extracted in the mcts extraction process for a tile set with mcts_id equal to an element of the array mcts_identifier[ i ].
num_applicable_tile_set_identifiers_minus1 plus 1 specifies the number of following mcts_identifier for which the following SEI messages are to be used in the mcts extraction process.
mcts_identifier[ i ] indicates all num_applicable_tile_set_identifiers_minus1 values of mcts_id for which the following SEI messages should be inserted when extracting the respective tile set with mcts_id equal to mcts_identifier[ i ] using the mcts extraction process.

## Slide 11: Proposal – Extraction Process
Input:
A bitstream.
Target MCTS identifier MCTSIdTarget.
Target layer identifier list layerIdListTarget.
Constraints or bitstream requirements:
tiles_enabled_flag equal to 1.
num_tile_columns_minus1 > 0 || num_rows_minus1 > 0.
MCTS SEI message with mcts_id[ i ] equal to MCTSIdTarget is present and associated with all pictures to be output.
MCTS with mcts_id[ i ] equal to MCTSIdTarget is present in bitstream.
Presence of mcts_extration(_nesting) SEI message for TMCTS with mcts_id[ i ] equal to MCTSIdTarget.
Process:
Remove all NAL units that do not belong to the tile set associated with mcts_id[ i ] equal to MCTSIdTarget.
Replace Parameter Sets according to mcts_extraction(_nesting) SEI message.
Adjust slice segment headers as follows:
  Exchange slice_pic_parameter_set_id in slice header according to mcts_extration(_nesting) SEI message.
  If necessary, adjust slice_segement_address and first_slice_segment_in_pic_flag to create a common picture plane from all rectangles in the tile set.
Replace SEI messages with SEI messages carried in mcts_nesting SEI.

## Slide 12: Proposal – Extraction Process
Persistance scope:
mcts_(nesting_)extraction: the remainder of the bitstream
mcts_nesting: the Access Unit containing the SEI messages

## Slide 13: Summary
System specificationw anticipate usage of MCTS to derive HEVC conformant bitstreams
Currently, no means for an encoder to signal respective information
The document proposes to add syntax to allow
carriage of MCTS specific Parameter Sets (mcts_extraction SEI)
carriage of MCTS specific SEI messages (mcts_nesting SEI) and a
MCTS extraction process