## Slide 1: JCTVC-Z0022 Chroma Adjustment for HDR Video
J. Ström, Per Wennersten, K. Andersson, R. Sjöberg, M. Pettersson,
Ericsson Research

## Slide 2: Background
Traditional subsampling of HDR data can give rise to luminance artifacts.
Small changes in the green component will affect all three components Y’, Cb and Cr.
original 4:4:4
traditional subsampling 4:2:0

## Slide 3: Luma adjustment
Luma adjustment can ameliorate this problem.
One side effect is that the luma often becomes more smooth.
Y’ frame 389
Y’ frame 390
Anchor 1.0
Y’ frame 389
Y’ frame 390
Anchor 3.2

## Slide 4: chroma
However, luma adjustment does not affect the chroma components.
They can vary quite a bit although the image looks flat.
Cb frame 389
Cb frame 390
RGB444 frame 389
RGB444 frame 390

## Slide 5: example
4:4:4 image
4:2:0 image (anchor 1.0)

## Slide 6: example
4:4:4 image
4:2:0 image (anchor 1.0)
We cannot tell the difference between these two

## Slide 7: example
4:4:4 image
4:2:0 image (anchor 1.0)
We cannot tell the difference between these two

## Slide 8: example
4:4:4 image
4:2:0 image (anchor 1.0)
Why not just use one of them, or the average?

## Slide 9: Main idea
Change an RGB444 color so that it is more similar to its neighbors.
Make the change small enough to be perceptually indistinguishable.
Then process the RGB444 image according to Anchor 3.2.
How to tell whether two colors are perceptually indistinguishable?
  Luminance:
    Calculate linear luminance , and check *
    Example: , where
[18] G. W. Larson, “The LogLuv Encoding for Full Gamut, High Dynamic Range Images”, Journal of Graphics Tools, 3(1):15-31, 1998.
* is the PQ EOTF, is the inverse of the PQ EOTF

## Slide 10: Main idea
Change an RGB444 color so that it is more similar to its neighbors.
Make the change small enough to be perceptually indistinguishable.
Then process the RGB444 image according to Anchor 3.2.
How to tell whether two colors are perceptually indistinguishable?
  Luminance:
    Calculate linear luminance , and check *
    Example: , where
[18] G. W. Larson, “The LogLuv Encoding for Full Gamut, High Dynamic Range Images”, Journal of Graphics Tools, 3(1):15-31, 1998.
Is equivalent to the quantization error (half a code step) for a gray color using 10-bit PQ.
* is the PQ EOTF, is the inverse of the PQ EOTF

## Slide 11: Main idea
Change an RGB444 color so that it is more similar to its neighbors.
Make the change small enough to be perceptually indistinguishable.
Then process the RGB444 image according to Anchor 3.2.
How to tell whether two colors are perceptually indistinguishable?
  Luminance:
    Calculate linear luminance , and check *
    Example: , where
  Chrominance
    Calculate CIE . According to Larson [18] a difference of 0.5/410 is indistinguishable for both and .
    Example: , where
[18] G. W. Larson, “The LogLuv Encoding for Full Gamut, High Dynamic Range Images”, Journal of Graphics Tools, 3(1):15-31, 1998.
Is equivalent to the quantization error (half a code step) for a gray color using 10-bit PQ.
* is the PQ EOTF, is the inverse of the PQ EOTF

## Slide 12: In detail.
For every linear RGB color in 444:
  Calculate and so that every color where satisfies that
    Luminance measure differs less than 0.5/876
    Chrominance measure differs less than 0.5/410 in both and
  Replace G with the average G of the neighborhood clamped against :
  Average/clamp happens twice, then repeated for blue and green.
neighboring -values
average
average of neighbors
clamp against
Replace with this value.

## Slide 13: Main idea
Change an RGB444 color so that it is more similar to its neighbors.
Make the change small enough to be visually negligible.
Then process the RGB444 image according to Anchor 3.2.
RGB 4:4:4
chroma adjustment
RGB 4:4:4
anchor 3.2 processing
Y’CbCr 4:2:0
visually similar

## Slide 14: results: smoother chroma
Cb frame 389
Cb frame 390
Anchor 1.0/Anchor 3.2
Cb frame 389
Cb frame 390
Chroma adj. + Anchor 3.2 (, )
More similar to each other

## Slide 15: results: smoother chroma
Cb frame 389
Cb frame 390
Anchor 1.0/Anchor 3.2
Cb frame 389
Cb frame 390
Chroma adj. + Anchor 3.2 (, )
Even more similar

## Slide 16: Results: Luma Smoother Too
Anchor 1.0
Anchor 3.2
Chroma adj. + Anchor 3.2 (, )

## Slide 17: Results: Luma Smoother Too
Y’ frame 389
Y’ frame 390
Anchor 1.0
Anchor 3.2
Y’ frame 389
Y’ frame 390
Y’ frame 389
Y’ frame 390
Chroma adj. + Anchor 3.2 (, )
More similar to each other

## Slide 18: Results: Visual results after compression improve
Anchor 1.0
Anchor 3.2
Chroma adj. + Anchor 3.2 (, )
uncompressed 4:4:4

## Slide 19: Results: Helps with mismatching filters
Replication of experiment in JCTVC-X0043
TM-filters in luma adjustment step and Lanczos-2 in decoder

## Slide 20: Results: Helps with mismatching filters
TM-filters in luma adjustment step and Lanczos-2 in decoder
Anchor 1.0
Anchor 3.2
Chroma adj. + Anchor 3.2
uncompressed 4:4:4

## Slide 21: objective results
BT.709 or P3 content in a BT.2020 container
  Effect should be limited, since colors are not saturated
BT.709 content in BT.709 container
  More similar to content filling out the BT.2020 container
 | tPSNRX | tPSNRY | tPSNRZ | tPSNRXYZ | OSNRXYZ | DE100 | MD100 | L100
All | -0.1% | -0.1% | 0.2% | 0.0% | 0.1% | 0.7% | -4.4% | -0.1%
 | tPSNRX | tPSNRY | tPSNRZ | tPSNRXYZ | OSNRXYZ | DE100 | MD100 | L100
All | -0.8% | -0.7% | -0.7% | -0.8% | -0.7% | -0.5% | -3.8% | -0.5%
 | tPSNRX | tPSNRY | tPSNRZ | tPSNRXYZ | OSNRXYZ | DE100 | MD100 | L100
All | -2.5% | -2.4% | -0.6% | -2.0% | -1.6% | -0.3% | 22.0% | -1.7%

## Slide 22: Summary
We present a preprocessing step called chroma adjustment.
It happens before Anchor 3.2 processing starts.
The output RGB 4:4:4 should be visually identical to the input RGB 4:4:4
The output is then processed according to Anchor 3.2.
RGB 4:4:4
chroma adjustment
RGB 4:4:4
anchor 3.2 processing
Y’CbCr 4:2:0
visually similar

## Slide 23: Summary
Chroma becomes smoother and easier to predict
Luma becomes smoother and easier to predict
Subjective quality of compressed material improves
Lowers impact of possibly mismatching filters
Objective gains for BT.709 content in BT.709 container
  2.4% tPSNR-Y

## Slide 25: Does it desaturate colors?
General answer: no
Some colors become more saturated, others less
Large areas of the same color will not be affected at all (change goes only 4 pixel deep)

## Slide 26: Does it desaturate colors?
General answer: no
Some colors become more saturated, others less
Large areas of the same color will not be affected at all (change goes only 4 pixel deep)

## Slide 27: Results
anchor 1.0
chroma adjustment
chroma adjustment + luma adjustment

## Slide 28: What is happening?
Two neighboring pixels:
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 29: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 30: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
Quite similar
Quite different
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 31: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 32: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
After converting back to RGB:
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 33: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
After converting back to RGB:
Quite similar
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 34: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
After converting back to RGB:
Quite similar
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 35: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
After converting back to RGB:
Quite similar
Conclusion:
Just averaging is not a problem.
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 36: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
Average Cb/Cr, non-average Y’:
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 37: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
Average Cb/Cr, non-average Y’:
Notes: The first step of subsampling is averaging, so let’s see what happens when we average two values.

## Slide 38: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
Average Cb/Cr, non-average Y’:

## Slide 39: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
Average Cb/Cr, non-average Y’:
After conversion back to RGB:

## Slide 40: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
Average Cb/Cr, non-average Y’:
After conversion back to RGB:
Way too dark!

## Slide 41: What is happening?
Two neighboring pixels:
After conversion to Y’CbCr:
After averaging
Average Cb/Cr, non-average Y’:
After conversion back to RGB:
Way too bright!

## Slide 42: example
444 image
420 image (anchor 1.0)

## Slide 43: example
444 image
420 image (anchor 1.0)
We cannot tell the difference between these two

## Slide 44: example
444 image
420 image (anchor 1.0)
We cannot tell the difference between these two

## Slide 45: example
444 image
420 image (anchor 1.0)
Why not just use one of them, or the average?