## Slide 1: JCTVC-Z0050/JVET-E0137 Update on JCT-VC and JVET 360 Video Activities
17 Jan 2017
Jill Boyce

## Slide 2: JCT-VC
JCTVC-Z0005 AHG Report: Omnidirectional 360° video projection indication (AHG5)
Mandates
  The AHG was established with the following mandates:
  Develop formulae to project samples of an equirectangular format picture to 360°/omnidirectional spherical space.
  Prepare and propose draft text for specification of a code point identification to indicate the use of the equirectangular projection mapping.
  Prepare and propose draft text for an SEI message to carry the projection map type indicator.
Input contribution JCTVC-Z0036: AhG5: Suggested draft text for omni-directional projection indication SEI message with equirectangular projection
  Updated in JCTVC-Z0051 (to be uploaded), based on meeting decisions
6 additional related contributions

## Slide 3: Draft SEI message syntax
omnidirectional_projection_indication( payloadSize ) { | Descriptor
omnidirectional_projection_indication_cancel_flag | u(1)
if( ! omnidirectional_projection_indication_cancel_flag) { | 
geometry_type | u(6)
sub_geometry_flag | u(1)
projection_type | u(8)
if (geometry_type = = 1 && sub_geometry_flag == 1 && projection_type = = 1) { | 
yaw_center | i(16)
pitch_center | i(16)
roll_center | i(16)
yaw_range | u(16)
pitch_range | u(16)
} | 
omnidirectional_projection_information_persistence_flag | u(1)
} | 
} | 
Angle granularity of 0.01 degrees
Yaw in [-180, 180)
Pitch, roll in [-90, 90]

## Slide 4: Equations
min = (yaw_center – yaw_range ÷ 2) * 0.01 * π ÷ 180 [Eq. X1]
max = (yaw_center + yaw_range ÷ 2 + 1) * 0.01 * π ÷ 180 [Eq. X2]
min = (pitch_center – pitch_range ÷ 2) * 0.01 * π ÷ 180 [Eq. X3]
max = (pitch_center + pitch_range ÷ 2 + 1) * 0.01 * π ÷ 180 [Eq. X4]
 = ( ( i′ + 0.5 ) * (max – min) ÷ (croppedWidthY − 0.5 ) + min [Eq. X5]
= − ( ( j′ + 0.5 ) * (max – min) ÷ croppedHeightY − 0.5 ) + min [Eq. X6]
where
i′ = i − SubWidthC * conf_win_left_offset [Eq. X7]
j′ = j − SubHeightC * conf_win_top_offset [Eq. X8]
Angle granularity of 0.01 degrees
Yaw in [-180, 180)
Pitch, roll in [-90, 90]

## Slide 5: JVET
JVET-E0008: AHG Report: 360 video coding tools and test conditions (AHG8)
Mandates
  Study the effect on compression of different projections formats, resolutions, and layouts of the input 360 video.
  Discuss refinements of common test conditions, test sequences, and evaluation criteria.
  Generate anchors and a reporting template for the common test conditions.
  Study viewpoint generation methods and evaluation criteria, and viewport-dependent video coding and streaming.
  Study coding tools dedicated to 360 video, and their impact on compression

## Slide 6: 360Lib Software
JVET-E0009: AHG Report on 360 video conversion software development
JVET-E0084: AHG8: Algorithm description of projection format conversion in 360Lib
360Lib is software toolkit
  Pre-/post-process to HM and JEM
  https://jvet.hhi.fraunhofer.de/svn/svn_360Lib/
  Can run in standalone mode or integrated with codec
Performs projection mappings and conversions, through spherical 3D representation
  Multiple projection formats and layouts included
  Low barrier for inclusion in the toolkit software
Performs multiple objective metric calculations
Can generate rectilinear viewports (static or dynamic)

## Slide 7: JVET AHG8 related contributions
20 contributions related to 360 video, in categories
    Testing procedures and metrics
    Conversion Software
    Projection Formats
    Coding tools
    Rotation
Contributions use test conditions set in JVET-D1030, Chengdu output document
  Included many objective metrics, computed at various locations
  Primary goal was to set conditions for coding tool evaluation

## Slide 8: AHG Recommendations
Refine the 360 video test conditions in an output document, and particularly to consider if the number of objective metrics can be reduced from those defined in JVET-D1030
Consider if the set of test sequences should be modified from those defined in JVET-D1030
Discuss viewport-based streaming evaluation criteria
Identify initial 360 video subjective testing methodology
Discuss potential CfE test conditions for 360 video
Review coding tool and projection formats contributions

## Slide 9: Projection format coding results
Document | Projection | WS_PSNR End-to-End |  | 
 |  | Y | U | V
Part of 360Lib SW |  |  |  | 
JVET-D1030 | CMP | -1.7% | -1.5% | -1.6%
JVET-D1030 | EAP | 8.4% | -2.9% | -3.8%
JVET-D1030 | OHP1 | 4.5% | 10.4% | 10.5%
JVET-D1030 | ISP1 | -1.3% | 1.8% | 1.6%
JVET-D1030 | OHP2 | 4.7% | 14.0% | 13.8%
JVET-D1030 | SSP Hor | -7.7% | -3.6% | -4.3%
Document | Projection | WS_PSNR End-to-End |  | 
 |  | Y | U | V
JVET-E proposals |  |  |  | 
JVET-E0025 | SSP Vert | -7.5% | -3.6% | -4.1%
JVET-E0029 | ISP New | -4.2% | -1.2% | -1.6%
JVET-E0056 | OHP New | 0.8% | 4.1% | 3.4%
JVET-E0057 | CMP New | NA | NA | NA
JVET-E0090 | ERP nested | -4.8% | -3.3% | -4.3%

## Slide 10: Observations
Significant variation in objective metric calculations, per sequence, per metric, per projection format
WS-PSNR (E2E) seems to be the single best metric from JVET-D1030, as it is the only one that computes E2E
  Additional E2E metrics recommended to be added to CTC for next meeting
Reduction in PSNR due to projection conversion doesn’t seem correlated to reduction in PSNR due to coding
No subjective testing has been done
  Particular concern about subjective quality of discontinuous edges
    Would be masked by average PSNR values
  Further study highly encouraged

## Slide 11: BoG on 360 video test conditions
BoG recommendations reported in JVET-E0135
  Add 3 new E2E objective metrics (CPP-PSNR, S-PSNR-I, S-PSNR-NN)
  Replace 2 sequences top/bottom 30 degree blended content
  Dynamic viewport generation: slow linear diagonal motion
Suggested mandates for AHG
  Encourage study of the current and other proposed test sequences, including viewing on HMDs at various coded bitrates
  Encourage study of subjective testing with different display devices including HMDs and make reports
  Study different viewport sizes, including those with larger horizontal than vertical FOV.