## Slide 1: Model-based Intra Coding for Depth Maps using a Depth Lookup Table
Fabian Jäger JCT2-A0010 Stockholm, Sweden

## Slide 2: General Coding Concept
Simple Signal requires Simple Coding

## Slide 3: General Coding Concept
INTRA Block
HTM INTRA Coding
DMC INTRA Coding
DMC_enable_flag
PredMode=INTRA
Prediction
Residual Coding

## Slide 4: DMC Prediction Modes
DC
Gradient
Edge
Texture
Reduced set of available modes sufficient to approximate depth map characteristics
Current prediction mode is predicted from neighboring block
Signaling of Edge mode different than DMM
Texture mode allows for 2 or 3 segments
Similar to DMM
4 Prediction Modes:

## Slide 5: Depth Lookup Table
Not the full range of available depth values is used
 Lookup Table for Depth
Example: Balloons

## Slide 6: DMC Residual Coding
Residuals for each segment are coded as DC offsets only (pixel domain)
No transform & quantization  no ringing
Depth Lookup Table (DLT) can be used to reduce residual bit depth
  Analysis of original depth sequence to generate DLT
  DLT is coded in SPS/APS
  Residual values are coded as indices into DLT

## Slide 7: DMC Simulation Results – ALL INTRA
Depth BD-Rate: Depth Bitrate VS. Synthesis PSNR
Total BD-Rate: Total Bitrate VS. Synthesis PSNR

## Slide 8: DMC Simulation Results – RANDOM ACCESS
Depth BD-Rate: Depth Bitrate VS. Synthesis PSNR
Total BD-Rate: Total Bitrate VS. Synthesis PSNR

## Slide 9: Summary and Recommendations
Proposed DMC Method yields significant BD-Rate savings
  for Depth Rate (AI: 24% / RA: 4%)
  for Total Rate (AI: 1.5% / RA: 0.75%)
Similar complexity as reference (decoder may be less complex)
DMC Residual Coding could be combined with DMM
Recommendation: Continue investigation of DMC in Core Experiment on Depth Intra Coding