## Slide 1: “3D-CE5.h related: Simplification of depth-based inter-view prediction”
Document: JCT2-A0013 (MPEG doc. M25842)
July 2012, Stockholm, Sweden
Tadashi Uchiumi, Tomohiro Ikai, Yoshiya Yamamoto
Sharp Corporation

## Slide 2: Summary
Simplify the disparity vector generation method using predicted depth map (PDM)
  Replace whole samples with Fixed four samples regardless of PU size
  No coding loss in average (anchor is HTM3.1)
Related to depth-based inter-view prediction (CE5.h related)
JCT2-A0013

## Slide 3: Introduction
In the current HTM, max disparity is decided from whole samples in the PDM
The latency of motion derivation process should be as fast as possible
We propose to use minimum fixed sample to decide max disparity
JCT2-A0013

## Slide 4: Proposal
Fixed four samples (on the corner) in a PDM block are used regardless of PU size
(a) HTM3.1
(b) Proposed
PDM
Pixels used for the calculation
Fig. 1
JCT2-A0013

## Slide 5: Proposal (continues)
Reduce comparing steps
Depth 16x16
Fig. 2
32x32 PU
64x64 PU
16x16 PU
256 → 4
64 → 4
16 → 4
Depth 8x8
Depth 4x4
JCT2-A0013

## Slide 6: Proposal (continues)
Remove a double loop and enable very clear description in WD
maxDepth = predDepthMap [x0][y0]
if (maxDepth < predDepthMap [x0+w-1][y0] ) maxDepth = predDepthMap [x0+w-1][y0]
if (maxDepth < predDepthMap [x0][y0+h-1] ) maxDepth = predDepthMap [x0][y0+h-1]
if (maxDepth < predDepthMap [x0+w-1][y0+h-1] ) maxDepth = predDepthMap [x0+w-1][y0+h-1]
The calculating steps are as follows:
where (x0, y0) specify the top-left sample of the PDM block, and w, h specify width and height of the PDM block.
JCT2-A0013

## Slide 7: Simulation Results
Overall average bdrate is the same as the anchor
JCT2-A0013
Table 1: Rate-distortion results on 3-view coding with depth
Sequences | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | -0.2% | 0.1% | 0.0% | -0.1% | -0.1%
Kendo | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
Newspapercc | 0.0% | -0.2% | 0.1% | 0.0% | 0.0% | 0.0%
GhostTownFly | 0.0% | -0.3% | -0.2% | -0.1% | -0.1% | -0.1%
PoznanHall2 | 0.0% | -0.4% | -0.2% | -0.1% | 0.0% | 0.0%
PoznanStreet | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0%
UndoDancer | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 0.0%
1024x768 | 0.0% | -0.1% | 0.1% | 0.0% | 0.0% | 0.0%
1920x1088 | 0.0% | -0.2% | -0.1% | -0.1% | 0.0% | 0.0%
average | 0.0% | -0.2% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 8: Simulation Results (continues)
Run times are almost the same as the anchor
JCT2-A0013
Sequences | enc time | dec time | ren time
Balloons | 100.5% | 99.5% | 100.3%
Kendo | 101.1% | 97.0% | 100.6%
Newspapercc | 101.4% | 98.2% | 100.8%
GhostTownFly | 99.3% | 99.9% | 98.4%
PoznanHall2 | 98.4% | 98.1% | 101.0%
PoznanStreet | 99.4% | 96.3% | 101.5%
UndoDancer | 98.1% | 100.0% | 100.3%
1024x768 | 101.0% | 98.2% | 100.6%
1920x1088 | 99.8% | 98.5% | 100.3%
average | 99.7% | 98.4% | 100.4%
Table 2: Running time ratio

## Slide 9: Additional tests (information)
Table 3: Simulation results with average disparity (not part of this proposal)
Average value instead of Max value from the same four samples is also investigated
Worse than using max value (=> Max value is better)
Sequences | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.0% | -0.6% | 1.4% | 0.2% | 0.0% | 0.1% | 106.2% | 98.8% | 99.0%
Kendo | 0.0% | -0.3% | 1.4% | 0.2% | 0.1% | 0.1% | 104.4% | 98.0% | 100.2%
Newspapercc | 0.0% | 0.0% | 0.8% | 0.2% | 0.0% | 0.0% | 105.1% | 97.5% | 100.5%
GhostTownFly | 0.0% | -0.5% | 0.6% | 0.0% | 0.0% | 0.0% | 97.8% | 101.2% | 99.7%
PoznanHall2 | 0.0% | -1.1% | 1.4% | 0.1% | 0.1% | 0.1% | 98.9% | 96.6% | 102.3%
PoznanStreet | 0.0% | -0.1% | 0.5% | 0.1% | 0.1% | 0.1% | 98.8% | 96.9% | 102.5%
UndoDancer | 0.0% | 0.3% | 0.6% | 0.1% | 0.1% | 0.1% | 98.0% | 96.0% | 100.8%
1024x768 | 0.0% | -0.3% | 1.2% | 0.2% | 0.0% | 0.1% | 105.2% | 98.1% | 99.9%
1920x1088 | 0.0% | -0.3% | 0.8% | 0.1% | 0.1% | 0.1% | 98.4% | 97.6% | 101.3%
average | 0.0% | -0.3% | 1.0% | 0.1% | 0.0% | 0.1% | 101.3% | 97.8% | 100.7%
JCT2-A0013

## Slide 10: Conclusions
Fixed samples in predicted depth map (PDM) for disparity vector generation is proposed
Reduce motion parameter derivation complexity without coding loss
In addition, WD description can be more clarified due to loop operations has been eliminated
The proposed method should be considered to be adopted in the new HTM for further evaluation
JCT2-A0013
Cross-checked by Samsung in JCT2-A0080. Thank you very much