## Slide 1: “3D-CE5.h related: Simplification of AMVP”
Yoshiya Yamamoto, Tadashi Uchiumi, Tomohiro Ikai
Sharp Corporation
Document: JCT2-A0014 (MPEG doc. M25843)
July 2012, Stockholm, Sweden

## Slide 2: Summary
Simplify the inter-view motion candidate derivation process for AMVP
  Decouple of inter-view candidate derivation and common AMVP candidate derivation
  No coding loss (anchor is HTM3.1)
JCT2-A0014

## Slide 3: Problem 1 in HTM3.1
Inter-view candidate
Spatial left candidate
Spatial top candidate
Temporal candidate
Zero candidate
Non base-view
derivation process
mvp_lX_idx = 0?
Inter-view candidate is available?
:pruning
Inter-view candidate derivation is always needed (light blue line)
JCT2-A0014
pruning check with inter-view candidate is a problem
yes
yes

## Slide 4: Problem 2 in HTM3.1
Inter-view candidate
Spatial left candidate
Spatial top candidate
Temporal candidate
Zero candidate
mvp_lX_idx = 0?
Inter-view candidate is available?
Even if pruning is removed, availability check of inter-view candidate is always needed (light blue line) and all candidate derivations are needed in the worst case (blue line)
JCT2-A0014
availability check of
Inter-view candidate
yes
yes
Non-available case for the inter-view candidate is a problem

## Slide 5: Problem 2(Detail) in HTM3.1
JCT2-A0014
Non-available case for the inter-view candidate is a problem
mvp_lX_idx | Available | Non-available
0 | Inter-view candidate | Special left candidate
1 | Special left candidate | Special top candidate
2 | Special top candidate | Temporal candidate
All candidate depends on the availability of the first candidate
Availability check of inter-view candidate is always needed

## Slide 6: Description problem in HTM3.1
The derivation process is different between Non-base view and Base-view. It means we needs some additional descriptions.
JCT2-A0014
Non-base view?
Inter-view candidate
Spatial left candidate
Spatial top candidate
Temporal candidate
Zero candidate
Spatial left candidate
Spatial top candidate
Temporal candidate
Zero candidate
Non base-view
derivation process
Base-view
Derivation process
mvp_lX_idx = 0?
Inter-view candidate is available?
yes
yes
yes

## Slide 7: Proposal
Remove the pruning process with inter-view candidate and use the same pruning process as the base-view
Use zero-candidate in case inter-view candidate is not available
Non-base view?
Inter-view candidate
Spatial left candidate
Spatial top candidate
Temporal candidate
Zero candidate
Zero candidate
Non base-view
extension
Base-view
Derivation process
(HM6.1)
Inter-view candidate is available?
mvp_lX_idx = 0?
yes
yes
yes

## Slide 8
JCT2-A0014
mvp_lX_idx | Available | Non-available
0 | Inter-view candidate | Special left candidate
1 | Special left candidate | Special top candidate
2 | Special top candidate | Temporal candidate
Inter-view candidate and other candidates are independent
Derivation of inter-view candidate or Availability check of inter-view candidate is Not needed (if mvp_lX_idx > 0)

## Slide 9: Benefit
Reduce derivation process complexity
  Inter-view candidate derivation process or the availability check process can be skipped
  Remove the worst case, which can occur in case inter-view candidate is not available
Minimize special process for non-base view pictures
  Most of the process are the same as base-view process(green part)
  Only add the inter-view candidate process into WD(yellow part)
JCT2-A0014
Inter-view candidate
Spatial left candidate
Spatial top candidate
Temporal candidate
Zero candidate
Zero candidate
Non base-view
extension
Base-view
process(as HM6.1)

## Slide 10: Simulation Results
Rate-distortion results on 3-view coding with depth
No coding loss
Run times are almost the same
Sequences | video 0 | video 1 | video 2 | video only | synthesized only | Encoding time | Decoding time
Balloons | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% | 99.9% | 100.2%
Kendo | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | 100.4% | 99.6%
Newspapercc | 0.0% | -0.1% | -0.1% | 0.0% | 0.1% | 100.9% | 100.5%
GhostTownFly | 0.0% | -0.1% | 0.2% | 0.0% | 0.0% | 99.9% | 100.3%
PoznanHall2 | 0.0% | -0.2% | -0.5% | -0.1% | 0.0% | 100.0% | 99.4%
PoznanStreet | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 100.8% | 99.5%
UndoDancer | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 99.5% | 99.4%
1024x768 | 0.0% | -0.1% | 0.0% | 0.0% | 0.1% | 100.4% | 100.1%
1920x1088 | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 100.0% | 99.7%
average | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 100.2% | 99.9%
JCT2-A0014

## Slide 11: Conclusions
Decouple of inter-view candidate derivation and normal AMVP candidate derivation
  Remove the pruning process with inter-view candidate and use the same pruning process as the base-view
  Use zero-candidate in case inter-view candidate is not available
Experiment results
  No coding loss
The proposed method should be considered to be adopted in the new HTM for further evaluation
JCT2-A0014
Cross-checked by Sony in JCT2-A0143. Thank you very much