## Slide 1: Depth Quadtree Prediction for HTM
JCT2-A044, Stockholm, July 2012
Joel Jung, Kartik Viswanathan – Orange Labs

## Slide 2: Introduction
  Current runtime of HTM3.1 is huge:
  Example – Kendo QP25 (1024x768) – Coding of Texture and Depth
  HM7.0 3h38 (43.4s per frame)
  HTM3.1 23h14 (280s per frame)
  Runtime for depth process represents the major part:
  Example – Kendo QP25 (1024x768) – Coding of Texture and Depth
  HTM3.1 texture: 4h40 (56s per frame)
  depth: 18h35 (224s per frame)
  It can be observed that “often” a given texture CU is more partitioned than its collocated depth CU
  In HTM3.1 QT for depth and texture are computed independently

## Slide 3: Proposed Method
  Proposed method includes 2 parts:
  1- Depth QT limitation
  The QT of the depth is linked to the QT of the collocated CTU QT in the texture
  2- Predictive depth QT coding
  The QT of the depth is predictively encoded relatively to the QT of the texture

## Slide 4: Depth QT Limitation
  Rule:
  - A given CU of the depth cannot be split more than its collocated CU in the texture.
  - During depth encoding, the partitioning is stopped when it reaches the partitioning of the texture, for a given CU.
Texture
Depth
Depth
allowed
partitioning
forbidden
partitioning
Saves encoder runtime for depth computing
Saves a few bits for QT signaling
Example:

## Slide 5: Predictive Depth QT Encoding
Texture | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Depth | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | 1 | 0 | 0 | 0 | 0
The basic idea is to send nothing if the CU of the texture is not further split, and send one bit to indicate if depth is split or not when the current partition of the texture is further split.
Texture
Depth
Texture | Depth | Residual Depth
1 | 1 | 1
0 | 0 | -
1 | 0 | 0
  Encoding
  Rule:
Residual Depth | 1 | 1 |  |  | 1 |  |  |  | 0 |  |  | 0 |  |  |  |  | 1 |  |  |  | 
Saves bits for QT signaling
(6 bits)
(17 bits)

## Slide 6: Predictive Depth QT Decoding
Texture | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Residual Depth | 1 | 1 |  |  | 1 |  |  |  | 0 |  |  | 0 | 1 |  |  |  | 1 |  |  |  | 
Texture
Texture | Residual Depth | Decoded depth
1 | 1 | 1
0 | * | 0
1 | 0 | 0
  Decoding
  Rule:
Decoded Depth | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |  |  |  | 1 | 0 | 0 | 0 | 0
The basic idea is that when the texture is split (1), the residual depth is read to know if it is split too, or not.

## Slide 7: Experimental Results
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Poznan_Hall2 | 0,0% | 0,0% | 0,0% | 0,0% | -0,8% | -1,6% | 58,2% | 107,4% | 98,5%
Poznan_Street | 0,0% | 0,0% | 0,0% | 0,0% | -0,5% | -0,8% | 67,3% | 101,0% | 102,7%
Dancer | 0,0% | 0,0% | 0,0% | 0,0% | -1,0% | -1,2% | 60,4% | 84,8% | 89,6%
GhostTownFly | 0,0% | 0,0% | 0,0% | 0,0% | -0,7% | -1,1% | 58,1% | 87,3% | 94,8%
Kendo | 0,0% | 0,0% | 0,0% | 0,0% | -0,2% | -0,7% | 59,9% | 105,7% | 121,3%
Balloons | 0,0% | 0,0% | 0,0% | 0,0% | 0,1% | -0,6% | 60,4% | 101,4% | 102,0%
Newspaper | 0,0% | 0,0% | 0,0% | 0,0% | 0,1% | -0,9% | 58,1% | 99,1% | 100,1%
1024x768 | 0,0% | 0,0% | 0,0% | 0,0% | 0,0% | -0,7% | 61,8% | 97,2% | 95,8%
1920x1088 | 0,0% | 0,0% | 0,0% | 0,0% | -0,8% | -1,1% | 59,1% | 98,1% | 104,1%
Average | 0,0% | 0,0% | 0,0% | 0,0% | -0,5% | -1,0% | 60,3% | 97,7% | 103,3%
CTC, HTM3.1,
The method is disabled on Intra slices.
(negative values are gains)
 | video 0 | video 1 | video only | synthesized only | coded & synthesized
Poznan_Hall2 | 0,0% | 0,0% | 0,0% | -0,4% | -1,3%
Poznan_Street | 0,0% | 0,0% | 0,0% | -0,4% | -0,6%
Dancer | 0,0% | 0,0% | 0,0% | -0,7% | -0,9%
GhostTownFly | 0,0% | 0,0% | 0,0% | -0,5% | -0,8%
Kendo | 0,0% | 0,0% | 0,0% | -0,1% | -0,7%
Balloons | 0,0% | 0,0% | 0,0% | 0,3% | -0,5%
Newspaper | 0,0% | 0,0% | 0,0% | 0,6% | -0,6%
1024x768 | 0,0% | 0,0% | 0,0% | 0,3% | -0,6%
1920x1088 | 0,0% | 0,0% | 0,0% | -0,5% | -0,9%
Average | 0,0% | 0,0% | 0,0% | -0,1% | -0,8%
3 views test case
2 views test case

## Slide 8: Analysis: Where do the gains come from?
CTB |  | Texture | 
 |  | Homogeneous 64x64 | Textured/Edge 8x8
Depth | Homogeneous 64x64 | Runtime savings (frequent) | No impact (frequent)
 | Textured/Edge 8x8 | Quality Loss + Bits savings (not a frequent case) | Bits savings for Depth QT
  - Most of the time is spent in the encoding of the depth
  - Savings relatively to the respective partitioning of Texture and Depth:
  - Method can smooth wrong depths edges (ex: Kendo)

## Slide 9: Conclusion
A modification of the depth quadtree decoding process is proposed.
For a given CTU, the quadtree of the depth is linked to the collocated CTU quadtree in the texture, so that a given CU of the depth cannot be split more than its collocated CU in the texture.
The quadtree of the depth is predictively encoded.
60% encoder runtime is achieved compared to the reference with BDR gains of 0.5% for synthetized only.
and 1.0% for coded + synthesized.
Propose this method for adoption in the HTM and in the WD.
Thanks to MediaTek for the cross-check
(JCT2-A0159)