## Slide 1: M26016/JCT2-A0073 proposal of depth-aware 3DV test condition and evaluation
July 14, 2012
Takanori Senoh, et al. (NICT)
Masayuki tanimoto, et al.(NISRI)

## Slide 2
Introduction
3DV coding:
originally: for FTV and 3D Images
currently: focused on auto-stereoscopic TVs
1
2
3
4
5
6
7
8
3D image capturing system
with multiple cameras
Object
Auto-stereoscopic
3D display
View changes depending on eye position
Pixel
Lenticular
lens
ISO/MPEG/MVC
test sequence
Forget something?

## Slide 3
Introduction
3DV coding: should pay attention not only to auto-stereoscopic TVs,
but also FTVs and other emerging 3D Images.
Free Viewpoint
Light Field display
Aerial 3D display
Holography
Volume scanning display

## Slide 4
Free View-point TV (FTV)
FTV enables: viewing point forward and backward, not only lateral.
If depth maps are distorted, FTV will be corrupted.
Free viewpoint walk through from [2] A. Ishikawa
Walk through image

## Slide 5
Light Field display
Light field display: displays 3D object on a rotating screen.
if depth maps are distorted, 3D object will be distorted.
Rotating mirror
3D image
FTV from [3] A. Jones
projector

## Slide 6
Volume scanning display
Volume scanning display: displays 3D object by scanning slices of 3d objects.
if depth maps are distorted, 3D object will be distorted.
Micro mirror array optics
screen
lens
Galvanometer
Mirror scanner
Volume scanning display from [4] D. Miyazaki

## Slide 7
Aerial 3D display
Aerial 3D display: displays 3D image in the air or water.
if depth maps are distorted, 3D images will be distorted.
principle
3D image
application
Aerial 3D display from [5] H. Watanabe

## Slide 8
Holographic 3D inmage
Holographic images: are generated from depth map.
if depth maps are distorted, 3D images will be distorted
prism
3D image
Display system
Depth map  Hologram
Holographic 3D image from [6] T. Senoh

## Slide 9
problem of current depth coding
QP values for depth map: are too high, especially for HEVC-based test condition.
Coded depth map quality: is bad. It cannot be used for other applications.
QPV0 | 51 | 50 | 49 | 48 | 47 | 46 | 45 | 44 | 43 | 42 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 34 | 33 | 32 | 31 | 30 | 29 | 28 | 27 | 26 | 25
QPD0 | 51 | 50 | 50 | 50 | 50 | 49 | 48 | 47 | 47 | 46 | 45 | 45 | 44 | 44 | 43 | 43 | 42 | 42 | 41 | 41 | 40 | 39 | 38 | 37 | 36 | 35 | 34
QPs for HECV-based test condition
Decoded depth map: QP=34(highest rate), 35dB/231Kbps

## Slide 10
Proposed Common test condition
The same QP values: should be used between view and depth.
If low bit rate for depth map is required: sub-sampling is a good candidate.
Decoded depth map: QP=35(2nd low rate), 51dB/144Kbps
Sub-sampling
1/2
1/2
QPV0 | 50 | 45 | 40 | 35 | 30 | 25
QPD0 | 50 | 45 | 40 | 35 | 30 | 25
Use same QP

## Slide 11
CE evaluation chart
Current chart: has no depth coding summary.
PSNR and bit rate evaluation for depth maps: should be added to the summary.
CE evaluation summary
Add depth column
Current:
proposed: