## Slide 1: JCT2-A0090 / M26046 Independent intra-period coding in 3D-HTM
July 2012, Stockholm
Jakub Siast Krzysztof Wegner, Olgierd Stankiewicz Marek Domański
Chair of Multimedia Telecommunications and Microelectronics Poznań University of Technology, Poland

## Slide 2: Introduction
Enhancement of experimentation.
Some interesting benefits
  parallel intra-periods coding
  fast debugging functionality
No normative change to the future standard is imposed
A proposal of 3D-HTM encoder software modification

## Slide 3: Independent IntraPeriod encoding
Allow parallelization of 3D sequence encoding by splitting into multiple runs, each for different IntraPeriod
  Each IntraPeriod would be encoded independently (in parallel)
  The resultant bitstreams would be merged into a single concatenated bitstream
  The concatenated bitstream should be binary identical to the one produced with a single-pass of the encoder (without parallelization).

## Slide 4: Single-pass versus proposed parallel IntraPeriod encoding

## Slide 5: Independent IntraPeriod encoding
Provide an approach for verification of deterministic operation of the encoder
  If after future integration of some new tool, there is a mismatch between single-pass encoding and parallel encoding, there might be an issue with deterministic operation of the software

## Slide 6: Independent IntraPeriod encoding
Allow stand-alone encoding of a selected IntraPeriod for debugging
  Currently, if an error occurs in e.g. 249th frame, the whole sequence has to be traced in order to find an exact location of the bug in the source code
  More feasible way would be to encode only the last IntraPeriod in which the error occurs
Such idea has been successfully implemented and exploited in Poznan University of Technology proposal for the CfP

## Slide 7: Implementation
Necessary modification of the encoder software
  Allow encoding of the selected IntraPeriod only
  Each IntraPeriod must be independent from others in encoding

## Slide 8: Implementation
Independent encoding of IntraPeriods
  In 3D-HTM it is true in general with two exceptions:
3D-HTM uses open-GOP encoding structure in which CDR frames (Clean Decoder Refresh) are used for prediction that breaks IntraPeriod boundaries
Context derivation of "cabac_init_flag" [1] in the slice header

## Slide 9: CDR frames
All IDR/CDR that are used as a source for prediction inside selected IntraPeriod must be encoded during selected IntraPeriod encoding

## Slide 10: "cabac_init_flag"
A flag in slice header of P/B frames.
Tells decoder which data to use as a initial setting for cabac.
Can be used by the encoder to attain better entropy coding.
In the reference software, this flag is derived basing on previously encoded frames.
This has no impact on decoding though, because this flag is explicitly singnalled in the bitstream in a non-context-aware manner.

## Slide 11: "cabac_init_flag” in 2D-HEVC
"cabac_init_flag" is cleared at the beginning of each IntraPeriod (with I frame) and thus there is no problem with intra-periods dependences in encoding.

## Slide 12: "cabac_init_flag” in 3D-HTM
No I frames in dependent views

## Slide 13: Proposal
Currently, each I frame reset the context only of a its view which causes the problem.
We propose to reset the context of "cabac_init_flag" across IntraPeriod boundaries in all views.
It can be solved simply by extending "cabac_init_flag" flag context reset to all views.
This would have minor impact of encoding efficiency, while fulfilling requirement of IntraPeriods independency.

## Slide 14: Summary
Proposed encoder modification involves no normative change to the future standard.
Independent intra-period coding eases debugging and parallel computing.
We recommend to:
  Fix the bug with "cabac_init_flag" context prediction across IntraPeriod boundaries.
  Adopt independent intra-period coding in 3D-HTM.
Poznan University of Technology does not have current or pending patent rights related to the technology described in this contribution