## Slide 1
On NAL Unit Header and Video Parameter Set Design
Byeongdoo Choi, Jaehyun Kim, Jeonghoon Park
Samsung Electronics Co., Ltd
July, 2012
Notes: <number>

## Slide 2: Motivation
NAL unit header
  MVC/SVC : base (1 byte), non-base (4 bytes) -> variable
    Extended 3 byte : view ID, priority ID, temporal ID, dependency ID, quality ID are present
  HEVC-extension : 2 bytes -> fixed
    Reserved 5 bits for 3D/scalability extension
  Needs on flexible design of NAL unit header
  for signaling scalability information
<number>

## Slide 3: Proposals
Signaling most of useful scalability information in NAL unit header
  In order that Network Elements get the important scalability information only by parsing NAL unit header for bitstream management
    Scalability extension type, Layer identifiers
  No need to parse any parameter set in system level
  Conforming to the VPS design.
<number>

## Slide 4: NAL unit design
Current NAL unit header of HEVC
<number>
F: forbidden_zero_bit
NRF: nal_ref_flag
NUT: nal_unit_type
TID : temporal_id
R5 : reserved_one_5bits

## Slide 5: Concept
<number>
Other NAL units :
VPS NAL unit :
Proposed NAL unit header
Proposed NAL unit header

## Slide 6: Proposed NAL unit design
Proposed NAL unit header for scalable/3D extension in VPS NAL unit
<number>
SET : scalable_extension_type specifies the type of scalability currently used, and how to map the layer_id into several scalability identifiers, e.g. dependency_id, quality_id, view_id, temporal_id, priority_id and so on.
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
F
NRF
NUT
SET
TID

## Slide 7: Proposed NAL unit design
Proposed NAL unit header for scalable/3D extension in other units
<number>
LID : layer_id specifies the layer identifier, which can be mapped into the dependency_id, quality_id, view_id, temporal_id, priority_id and so on.
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
F
NRF
NUT
LID
TID

## Slide 8: Mapping method of layer_id #1
<number>
Direct mapping into scalability ID by splitting sub-layer IDs
  The layer_id (5/6bits) can be split into two or three sub_layer_id,
  and each sub_layer_id can be mapped into a specific identifier.
scalability_extension_type (5bits) | layer_id (5bits) |  | 
0 | forbidden |  | 
1 | depth_flag (1bit) | view_id (4bits) | 
2 | dependency_id (2bits) |  | quality_id (3bits)
3….31 | reserved |  | 

## Slide 9: Syntax for the proposed NAL unit header
<number>
scalability_extension_type indicates the scalability types of all layers associated with the current video_parameter_set. The value of scalable_extension_type specifies the mapping rule of the layer_id in the NAL unit headers of the following NAL units into scalability identifiers.
layer_id_plus1 minus 1 indicates the layer identification.

## Slide 10: Proposals
Conforming to VPS design
  The information of the video coding standards for hybrid 3D codec (AVC + HEVC) is signaled
<number>

## Slide 11: VPS syntax for multi-standards scalability
<number>

## Slide 12: Conclusion
Suggestion #1
  Fix the reserved 5 bits (or 6 bits) in NAL unit header to the generic layer_id in non-VPS NAL units. In VPS NAL unit headers, the reserved bits will be used in a different purpose.
Suggestion #2
  At most, all scalability identifiers can be obtained by parsing only NAL unit headers.
Suggestion #3
  For easy manipulation of all heterogeneous view streams (e.g. base: AVC, non-base: HEVC), non-HEVC bitstreams are encapsulated by HEVC NAL unit header in multi-standard 3D.
<number>

## Slide 13
Thank you !
<number>