## Slide 1
On Random Access Pictures
(A0117)
Byeongdoo Choi, Jaehyun Kim, Jeonghoon Park
Samsung Electronics Co., Ltd
July, 2012
Notes: <number>

## Slide 2: Motivation
Without restrictions on the use of RAP-related pictures, the decoding error, over-/under-flow in HRD, or the POC mismatch may occur. To avoid unintended operation in decoder, several restrictions on CRA, BLA, and TFD are proposed.
  Restriction on RAP pictures
  Restriction on TFD pictures
  Restriction on Temporal layer
<number>

## Slide 3: Proposal #1
The NAL unit/picture type of the enhancement (non-base) view picture shall be BLA, when the NAL unit/picture type of the associated base view picture is BLA.
The NAL unit/picture type of the enhancement view picture shall be CRA, when the NAL unit/picture type of the associated base view picture is CRA.
The NAL unit/picture type of the enhancement (non-base) view picture shall not be CRA, when the NAL unit/picture type of the associated base view picture is BLA.
<number>

## Slide 4: Reason #1
The leading (TFD) pictures associated with the CRA picture in the enhancement view cannot reference the TFD pictures associated with the BLA picture in the base view after the system discards the TFD pictures associated with the BLA pictures.
<number>
I
TFD
TFD
I
TFD
TFD
TFD
BLA
TFD
CRA
Enhancement
View
Base
View

## Slide 5: Reason #2
The leading (TFD) pictures associated with the CRA picture in the enhancement view cannot reference the TFD pictures associated with the BLA picture in the base view after the system discards the TFD pictures associated with the BLA pictures.
<number>
I
I
CRA
BLA
Enhancement
View
Base
View
POC MSB : 128
POC LSB : 16
POC MSB : 0
POC LSB : 17
POC MSB : 0
POC LSB : 18
POC MSB : 0
POC LSB : 19
POC MSB : 0
POC LSB : 20
POC MSB : 128
POC LSB : 16
POC MSB : 128
POC LSB : 17
POC MSB : 128
POC LSB : 18
POC MSB : 128
POC LSB : 19
POC MSB : 128
POC LSB : 20

## Slide 6: Proposal #2
The NAL unit/picture type of the enhancement view picture shall be TFD, when the NAL unit/picture type of the associated base view picture is the TFD picture type.
Even though the pictures of enhancement views are not the non-decodable leading pictures associated with a CRA or BLA picture, those pictures are marked as the TFD pictures when the picture type of the base view is TFD.
Simultaneously, the associated pictures referencing the TFD pictures in the enhancement view, but not non-decodable leading pictures, shall be marked as the TFD pictures.
<number>

## Slide 7: Reason #1
If the TFD pictures in the base view are discarded, all pictures dependent on the discarded TFD pictures cannot be correctly decoded. Thus, when the TFD pictures are discarded in the base view, all related pictures in the enhancement views should be discarded.
<number>
I
TFD
TFD
I
I
I
B
BLA
P
BLA
Not non-decodable leading pictures, but shall be TFD
Enhancement
View
Base
View

## Slide 8: Proposal #3
The NAL unit/picture type of the enhancement view picture cannot be the non-TLA, when the NAL unit/picture type of the associated base view picture is the TLA.
Whereas, the NAL unit/picture type of the enhancement view picture can be the TLA, when the NAL unit/picture type of the associated base view picture is the normal picture.
<number>

## Slide 9: Reason #1
This restriction is to guarantee that the temporal_id of the enhancement view shall be higher than the temporal_id of the base view in the same access unit, to avoid the error of inter-view prediction.
<number>
I
TLA
I
B
B
I
B
I
Enhancement
View
Base
View
TID : 0
TID : 0
TID : 0
TID : 0
TID : 0
TID : 0
TID : 0
TID : 1
TID :1
TID : 1
Higher temporal layer cannot be decoded

## Slide 10: Conclusion
Proposal #1
  Base : CRA -> non-Base : CRA
  Base : BLA -> non-Base : BLA
Proposal #2
  Base : TFD -> non-Base (including associated pictures) : TFD
Proposal #3
  Base : TLA -> non-Base : TLA
    The temporal_id of enhancement view shall be larger than the temporal_id of the base view in the same access unit.
<number>

## Slide 11
Thank you !
<number>