## Slide 1
On View Layer Switching
(A0118)
Byeongdoo Choi, Jaehyun Kim, Jeonghoon Park
Samsung Electronics Co., Ltd
July, 2012
Notes: <number>

## Slide 2: Motivation
One key feature of multiview video is the interaction which can choose viewpoints of interests freely.
When different viewpoints are sequentially displayed, the decoded views will frequently change to support smooth and fast viewpoint switches.
  A new NAL unit / picture type are proposed
  to support the smooth view layer switching.
<number>

## Slide 3: Problem #1
In general, the IDR unit/picture can support all kinds of layer switching, but its frequent use degrades the coding efficiency.
The CRA also can support the view layer switching. However, the CRA may result in decoding error of frame loss when a view layer switching is performed because the non-decodable leading pictures associated with the CRA picture in the switched view cannot be corrected decoded.
<number>
I
B
B
B
B
B
CRA
B
CRA
Enhancement
View
Base
View
Not decodable
B
B
View layer switching

## Slide 4: Problem #2
Even if a CRA picture in the non-base view is changed to a BLA picture when the view layer switching is performed, the POC misalignment between views occurs and may result in the error of the interview prediction.
<number>
I
B
B
TFD
TFD
B
CRA
TFD
BLA
Enhancement
View
Base
View
Discarded
B
B
View layer switching
POC mismatch

## Slide 5: Problem #3
If all CRA pictures of all view are changed to BLA pictures when the view layer switching is performed, the TFD pictures in the base view will be discarded. This means the sequence is not continuously displayed.
<number>
I
TFD
TFD
TFD
TFD
TFD
BLA
TFD
BLA
Enhancement
View
Base
View
Discarded
B
B
View layer switching

## Slide 6: Solution
View layer access (VLA) picture/NAL unit type is introduced
  VLA is only used in non-base view
  When VLA pictures are present in a non-base view, view layer switching is allowed to that view
  VLA pictures do not reset POC MSB. Instead, the POC MSB is signalled or inferred from the base view.
  Option #1
  Similarly to CRA, non-decodable leading pictures are allowed.
  Non-decodable leading pictures associated with a VLA picture are marked as TFD pictures.
  When the view layer switching is done, the TFD pictures are discarded.
  Option #2
  Similarly to IDR, non-decodable leading pictures are disallowed.
<number>

## Slide 7: Option #1
  Option #1
  Similarly to CRA, non-decodable leading pictures are allowed.
  Non-decodable leading pictures associated with a VLA picture are marked as TFD pictures.
  When the view layer switching is done, the TFD pictures are discarded.
<number>
I
B
B
TFD
TFD
B
I
TFD
VLA
Enhancement
View
Base
View
Discarded
B
B
View layer switching

## Slide 8: Option #2
  Option #2
  Similarly to IDR, non-decodable leading pictures are disallowed.
<number>
I
B
B
B
B
B
I
B
VLA
Enhancement
View
Base
View
B
B
View layer switching
Decodable leading pictures

## Slide 9: Conclusion
For stable and quick view point/layer switching, a new picture type is necessary -> View layer access picture (VLA)
Recommend to adopt
  Option 1 or 2
  Both
<number>

## Slide 10
Thank you !
<number>