## Slide 1: JCT2-A0133 CE5.h related: Reducing the coding cost of merge index by dynamic merge candidate list re-ordering
T. Guionnet (INRIA)
L. Guillo (Irisa/CNRS)
C. Guillemot (INRIA)
July 2012

## Slide 2: Introduction
  HEVC: Merge candidate list
    Order of the candidates carefully designed: Most likely candidates first
  Encoding of the merge index
    Binarization using unary code: most likely candidate gets the shortest codeword
    CABAC in equiprobable mode, except for the first bin
  3D-HTM: inter-view motion prediction
    New candidate added at the beginning of the list
    Inter-view motion predictor generally the most likely,
    But not always: In second or third position for 11% of the images of the CTC test set

## Slide 3: Proposed method
  Keep track of the merge index likelihoods thanks to a histogram
  Update the histogram each time a merge index is decoded/encoded
  Derive a conversion table from the histogram
    Convert from/to actual position in the list to/from encoded index
  Reinitialize the process at the same points as the CABAC
    No data dependancies addition, keeping parallelization possible
    No robustness loss

## Slide 4: Results
 | video 0 | video 1 | video 2 | video only | enc time | dec time
Balloons | 0,0% | 0,0% | 0,0% | 0,0% | 99,5% | 100,8%
Kendo | 0,0% | 0,0% | -0,1% | 0,0% | 101,0% | 101,2%
Newspapercc | 0,0% | 0,1% | -0,1% | 0,0% | 103,1% | 100,0%
GhostTownFly | 0,0% | -0,5% | -0,6% | -0,1% | 107,7% | 100,6%
PoznanHall2 | 0,0% | 0,1% | 0,1% | 0,0% | 107,2% | 99,0%
PoznanStreet | 0,0% | 0,0% | 0,1% | 0,0% | 108,1% | 100,5%
UndoDancer | 0,0% | -0,3% | -0,2% | -0,1% | 106,3% | 101,6%
1024x768 | 0,0% | 0,0% | 0,0% | 0,0% | 101,2% | 100,7%
1920x1088 | 0,0% | -0,2% | -0,1% | 0,0% | 107,3% | 100,4%
average | 0,0% | -0,1% | -0,1% | 0,0% | 104,7% | 100,5%

## Slide 5: Conclusion
  Proposal: improve merge index coding by dynamic re-ordering
  0.1 % gain on average
  Gain can be high, depending on the sequence: up to 0.6% on the CTC test set
  Gain can be even higher locally inside the sequences
  Propose to further study the method in a core experiment

## Slide 6: Thank you