## Slide 1: JCTVC-J0072 AHG9 High-Level Syntax: APS loss detection
Miska M. Hannuksela Nokia Research Center

## Slide 2: Problem Setting
Inability to detect APS loss, usage of wrong APS
  Happens when a lost APS re-used an aps_id value (ID1) that had already been used earlier by another APS
  Consequently, the decoder interprets any reference to the aps_id value ID1 to the previous APS NAL unit using the same aps_id value.
JCTVC-J0072

## Slide 3: Background
JCTVC-I0069: a constraint to the aps_id values that enabled to detect losses of APS NAL units
  Re-proposed in this contribution
  The proposed constraint is analogous to the max POC difference constraint
In Geneva, JCTVC-I0069 received the comments:
  A problem for splicing, as the range in which the APS IDs would fall after the splice point is not under the control of the encoder
  An alternative loss detection suggestion was to send a parameter set checksum in an SEI message
JCTVC-J0072

## Slide 4: Motivation for Re-proposing
The issue with splicing has been solved similarly to what is done for POC, i.e. the aps_id constraint is “reset” at IDR and BLA access units
Proposed aps_id constraint and the parameter set checksum SEI have different strengths
  Proposed aps_id constraint provides a basic level of error resilience without implementation or RD cost
  Parameter set checksum SEI is optional for both encoders and decoders and is helpful only if both ends use the mechanism
  Parameter set checksum SEI may enable detecting parameter set losses quicker than the proposed aps_id constraint
  Decoders may deallocate memory based on parameter set checksum SEI
   the mechanisms complement each other
JCTVC-J0072

## Slide 5: APS Loss Detection
max_aps_id given in SPS: aps_id has the range of 0 to max_aps_id
max_aps_id_diff given in SPS: a range of aps_id values that are considered “used”
  The range is relative to the maximum used aps_id value
  An APS in the “used” range can be retransmitted (for error resilience)
  A new APS must use an aps_id from the “unused” range (usually increment by 1 in modulo arithmetic)
  When maximum used aps_id value is updated, the APSes that fall outside the window of “used aps_id values” are marked as unavailable – hence, no accidental re-use of an APS can happen
0
max_aps_id
Max used aps_id
max_aps_id_diff
”used aps_id values”
”unused”
”unused”
JCTVC-J0072
Constraint: max_aps_id_diff * 2 shall be less than max_aps_id