## Slide 1: JCT3V-B0033 AHG7 3D-AVC: Loss Detection of Depth Parameter Sets
Miska M. Hannuksela Nokia Research Center

## Slide 2: Problem Setting
Inability to detect DPS loss, usage of wrong DPS
  Happens when a lost DPS re-used an dps_id value (ID1) that had already been used earlier by another DPS
  Consequently, the decoder interprets any reference to the dps_id value ID1 to the previous DPS NAL unit using the same dps_id value.
JCT3V-B0033
DPS01
VCL
DPS02
VCL
...
DPS01
VCL
No losses:
DPS01
VCL
DPS02
VCL
...
DPS01
VCL
Loss:
Decoder refers to wrong DPS without detecting the loss

## Slide 3: Depth Parameter Set in 3D-AVC Draft 3
Carries depth range and VSP parameters (focal length etc.)
depth_parameter_set_id equal to 0 used for the parameters carried in the SPS
depth_parameter_set_id greater than 0 used in depth parameter set NAL units
dps_id in slice header indicates which Depth Parameter Set is used
JCT3V-B0033

## Slide 4: DPS Loss Detection
max_dps_id given in SPS: dps_id in DPS in the range of 1 to max_dps_id+1
max_dps_id_diff given in SPS: a range of dps_id values that are considered “used”
  The range is relative to the maximum used dps_id value
  A DPS in the “used” range can be retransmitted (for error resilience)
  A new DPS must use an dps_id from the “unused” range (usually increment by 1 in modulo arithmetic)
  When maximum used dps_id value is updated, the DPSes that fall outside the window of “used dps_id values” are marked as unavailable – hence, no accidental re-use of a DPS can happen
1
max_dps_id
Max used dps_id
max_dps_id_diff
”used dps_id values”
”unused”
”unused”
JCT3V-B0033
Constraint: max_dps_id_diff * 2 shall be less than max_dps_id