## Slide 1: 3D-CE5.h related:Early Termination of PU Prediction in Depth Intra Coding (JCT3V-B0042)
2012-10-1
ZTE Corporation
Hongwei Li, Ming Li, Ping Wu
Yingjie Hong,Guoqiang Shang

## Slide 2: Outline
1. Summary
2. Motivation
3. Proposed Method
4. Experimental Results
5. Conclusion

## Slide 3: Summary
Proposed method
  Fully standard compliant, no syntax change
  Perform an early termination of PU prediction in depth intra prediction for DMM by three judgments conditions.
Performance
  For intra-only configuration
  0.8% BD-rate change on “coded and synthesized view” on average
  The encoding and decoding runtime is reduced by 41.1% and 24.2% ,respectively.
Notes: <number>

## Slide 4: Motivation
DMM takes very high percentage of coding time while comparing with other intra coding modes
The bigger the size of the block , the longer the runtime for DMM.
The possibility which the prediction mode of the big PU becomes the final prediction mode of this PU is small.
when the difference between maximum and minimum pixel values in a PU is less than 10, the possibility which DMM is selected as the final prediction mode is small.
Evidences show that DMM mainly is applied to a depth block containing an edge, and also this kind of block contains two different constant pixel regions at least
Notes: <number>

## Slide 5: Proposed Method

## Slide 6: Experimental Results
Experimental Results
 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.0% | 1.0% | 0.7% | 58.0% | 80.9% | 95.1%
Kendo | 0.0% | 1.5% | 1.0% | 62.9% | 83.4% | 94.6%
Newspapercc | 0.0% | 1.8% | 1.2% | 56.7% | 62.3% | 99.2%
GhostTownFly | 0.0% | 1.2% | 0.9% | 72.2% | 73.4% | 98.5%
PoznanHall2 | 0.0% | 1.7% | 1.1% | 51.7% | 92.6% | 95.2%
PoznanStreet | 0.0% | 0.9% | 0.6% | 61.5% | 63.4% | 99.6%
UndoDancer | 0.0% | 0.5% | 0.3% | 52.1% | 79.4% | 101.6%
1024x768 | 0.0% | 1.4% | 0.9% | 59.1% | 74.9% | 96.3%
1920x1088 | 0.0% | 1.1% | 0.7% | 58.8% | 76.5% | 98.7%
average | 0.0% | 1.2% | 0.8% | 58.9% | 75.8% | 97.7%
Configuration: the intra-only configuration for CE6
Software version:HTM4.0.1
Notes:
Compare “HTM4.0.1 without DMM” to “HTM4.0.1 with DMM”, Qp=25
 | enctime | dectime
Balloons | 45.8 | 85.7%

## Slide 7: Conclusion
Method being tested
  Perform an early termination of PU prediction in depth intra prediction for DMM by three conditions.
  No decoder change is needed.
Performance
  The encoding and decoding runtime is reduced by 41.1% and 24.2% ,respectively .
  -0.8% BD-rate gain
<number>
Notes: <number>