## Slide 1
1. Summary
2. Proposed Method
3. Experimental Results
4. Conclusion
Contents
3D-CE2.h : Results of Illumination Compensation for Inter-View Prediction (JCT3V-B0045)
2012-10-12
China TV Lab. / Media Part
Hongbin Liu, Jiwook Jung, Jaewon Sung, Jie Jia, Sehoon Yea
(LG Electronics)

## Slide 2: Summary
Proposed method
  Linear illumination compensation (IC) model is used to correct discrepancy between different views
Performance
When IC is applied to luma, chroma and depth
  -0.7%, -1.0% BD-rate gain on two side views on average
  -0.3% BD-rate gain on “coded and synthesized view” on average
  Best performance is achieved on kendo, -3.6%, -4.0% gain on two side views, -1.3% gain on coded and synthesized view.
Crosscheck
  JCT3V-B0072 (by ETRI and KHU)
  JCT3V-Bxxxx (by Qualcomm)
JCT3V-B0045

## Slide 3: Proposed Method
Motivation
  mismatch may occur when cameras at different positions are not perfectly calibrated.
Proposed
  Encoder and Decoder use same
  method to calculate linear
  parameters
  CU level IC flag
Current inter-view motion compensation
Proposed inter-view motion compensation
JCT3V-B0045

## Slide 4: Proposed Method
Proposed
Picture level IC flag
  To prevent inefficient usage of IC
  Encode a flag for each picture of dependent views
  Signaled at slice header of the first slice
Simplification of Encoder
  If the best mode after checking Merge mode and Size_2Nx2N mode does not employ IC, disable IC in the following inter modes.
  Otherwise, perform rate distortion optimized selection between IC on/off for the following inter modes.
JCT3V-B0045
Picture level IC flag decision process

## Slide 5: Experimental Results
JCT3V-B0045
Five simulation sets
  Set 1: Weighted prediction is enabled
  Set 2: Illumination compensation is enabled on luma
  Set 3: Weighted prediction is enabled + illumination compensation is enabled on luma
  Set 4: Illumination compensation is enabled on both luma and depth
  Set 5: Illumination compensation is enabled on both luma and chroma

## Slide 6: Set1: Weighted prediction
Table 1: Results of weighted prediction
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.1% | 0.4% | 0.4% | 0.2% | 0.5% | 0.5% | 106.3% | 99.5%
Kendo | 0.1% | 0.5% | 0.0% | 0.1% | 1.0% | 1.0% | 145.2% | 103.7%
Newspapercc | 0.1% | 0.4% | 0.4% | 0.2% | 0.4% | 0.4% | 118.2% | 101.7%
GhostTownFly | 0.4% | 0.3% | 0.3% | 0.4% | -0.2% | -0.1% | 152.6% | 102.3%
PoznanHall2 | 0.1% | 0.5% | 0.5% | 0.3% | 1.0% | 0.9% | 124.0% | 89.2%
PoznanStreet | 0.0% | 0.3% | 0.3% | 0.1% | 0.2% | 0.2% | 103.1% | 98.0%
UndoDancer | 0.0% | 0.1% | 0.2% | 0.1% | 0.0% | 0.1% | 119.0% | 108.9%
1024x768 | 0.1% | 0.4% | 0.2% | 0.2% | 0.6% | 0.6% | 122.2% | 101.6%
1920x1088 | 0.2% | 0.3% | 0.3% | 0.2% | 0.3% | 0.3% | 123.4% | 99.4%
average | 0.1% | 0.4% | 0.3% | 0.2% | 0.4% | 0.4% | 122.9% | 100.3%

## Slide 7: Set2: Illumination compensation on Luma
Table 2: Results of illumination compensation on luma
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | -1.4% | -1.1% | -0.6% | -0.4% | -0.5% | 109.1% | 101.1%
Kendo | 0.0% | -3.1% | -3.3% | -1.4% | -1.0% | -1.1% | 114.2% | 100.9%
Newspapercc | 0.0% | -0.6% | -0.8% | -0.3% | -0.2% | -0.2% | 108.2% | 101.2%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 105.4% | 100.6%
PoznanHall2 | 0.0% | 0.3% | -0.8% | -0.2% | -0.1% | -0.1% | 108.6% | 93.2%
PoznanStreet | 0.0% | 0.1% | -0.2% | 0.0% | 0.0% | 0.0% | 106.1% | 96.9%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 105.0% | 104.8%
1024x768 | 0.0% | -1.7% | -1.7% | -0.7% | -0.5% | -0.6% | 110.5% | 101.1%
1920x1088 | 0.0% | 0.1% | -0.3% | 0.0% | 0.0% | 0.0% | 106.3% | 98.8%
average | 0.0% | -0.7% | -0.9% | -0.3% | -0.2% | -0.3% | 108.0% | 99.8%

## Slide 8: Set3: Weighted prediction + Illumination compensation on Luma
Table 3: Results of weighted prediction + illumination compensation on luma
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.1% | -0.9% | -0.5% | -0.3% | 0.1% | 0.0% | 117.0% | 100.9%
Kendo | 0.1% | -2.0% | -1.8% | -0.8% | 0.3% | 0.2% | 151.3% | 102.6%
Newspapercc | 0.1% | -0.1% | -0.4% | -0.1% | 0.2% | 0.2% | 125.2% | 101.3%
GhostTownFly | 0.4% | 0.3% | 0.3% | 0.4% | -0.1% | -0.1% | 154.6% | 104.2%
PoznanHall2 | 0.1% | 0.8% | -0.3% | 0.1% | 0.9% | 0.8% | 125.5% | 101.0%
PoznanStreet | 0.0% | 0.4% | 0.1% | 0.1% | 0.2% | 0.2% | 107.0% | 101.1%
UndoDancer | 0.0% | 0.2% | 0.2% | 0.1% | 0.0% | 0.0% | 125.5% | 98.2%
1024x768 | 0.1% | -1.0% | -0.9% | -0.4% | 0.2% | 0.2% | 130.4% | 101.6%
1920x1088 | 0.2% | 0.4% | 0.1% | 0.2% | 0.2% | 0.2% | 127.1% | 101.1%
average | 0.1% | -0.2% | -0.4% | -0.1% | 0.2% | 0.2% | 128.5% | 101.3%

## Slide 9: Set4: Illumination compensation on Luma and Depth
Table 4: Results of illumination compensation on luma and depth
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | -1.4% | -1.1% | -0.6% | -0.6% | -0.6% | 115.8% | 100.9%
Kendo | 0.0% | -3.1% | -3.3% | -1.4% | -1.4% | -1.3% | 122.8% | 102.6%
Newspapercc | 0.0% | -0.6% | -0.8% | -0.3% | -1.2% | -1.0% | 116.9% | 101.3%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 108.9% | 104.2%
PoznanHall2 | 0.0% | 0.3% | -0.8% | -0.2% | -0.2% | -0.2% | 116.3% | 101.0%
PoznanStreet | 0.0% | 0.1% | -0.2% | 0.0% | -0.3% | -0.2% | 113.4% | 101.1%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 111.2% | 98.2%
1024x768 | 0.0% | -1.7% | -1.7% | -0.7% | -1.1% | -1.0% | 118.4% | 101.6%
1920x1088 | 0.0% | 0.1% | -0.3% | 0.0% | -0.2% | -0.1% | 112.4% | 101.1%
average | 0.0% | -0.7% | -0.9% | -0.3% | -0.6% | -0.5% | 115.0% | 101.3%

## Slide 10: Set5: Illumination compensation on Luma and Chroma
Table 5: Results of illumination compensation on luma and chroma
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | -1.2% | -1.5% | -0.6% | -0.4% | -0.5% | 107.8% | 99.8%
Kendo | 0.0% | -3.6% | -4.0% | -1.6% | -1.3% | -1.3% | 109.3% | 99.7%
Newspapercc | 0.0% | -0.6% | -1.1% | -0.4% | -0.2% | -0.3% | 106.5% | 100.0%
GhostTownFly | 0.0% | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 104.5% | 99.9%
PoznanHall2 | 0.0% | 0.1% | -0.1% | -0.1% | 0.1% | 0.0% | 106.3% | 99.8%
PoznanStreet | 0.0% | 0.0% | -0.4% | -0.1% | -0.1% | -0.1% | 106.0% | 94.9%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 105.9% | 99.8%
1024x768 | 0.0% | -1.8% | -2.2% | -0.8% | -0.6% | -0.7% | 107.9% | 99.8%
1920x1088 | 0.0% | 0.0% | -0.1% | 0.0% | 0.0% | 0.0% | 105.7% | 98.6%
average | 0.0% | -0.7% | -1.0% | -0.4% | -0.3% | -0.3% | 106.6% | 99.1%

## Slide 11: Conclusion
Propose method
  Linear illumination compensation (IC) model is used to correct discrepancy between different views
  Picture level IC flag is used to prevent inefficient IC use
Performance
  Influence of illumination compensation does not overlap with weighted prediction much
  -0.7%, -1.0% BD-rate gain on two side views on average, with maximum -3.6%, -4.0% BD-rate gain for kendo.
  -0.3% BD-rate gain on “coded and synthesized view” on average, with maximum -1.3% BD-rate gain for kendo.
  Small influence on decoding time
It is recommended to adopt illumination compensation into 3D-HEVC
JCT3V-B0045