## Slide 1: JCT3v-b0058/M26750: report on the relation of global view and depth format and 3DV standardization tracks
October 13, 2012
Takanori Senoh, et al. (NICT)
Masayuki tanimoto, et al.(NISRI)

## Slide 2
Introduction
This contribution reports on the AHG8 mandate:
Explore the relation of Global View and Depth format and 3DV standardization tracks.
Global View and Depth format : Low complexity
Current 3DV standardization tracks: High coding efficiency
Global View and Depth format
Depth maps
Multi-views
Bit stream
3DV standardization tracks
Bit stream
High quality
Easy implementation
Low complexity
High coding efficiency

## Slide 3
Global view and depth
Approach:
- Frame-base view synthesis prediction (VSP) only
- Fast encoding/decoding process (Low complexity)
- Subjectively good view quality (Reasonable coding efficiency)
Core codec
(AVC or HEVC)
Global depth
Residual view
Post-process (View synthesis)
Depth maps
Multi-views
Decoded global view
Synthesized
views
Pre-process (Global depth, Residual)
Decoded depth
global view
Decoded
Residual view
Decoded
global depth
Base view
Forward compatibility

## Slide 4
Current 3DV tracks
Approach:
- Addition of inter-depth coding or view synthesis prediction (VSP)
- Realizing high coding efficiency
- High complexity (long encoding/decoding time)
MVC + D
Depth maps
Multi-views
MVC + VSP
Bit stream
HEVC + MVC
+ VSP
Bit stream
Bit stream
Forward compatibility
High quality
High coding efficiency
These codecs are slow because of search-base inter-view prediction.
Simple extension of MVC
Higher coding efficiency

## Slide 5
Relation
3DV Coding will need both low complexity profile and high coding efficiency profile to suffice wide variety of market requirements.
Low complexity: Global View and Depth format
High coding efficiency: Current 3DV standardization tracks
Global View and Depth tools
Tools of 3DV standardization tracks
Low complexity profile
High coding efficiency profile
Core codec
(AVC, HEVC)

## Slide 6
Warp(for your reference)
Approach:
- Replacing depth with warp data
- Subjectively good image quality (no sharp artifacts)
- Concentrated on multi-view 3D image (no depth-base 3D image)
Core codec
(MVC or HEVC+MVC)
Warp generation
Depth maps
Multi-views
View warp
Multi-views
Synthesized
views
2D shift

## Slide 7
Global view/Depth and warp
Both Global View and Depth format and Warp format are necessary for wide variety of applications having different requirements.
Global View and Depth format
Depth maps
Multi-views
Bit stream
Warp format
Bit stream
Depth-base
Warp-base
Wide variety of applications
Free Viewpoint
Light Field display
Volume scanning display
Aerial 3D display
Multi-view 3D display
Subjectively smooth
Wide application capability

## Slide 8
conclusion
Both Global View and Depth format and current 3DV tracks are necessary for wide variety of market requirements.
Global View and Depth format
Depth maps
Multi-views
Bit stream
3DV standardization tracks
Bit stream
High quality
Easy implementation
Low complexity
High coding efficiency
Forward compatibility