## Slide 1: JCT3V-B0078 CE5.h: Reducing the coding cost of merge index by dynamic merge index re-allocation
T. Guionnet (INRIA)
L. Guillo (Irisa/CNRS)
C. Guillemot (INRIA)
October 2012

## Slide 2: Introduction
  HEVC: Merge candidate list
    Order of the candidates carefully designed: Most likely candidates first
  Encoding of the merge index
    Binarization using unary code: most likely candidate gets the shortest codeword
    CABAC in equiprobable mode, except for the first bin
  3D-HTM: inter-view motion prediction
    New candidate added at the beginning of the list
    Inter-view motion predictor generally the most likely,
    But not always: In second or third position for 11% of the images of the CTC test set

## Slide 3: Proposed method
  Dynamic merge index
    Keep track of the merge index likelihoods thanks to a histogram
    Update the histogram each time a merge index is decoded/encoded
    Derive a conversion table from the histogram
    Only the 3 first merge indexes are considered

## Slide 4: Proposed method
  Parsing process adaptation
    Dynamic merge index re-allocation impacts the bins distribution (Mainly 3 first bins)
    CABAC contexts dedicated to the merge index permutations (6 possible permutations)
    3 first bins with CABAC contexts, others bypassed

## Slide 5: Results
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0,0% | -0,2% | -0,2% | -0,1% | -0,1% | -0,1% | 100,4% | 100,6%
Kendo | 0,0% | -0,1% | 0,0% | 0,0% | 0,0% | 0,0% | 100,6% | 100,9%
Newspapercc | 0,0% | -0,1% | -0,3% | -0,1% | -0,1% | -0,1% | 100,0% | 98,9%
GhostTownFly | 0,0% | -1,0% | -1,0% | -0,2% | -0,2% | -0,2% | 102,3% | 99,7%
PoznanHall2 | 0,0% | -0,1% | -0,4% | -0,1% | -0,1% | -0,1% | 102,3% | 98,3%
PoznanStreet | 0,0% | -0,6% | -0,4% | -0,2% | -0,2% | -0,2% | 99,8% | 99,6%
UndoDancer | 0,0% | -0,7% | -0,6% | -0,2% | -0,2% | -0,2% | 100,1% | 99,7%
1024x768 | 0,0% | -0,1% | -0,1% | -0,1% | 0,0% | 0,0% | 100,3% | 100,1%
1920x1088 | 0,0% | -0,6% | -0,6% | -0,2% | -0,2% | -0,2% | 101,1% | 99,3%
Average | 0,0% | -0,4% | -0,4% | -0,1% | -0,1% | -0,1% | 100,8% | 99,7%

## Slide 6: Conclusion
  0.4 % gain on average on side views
  Gain can be high, depending on the sequence: up to 1%
  No added complexity
  Proposed for adoption
  Thanks to Orange for cross-checking (JCT3V-B0097)