## Slide 1: 3D-CE5.h related: Restricted motion vector coding for inter-view prediction
Uchiumi Tadashi and Tomohiro Ikai
Sharp Corporation
Document: JCT3V-B0113
Oct. 2012, Shanghai, China

## Slide 2: Summary
For sequences of which the vertical component of disparity vector is always zero
In the proposed method, vertical component of disparity vector difference (mvd) is not sent because it is redundant
The proposal achieves coding gains of 0.4% compared to encoder only restriction
JCT3V-B0113

## Slide 3: Introduction
Stereoscopic video sequences are arranged with 1-D camera arrangement
Vertical component of motion vector difference is always zero when that arrangement is precise
Accurate 1-D camera arrangement has no vertical disparity
x
y
No disparity in y-direction
JCT3V-B0113
the sending of the vertical disparity vector is totally redundant

## Slide 4: Proposal
Vertical component of disparity vector difference is not sent at accurate setting sequences
A new flag disp_mvdy_zero_flag is added in SPS to indicate whether vertical component can be ommited
Decoder
Encoder
disp_mvdy_zero_flag = 1 ( in SPS )
mvdLX[1] of disparity vector
Video sequence with no vertical disparity
JCT3V-B0113
mvdLX[0] of disparity vector

## Slide 5: Details and Text (1)
A flag is added in SPS extension
seq_parameter_set_extension_rbsp( ) { | Descriptor
… | 
base_view_flag | u(1)
if (!base_view_flag){ | 
disp_mvdy_zero_flag | u(1)
depth_flag | u(1)
… | 
} | 
… | 
} | 
disp_mvdy_zero_flag equals to 1 specifies that the vertical component of motion vector associated with inter-view prediction shall be zero and its difference is not present. disp_mvdy_zero_flag equals to 0 specifies that that vertical components of motion vector differences is present. When disp_mvdy_zero_flag is not present, it is inferred to be equal to 0.
JCT3V-B0113

## Slide 6: Details and Text (2)
mvdLX[1] is conditionally omited
mvd_coding( x0, y0, refList ) { | Descriptor
abs_mvd_greater0_flag[ 0 ] | ae(v)
if(!inter_view_pred ¦¦ !disp_mvdy_zero_flag) | 
abs_mvd_greater0_flag[ 1 ] | ae(v)
if(abs_mvd_greater0_flag[ 0 ] ) | 
abs_mvd_greater1_flag[ 0 ] | ae(v)
if(abs_mvd_greater0_flag[ 1 ] ) | 
abs_mvd_greater1_flag[ 1 ] | ae(v)
if(abs_mvd_greater0_flag[ 0 ] ) { | 
if(abs_mvd_greater1_flag[ 0 ] ) | 
abs_mvd_minus2[ 0 ] | ae(v)
mvd_sign_flag[ 0 ] | ae(v)
} | 
if(abs_mvd_greater0_flag[ 1 ] ) { | 
if(abs_mvd_greater1_flag[ 1 ] ) | 
abs_mvd_minus2[ 1 ] | ae(v)
mvd_sign_flag[ 1 ] | ae(v)
} | 
} | 
JCT3V-B0113

## Slide 7: Details and Text (3)
mvdLX[1] is inferred to be zero if it is ommited
abs_mvd_greater0_flag[ compIdx ] specifies whether the absolute value of a motion vector component difference is greater than 0. The horizontal motion vector component difference is assigned compIdx = 0 and the vertical motion vector component is assigned compIdx = 1.
When abs_mvd_greater0_flag is not present, it is inferred to be equal to 0.
The variable inter_view_pred , which specifies whether the prediction unit associated with the motion vector difference is used as inter-view prediction, is derived as follows
When the ViewId of the RefPicListLX[ refIdxLX ] is not equal to ViewId, inter_view_pred is set to be 1, otherwise inter_view_pred is set to be 0.
JCT3V-B0113

## Slide 8: Non-normative change
Motion estimation is restricted at encoder
  Set vertical search range for inter-view prediction to zero
Restriction on disparity vector search
Reference Picture (e.g. view 0)
Disparity vector mv = (x,0)
Search range (vertical direction = 0)
Coding Picture (e.g. view 1)
JCT3V-B0113

## Slide 9: Simulation results
Table 1: Experimental result (proposal)
At the accurate arranged sequences such as GhostTownFly and UndoDancer, the disparity vector can be restricted without significant loss
Enc time decreased by 10 %
Sequences | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.0% | 4.4% | 2.1% | 1.5% | 1.0% | 1.1% | 90.7% | 94.5% | 100.4%
Kendo | 0.0% | 4.0% | 1.9% | 1.4% | 0.9% | 1.0% | 89.1% | 94.9% | 99.4%
Newspapercc | 0.0% | 3.6% | 10.0% | 3.0% | 1.9% | 2.1% | 87.3% | 93.7% | 99.7%
GhostTownFly | 0.0% | -0.9% | -0.5% | 0.0% | 0.0% | 0.0% | 91.6% | 93.6% | 100.6%
PoznanHall2 | 0.0% | 9.9% | 7.0% | 4.1% | 2.9% | 3.2% | 88.7% | 95.6% | 101.0%
PoznanStreet | 0.0% | 21.2% | 26.1% | 8.2% | 6.0% | 6.5% | 89.5% | 93.1% | 99.6%
UndoDancer | 0.0% | -0.5% | -0.6% | -0.1% | 0.2% | 0.1% | 91.9% | 94.2% | 100.7%
1024x768 | 0.0% | 4.0% | 4.6% | 1.9% | 1.2% | 1.4% | 89.0% | 94.4% | 99.8%
1920x1088 | 0.0% | 7.4% | 8.0% | 3.0% | 2.3% | 2.4% | 90.4% | 94.1% | 100.5%
average | 0.0% | 6.0% | 6.6% | 2.6% | 1.8% | 2.0% | 89.8% | 94.2% | 100.2%
JCT3V-B0113

## Slide 10: Additional test
Table 2: Experimental result (encoder restriction only)
Encoder only restriction was tested for comparison
Without proposal, the coding efficiency is 0.4% worse
Sequences | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.0% | 5.2% | 2.7% | 1.8% | 1.2% | 1.4% | 90.7% | 97.2% | 99.7%
Kendo | 0.0% | 4.8% | 2.8% | 1.7% | 1.2% | 1.3% | 88.9% | 96.4% | 100.6%
Newspapercc | 0.0% | 4.8% | 10.9% | 3.4% | 2.3% | 2.5% | 87.1% | 100.1% | 99.2%
GhostTownFly | 0.0% | 0.7% | 0.8% | 0.4% | 0.4% | 0.4% | 90.4% | 97.8% | 102.4%
PoznanHall2 | 0.0% | 11.4% | 8.2% | 4.7% | 3.4% | 3.7% | 88.7% | 95.7% | 99.0%
PoznanStreet | 0.0% | 22.8% | 28.0% | 8.8% | 6.5% | 7.0% | 90.2% | 95.7% | 97.6%
UndoDancer | 0.0% | 0.7% | 0.7% | 0.4% | 0.6% | 0.5% | 91.3% | 96.9% | 101.3%
1024x768 | 0.0% | 4.9% | 5.5% | 2.3% | 1.6% | 1.7% | 88.9% | 97.9% | 99.8%
1920x1088 | 0.0% | 8.9% | 9.4% | 3.6% | 2.7% | 2.9% | 90.1% | 96.5% | 100.1%
average | 0.0% | 7.2% | 7.7% | 3.0% | 2.2% | 2.4% | 89.6% | 97.1% | 100.0%
JCT3V-B0113

## Slide 11: Conclusions & Remarks
In the practical encoder, zero restriction at vertical component of disparity vector is beneficial
Experiment shows two accurate arrangement sequences can be encoded without significant loss if proposed motion vector coding scheme is applied (0.4% loss at encoder only case)
It is recommended to adopt the motion vector coding scheme into next HTM
  This proposal has been cross-checked by Sony (JCT3V-B0197). Thanks for the cross-checking
JCT3V-B0113