## Slide 1
Jung-Ah Choi, Cheon Lee, and Yo-Sung Ho
October 13th, 2012
Gwangju Institute of Science and Technology
Throughput Improvement on CABAC for Depth Videos with Modified Level Coding
ISO/IEC JTC1/SC29/WG11
JCT3V-B0123

## Slide 2: Throughput Issue
Key issue of CABAC decoding
  Other processes can be parallelized
  The serial nature of entropy coders
    Bottleneck for overall codec performance
CABAC gives a good coding efficiency, but its throughput remains a challenge
  CABAC: ~ 1 bin/cycle
  CAVLC: at least one codeword/cycle

## Slide 3: Two Coding Modes in CABAC
Regular coding mode (≡ context-coded bin)
  LPS value and LPS probability of each bin are estimated by a predetermined context model
  Each bin is encoded by binary arithmetic coding based on LPS probability
Bypass coding mode (≡ bypass bin)
  Less complexity than the regular coding mode
  To encode a symbol having equal probability
    LPS value and LPS probability are fixed
  Estimation is skipped

## Slide 4: Main Reason of Limited Throughput
Serial dependencies in CABAC
Data dependencies for context model selection
  Often the context model selection for a bin depends on the value of a previously encoded/decoded bin
  This dependency makes parallelism difficult
Reduce context-coded bins

## Slide 5: Background
Level coding in CABAC
  Three context coded bins for one coefficient
  coeff_sign_flag and coeff_abs_ remaining are bypass bins
Not all the context-coded bins are beneficial for compression efficiency while exaggerating the throughput
  Code up to 8 coeff_abs_level_greater1_flag for the non-zero coefficients in a subset of 16 coefficients
  Code up to 1 coeff_abs_level_greater2_flag a subset of 16 coefficients
  Early switch to Golomb-Rice bypass code
significant_coeff_flag
coeff_abs_level_greater1_flag
coeff_abs_level_greater2_flag
coeff_sign_flag
coeff_abs_remaining

## Slide 6: Background
Example of level coding
 | 0 | 1 | -1 | 0 | 2 | 4 | -1 | -4 | 4 | 2 | -6 | 4 | 7 | 6 | -12 | 18
(a) | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
(b) |  | 0 | 0 |  | 1 | 1 | 0 | 1 | 1 | 1 |  |  |  |  |  | 
(c) |  |  |  |  | 0 |  |  |  |  |  |  |  |  |  |  | 
(d) |  | 0 | 1 |  | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
(e) |  |  |  |  |  | 2 |  | 2 | 2 | 0 | 5 | 3 | 6 | 5 | 10 | 17
Coding order
(a) significant_coeff_flag
(b) coeff_abs_level_greater1_flag
(c) coeff_abs_level_greater2_flag
(d) coeff_sign_flag
(e) coeff_abs_remaining
18 | 6 | -6 | -1
-12 | 4 | -4 | 0
7 | 4 | 2 | 1
2 | 4 | -1 | 0

## Slide 7: Motivation
Level coding in the current HTM is originally designed for texture → Level coding modification for depth is required
It can be observed that “often” a given texture TU has a lot of quantized transform coefficients than its collocated depth TU → The number of coeff_abs_level_greater1_flag can be reduced

## Slide 8: Consideration
Then, how many context-coded bins for coeff_abs_level_greater1_flag can be reduced?
  Much context-coded bin reduction, much throughput improvement
Restriction
  Keeping coding efficiency of the current HTM
  The trade-off between coding efficiency and throughput efficiency

## Slide 9: Simulation Results (1)
coeff_abs_level_greater1_flag = 4
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 10: Simulation Results (2)
coeff_abs_level_greater1_flag = 2
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.6% | 0.3%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%
Average | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%

## Slide 11: Simulation Results (3)
coeff_abs_level_greater1_flag = 0, so coeff_abs_level_greater2_flag = 0
  In most cases, no coding efficiency loss
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 0.1%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0%
Average | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1%

## Slide 12: Proposal
Do not code coeff_abs_level_greater1_flag and coeff_abs_level_greater2_flag in depth coding (empirically determined)
(a) significant_coeff_flag
(b) coeff_abs_level_greater1_flag
(c) coeff_abs_level_greater2_flag
(d) coeff_sign_flag
(e) coeff_abs_remaining
 | 0 | 1 | -1 | 0 | 2 | 4 | -1 | -4 | 4 | 2 | -6 | 4 | 7 | 6 | -12 | 18
(a) | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
(b) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(c) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
(d) |  | 0 | 1 |  | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
(e) |  | 0 | 0 |  | 1 | 3 |  | 3 | 3 | 1 | 5 | 3 | 6 | 5 | 10 | 17
Coding order
18 | 6 | -6 | -1
-12 | 4 | -4 | 0
7 | 4 | 2 | 1
2 | 4 | -1 | 0

## Slide 13: Throughput Efficiency
Maximum number of context coded bins between HTM 4.0.1 and proposed method in worst-case scenario
  Reduces the maximum numbers of context bins from 25 to 16
  36% of context-coded bins in level coding are reduced
 | HTM 4.0.1 | Proposed Method
significant_coeff_flag | 16 | 16
coeff_abs_level_greater1_flag | 8 | 0
coeff_abs_level_greater2_flag | 1 | 0
Total | 25 | 16

## Slide 14: Summary
Simple change of current CABAC to restrict the number of context-coded bins to improve throughput
  Modified level coding for keeping coding performance
36% of context-coded bins of CABAC level coding in depth coding is reduced
  No significant coding efficiency loss on average
  No encoding/decoding/rendering time increase
It seems worth reducing context-coded bins of CABAC considering characteristics of depth videos
  Processes of current CABAC are kept unchanged
  No additional module is needed