## Slide 1
Do-Young Kim, Woo-Seok Jang, and Yo-Sung Ho
October 13th, 2012
Gwangju Institute of Science and Technology
Analysis of View Synthesis Methods (VSRS 1D fast vs. VSRS 3.5)
ISO/IEC JTC1/SC29/WG11
JCT3V-B0124

## Slide 2: Motivation
There are two reference software for virtual view generation (VSRS3.5 and VSRS 1D Fast)
Coding Tools with VSRS
  View Synthesis Prediction (VSP) and View Synthesis Optimization (VSO)
  Better synthesis performance can improve coding gain.
Two VSRS software generated different synthesized image with the same depth data
?
Which tool is better?
What error compensation method is in the VSRS tools?
Which type of depth data between blurred depth and edge-preserved is better?

## Slide 3: Flow Chart of View Synthesis Methods
Up sampling
Warping
Interpolation
Hole Filling
Reliability
Map Creation
Similarity
Enhancement
Combination
Chroma
Decimation
Texture
Depth
Synthesis
Output
Mapping to
Target View
Texture Mapping
Synthesis
Output
Filtering by
Median Filter
Hole Filling
Blending
Inpainting
Texture
Depth
VSRS 1D Fast
VSRS 3.5

## Slide 4: VSRS 1D Fast vs. VSRS 3.5
 | VSRS 1D Fast | VSRS 3.5
Projection to target viewpoint | Disparity shifting | 3D image warping
Mapping to target viewpoint | Interpolation and processing according to disocclusion and occlusion | Processing according to homography
Hole filling | Line-wise background extension | Inpainting
Combination stage | Similarity enhancement and blending according to reliability map | Blending according to weighting

## Slide 5: Process of View Synthesis Methods
Up sampling
Warping
Interpolation
Hole Filling
Reliability
Map Creation
Similarity
Enhancement
Combination
Chroma
Decimation
Texture
Depth
Synthesis
Output
Mapping to
Target View
Texture Mapping
Synthesis
Output
Filtering by
Median Filter
Hole Filling
Blending
Inpainting
Texture
Depth
Warping stage
Combination stage
VSRS 1D Fast
VSRS 3.5

## Slide 6: Performance Evaluation (1)
Synthesis quality
  Goal: To compare synthesis results generated by the original depth data
  Differences in PSNR values between the original and original synthesis sequences
  Performance comparison between results at each stage
Original
View
Synthesis
Original synthesis
Difference

## Slide 7: Result for Synthesis Performance
Performance improvement
  Combination stage in VSRS 1D fast
  Gain = Final result – result of warping stage (PSNR)
 | Results of warping stage (dB) |  |  | Final Results (dB) |  |  | Gain (dB) |  | 
Method | 1D fast | VSRS | ∆ | 1D fast | VSRS | ∆ | 1D fast | VSRS | ∆
Dancer | 40.8872 | 37.4513 | 3.4359 | 42.4126 | 39.1757 | 3.2369 | 1.5254 | 1.7244 | -0.1990
Kendo | 35.3161 | 36.0073 | -0.6912 | 37.1833 | 37.4609 | -0.2776 | 1.8672 | 1.4536 | 0.4136
Balloons | 34.3989 | 35.3905 | -0.9916 | 36.3434 | 36.4584 | -0.1150 | 1.9445 | 1.0679 | 0.8766
Newspaper | 28.6552 | 30.8054 | -2.1502 | 33.2104 | 32.8799 | 0.3305 | 4.5552 | 2.0745 | 2.4807

## Slide 8: Comparison of Synthesis Performance
Chart: 
| 1D fast | VSRS | 1D fast | VSRS | 1D fast | VSRS | 1D fast | VSRS | Dancer | Kendo | Balloons | Newspaper
Results of warping stage (dB) | 40.8872 | 37.4513 | 35.3161 | 36.0073 | 34.3989 | 35.3905 | 28.6552 | 30.8054
Gain (dB) | 1.5254 | 1.7244 | 1.8672 | 1.4536 | 1.9445 | 1.0679 | 4.5552 | 2.0745

## Slide 9: Performance Evaluation (2)
Quality of coding error compensation
  Goal: To compare synthesis results generated by the coded depth data
  Two depth data
    VSO on: relatively blurred depth data due to VSO
    VSO off: edge preserved depth data
  Differences in PSNR values between the original and encoded synthesis sequences
  Performance comparison between results at each stage
Encoded
(VSO on/off)
View
Synthesis
Encoded synthesis
Original
Difference

## Slide 10: Results for Coding Error Compensation
VSO ON |  |  |  |  |  |  |  |  | 
 | Results of warping stage (dB) |  |  | Final Results (dB) |  |  | Gain (dB) |  | 
Method | 1D fast | VSRS | ∆ | 1D fast | VSRS | ∆ | 1D fast | VSRS | ∆
Dancer | 35.7805 | 32.8516 | 2.9289 | 36.5520 | 33.2861 | 3.2659 | 0.7715 | 0.4345 | 0.3370
Kendo | 34.0252 | 34.6378 | -0.6126 | 35.5679 | 35.3742 | 0.1937 | 1.5427 | 0.7364 | 0.8063
Balloons | 33.2376 | 34.0776 | -0.8400 | 34.7637 | 34.8866 | -0.1229 | 1.5261 | 0.8090 | 0.7171
Newspaper | 28.3772 | 31.3274 | -2.9502 | 32.4221 | 32.4098 | 0.0123 | 4.0449 | 1.0824 | 2.9625
VSO OFF |  |  |  |  |  |  |  |  | 
 | Results of warping stage (dB) |  |  | Final Results (dB) |  |  | Gain (dB) |  | 
Method | 1D fast | VSRS | ∆ | 1D fast | VSRS | ∆ | 1D fast | VSRS | ∆
Dancer | 35.3704 | 32.3884 | 2.9820 | 36.1940 | 33.0445 | 3.1495 | 0.8236 | 0.6561 | 0.1675
Kendo | 34.0483 | 34.6384 | -0.5901 | 35.5322 | 35.4012 | 0.1310 | 1.4839 | 0.7628 | 0.7211
Balloons | 33.1821 | 33.9807 | -0.7986 | 34.7082 | 34.8429 | -0.1347 | 1.5261 | 0.8622 | 0.6639
Newspaper | 27.6487 | 31.2357 | -3.5870 | 32.1963 | 32.3898 | -0.1935 | 4.5476 | 1.1541 | 3.3935

## Slide 11: Comparison of Coding Error Compensation (1)
Chart: 
| 1D fast | VSRS | 1D fast | VSRS | 1D fast | VSRS | 1D fast | VSRS | Dancer | Kendo | Balloons | Newspaper
Results of warping stage (dB) | 35.7805 | 32.8516 | 34.0252 | 34.6378 | 33.2376 | 34.0776 | 28.3772 | 31.3274
Gain (dB) | 0.7715 | 0.4345 | 1.5427 | 0.7364 | 1.5261 | 0.809 | 4.0449 | 1.0824
VSO ON

## Slide 12: Comparison of Coding Error Compensation (2)
Chart: 
| 1D fast | VSRS | 1D fast | VSRS | 1D fast | VSRS | 1D fast | VSRS | Dancer | Kendo | Balloons | Newspaper
Results of warping stage (dB) | 35.3704 | 32.3884 | 34.0483 | 34.6384 | 33.1821 | 33.9807 | 27.6487 | 31.2357
Gain (dB) | 0.8236 | 0.6561 | 1.4839 | 0.7628 | 1.5261 | 0.8622 | 4.5476 | 1.1541
VSO OFF

## Slide 13: Performance Evaluation (3)
Coding performance
  Goal: To compare synthesis results generated by the coded depth data and the original depth data
  Differences in PSNR values between the original synthesis and encoded synthesis sequences
Encoded
View
Synthesis
Encoded synthesis
Original
Difference
View
Synthesis
Original synthesis

## Slide 14: Results for Coding Performance
 | VSO ON (dB) |  |  | VSO OFF (dB) |  | 
Method | 1D fast | VSRS | ∆ | 1D fast | VSRS | ∆
Poznan_street | 37.0828 | 36.8761 | 0.2067 (↑ 0.56%) | 36.8421 | 36.6479 | 0.1942 (↑ 0.53%)
Dancer | 37.4853 | 34.0236 | 3.4617 (↑ 10.17%) | 36.8878 | 33.8773 | 3.0105 (↑ 8.89%)
Kendo | 39.5698 | 39.3596 | 0.2102 (↑ 0.53%) | 39.3302 | 39.2675 | 0.0627 (↑ 0.16%)
Balloons | 39.1229 | 38.7785 | 0.3444 (↑ 0.89%) | 38.8649 | 38.6223 | 0.2426 (↑ 0.63%)
Newspaper | 36.7973 | 34.6244 | 2.1729 (↑ 6.28%) | 36.1561 | 34.5867 | 1.5694 (↑ 4.54%)
Average (%) | ↑ 3.69 % |  |  | ↑ 2.95 % |  | 

## Slide 15: Summary
Combination stage in VSRS 1D fast
  Performance improvement for synthesis quality
  Increased quality of coding error compensation
Coding performance of VSRS 1D fast
  Average gain 3.69% in VSO on
  Average gain 2.95% in VSO off