## Slide 1: Inter-view SAO Process in 3DV Coding (JCT3V-B0130)
Taesup Kim, Jin Heo, Moonmo Koo, Sehoon Yea
LG Electronics
Oct. 2012

## Slide 2: Introduction
Sample Adaptive Offset (SAO) Process
  In-loop filter for reconstructed signal by using offset values (org∽rec’=rec+offset)
  SAO parameters : LCU-based merge flags, offset type and values
Current
LCU
Up
LCU
Left
LCU
Merge Left Flag
Merge Up Flag
Offset Type,
Offset Values

## Slide 3: Introduction
SAO Process in 3DV Coding
View 0
SAO Parameters
Derive
Codec

## Slide 4: Introduction
SAO Process in 3DV Coding
View 0
View 1
View 2
SAO Parameters
SAO Parameters
SAO Parameters
Derive
Codec
Derive
Codec
Derive
Codec

## Slide 5: Proposed Method (1)
Simple Inter-view SAO Process
View 0
View 1
View 2
SAO Parameters
Derive
Codec

## Slide 6: Proposed Method (1)
Simple Inter-view SAO Process
View 0
View 1
View 2
SAO Parameters
Derive
Codec

## Slide 7: Proposed Method (1)
Simple Inter-view SAO Process
View 0
View 1
View 2
SAO Parameters
Derive
Codec
parseSliceHeader(){ | Desc.
… | 
if (viewIdx==0){ | 
sao_interleaving_flag | u(1)
sao_flag | u(1)
if (sao_interleaving_flag && sao_flag){ | 
sao_flag_cb | u(1)
sao_flag_cr | u(1)
} | 
} | 
… | 
} | 
Proposed syntax
change on slice header
parseAPS(viewIdx){ | Desc.
… | 
if (viewIdx==0){ | 
aps_sao_interleaving_flag | ae(v)
if (!aps_sao_interleaving_flag){ | 
aps_sao_flag | ae(v)
if (aps_sao_flag) | 
aps_sao_param() | 
} | 
} | 
… | 
} | 
Proposed syntax
change on SPS

## Slide 8: Proposed Method (2)
Inter-view SAO Process w/ Global Disp.
View 0
View 1
View 2
SAO Parameters
Derive
Codec

## Slide 9: Proposed Method (2)
Inter-view SAO Process w/ Global Disp.
View 0
View 1
View 2
SAO Parameters
Derive
Codec
w/ global disparity
between view 0 & 1
w/ global disparity
between view 0 & 2

## Slide 10: Proposed Method (2)
Inter-view SAO Process w/ Global Disp.
  Dependent views
Base View
Dependent View
Global
Disparity

## Slide 11: Proposed Method (2)
Global
Disparity
Inter-view SAO Process w/ Global Disp.
  Dependent views
Base View
Dependent View
① Align dependent view to base view
For dependent views,

## Slide 12: Proposed Method (2)
Global
Disparity
Inter-view SAO Process w/ Global Disp.
  Dependent views
Base View
Dependent View
① Align dependent view to base view
② Apply SAO process with base view’s ffffSAO parameters
(only over overlapped regions)
For dependent views,

## Slide 13: Proposed Method (2)
Inter-view SAO Process w/ Global Disp.
  Dependent views
Base View
Dependent View
Global
Disparity
parseSliceHeader(){ | Desc.
… | 
if (viewIdx==0){ | 
sao_interleaving_flag | u(1)
sao_flag | u(1)
if (sao_interleaving_flag && sao_flag){ | 
sao_flag_cb | u(1)
sao_flag_cr | u(1)
} | 
}else if (viewIdx!=0){ | 
delta_global_disparity | se(v)
} | 
… | 
} | 
Proposed syntax
change on slice header

## Slide 14: Simulation Results
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | -1.5% | -1.6% | -0.5% | -0.5% | -0.5%
Kendo | 0.0% | -1.8% | -1.4% | -0.5% | -0.5% | -0.5%
Newspapercc | 0.0% | -1.4% | -1.1% | -0.3% | -0.4% | -0.3%
GhostTownFly | 0.0% | -2.5% | -2.3% | -0.4% | 0.0% | -0.1%
PoznanHall2 | 0.0% | -1.4% | -2.4% | -0.6% | -0.7% | -0.6%
PoznanStreet | 0.0% | -2.1% | -1.1% | -0.1% | -0.4% | -0.3%
UndoDancer | 0.0% | -1.2% | -1.2% | -0.1% | -0.3% | -0.2%
1024x768 | 0.0% | -1.6% | -1.4% | -0.4% | -0.5% | -0.4%
1920x1088 | 0.0% | -1.8% | -1.8% | -0.3% | -0.3% | -0.3%
average | 0.0% | -1.7% | -1.6% | -0.4% | -0.4% | -0.4%
Rate-distortion results of proposed method (1)
‘Simple Inter-view SAO Process’

## Slide 15: Simulation Results
 | enc time | dec time | ren time
Balloons | 100.1% | 92.1% | 101.5%
Kendo | 100.1% | 101.2% | 98.8%
Newspapercc | 100.4% | 95.1% | 99.0%
GhostTownFly | 99.6% | 97.8% | 105.0%
PoznanHall2 | 99.9% | 108.9% | 105.4%
PoznanStreet | 99.9% | 98.1% | 105.6%
UndoDancer | 99.5% | 96.1% | 107.2%
1024x768 | 100.2% | 96.1% | 99.8%
1920x1088 | 99.7% | 100.1% | 105.8%
average | 99.9% | 98.4% | 103.2%
Running time ratio of proposed method (1)
‘Simple Inter-view SAO Process’

## Slide 16: Simulation Results
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | -1.5% | -1.4% | -0.4% | -0.4% | -0.4%
Kendo | 0.0% | -1.7% | -1.3% | -0.5% | -0.5% | -0.4%
Newspapercc | 0.0% | -1.3% | -0.9% | -0.2% | -0.3% | -0.2%
GhostTownFly | 0.0% | -2.2% | -2.2% | -0.4% | 0.0% | -0.1%
PoznanHall2 | 0.0% | -1.8% | -2.6% | -0.7% | -0.7% | -0.7%
PoznanStreet | 0.0% | -1.8% | -0.8% | 0.0% | -0.3% | -0.2%
UndoDancer | 0.0% | -1.4% | -1.3% | -0.2% | -0.2% | -0.2%
1024x768 | 0.0% | -1.5% | -1.2% | -0.4% | -0.4% | -0.3%
1920x1088 | 0.0% | -1.8% | -1.7% | -0.3% | -0.3% | -0.3%
average | 0.0% | -1.7% | -1.5% | -0.3% | -0.3% | -0.3%
Rate-distortion results of proposed method (2)
‘Inter-view SAO Process w/ Global Disp.’

## Slide 17: Simulation Results
 | enc time | dec time | ren time
Balloons | 101.4% | 104.1% | 103.7%
Kendo | 101.3% | 104.1% | 102.0%
Newspapercc | 101.5% | 97.1% | 100.0%
GhostTownFly | 101.8% | 102.0% | 109.0%
PoznanHall2 | 102.1% | 105.9% | 103.7%
PoznanStreet | 102.1% | 104.9% | 98.7%
UndoDancer | 102.1% | 102.0% | 106.8%
1024x768 | 101.4% | 101.7% | 101.9%
1920x1088 | 102.0% | 103.7% | 104.5%
average | 101.8% | 102.8% | 103.4%
Running time ratio of proposed method (2)
‘Inter-view SAO Process w/ Global Disp.’

## Slide 18: Summary
1.6% ~ 1.7% BD-gains (up to 2.5%) on all dependent views (both proposed methods) w/o complexity impact
  Implementation benefits for dependent views
  - Removal of SAO parameter parsing
  - Line-memory reduction in LCU decoding
  - Simplification of SAO encoding process
  Orthogonal to migrational changes (to latest HM)
  - Non-interleaved (HM6.X) vs. Interleaved (HM8.x & beyond)
  : SAO parameter determination: Quadtree vs. LCU
  : SAO parameter signaling (SE parsing): APS vs. LCU
  - In both cases, copy stored SAO parameters per LCU
  : akin to motion/mode info pred. (CE5), but much simpler

## Slide 19: Answers to questions noted in chairs’ note
Q1) There were concerns about seeing this proposal for the first time and imposing significant changes.
Changes are limited (see JCT3V-B0130_WD_1_r2.doc &
JCT3V-B0130_WD_2_r2.doc for methods 1 & 2, respectively)
- does not touch upon SAO filtering process itself
- independent of related SE parsing process
- independent of SAO parameter determination process (i.e., Quadtree vs. Interleaved)
- Simply proposes to copy the stored filter data in LUC from the baseview and use it without having to parse & derive the filter parameter again for the dependent view

## Slide 20: Answers to questions noted in chairs’ note
Q2) Change of signalling of SAO parameters: In HM8.2 SAO parameter is signalled on CTU level, while in HM6.1 SAO parameters were signalled on picture level. This may be relevant for the contribution.
Q3) One expert expressed, that the encoder behaviour is completely changed.
Q4) There was a question, whether the gains will still be maintained with newer HM-version.
  Migrational changes are orthogonal to the
  proposal (“migration-proof”)
  - SAO parameters are copied from the exactly same data-structure (or memory area) used for decoding LCUs be it interleaved or non-interleaved mode.

## Slide 21: SAO Parameter Determination
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode

## Slide 22: SAO Parameter Determination
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode

## Slide 23: SAO Parameter Signaling
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode
parseSliceData(){ | Desc.
do { | 
// for each LCU | 
… | 
if (slice_sao_interleaving_flag){ | 
parseSaoOneLcuInterleaving(x,y) | 
} | 
… | 
} while( !end_of_slice_flag ) | 
} | 
parseAPS(viewIdx){ | Desc.
… | 
aps_sao_interleaving_flag | ae(v)
if (!aps_sao_interleaving_flag){ | 
aps_sao_flag | ae(v)
if (aps_sao_flag) | 
aps_sao_param() | 
} | 
… | 
} | 

## Slide 24: SAO Parameter Signaling
parseSliceData(){ | Desc.
do { | 
// for each LCU | 
… | 
if (slice_sao_interleaving_flag){ | 
parseSaoOneLcuInterleaving() | 
} | 
… | 
} while( !end_of_slice_flag ) | 
} | 
parseAPS(viewIdx){ | Desc.
… | 
aps_sao_interleaving_flag | ae(v)
if (!aps_sao_interleaving_flag){ | 
aps_sao_flag | ae(v)
if (aps_sao_flag) | 
aps_sao_param() | 
} | 
… | 
} | 
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode

## Slide 25: SAO Processing
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode
LCU-based
Process
Identical !

## Slide 26: SAO Processing
Current
LCU
Up
LCU
Left
LCU
Merge Left Flag
Merge Up Flag
Offset Type,
Offset Values
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode
Identical !

## Slide 27: Proposed Method
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode
Proposal is orthogonal to migrational changes
that entail determining & signaling SAO parameters