## Slide 1: Inter-view SAO Process in 3DV Coding (JCT3V-B0130)
Taesup Kim, Jin Heo, Moonmo Koo, Sehoon Yea
LG Electronics
Oct. 2012

## Slide 2: Introduction
Sample Adaptive Offset (SAO) Process
  In-loop filter for reconstructed signal by using offset values (org∽rec’=rec+offset)
  SAO parameters : LCU-based merge flags, offset type and values
Current
LCU
Up
LCU
Left
LCU
Merge Left Flag
Merge Up Flag
Offset Type,
Offset Values

## Slide 3: Introduction
SAO Process in 3DV Coding
View 0
SAO Parameters
Derive
Codec

## Slide 4: Introduction
SAO Process in 3DV Coding
View 0
View 1
View 2
SAO Parameters
SAO Parameters
SAO Parameters
Derive
Codec
Derive
Codec
Derive
Codec

## Slide 5: Proposed Method (1)
Simple Inter-view SAO Process
View 0
View 1
View 2
SAO Parameters
Derive
Codec

## Slide 6: Proposed Method (1)
Simple Inter-view SAO Process
View 0
View 1
View 2
SAO Parameters
Derive
Codec

## Slide 7: Proposed Method (1)
Simple Inter-view SAO Process
View 0
View 1
View 2
SAO Parameters
Derive
Codec
parseSliceHeader(){ | Desc.
… | 
if (viewIdx==0){ | 
sao_interleaving_flag | u(1)
sao_flag | u(1)
if (sao_interleaving_flag && sao_flag){ | 
sao_flag_cb | u(1)
sao_flag_cr | u(1)
} | 
} | 
… | 
} | 
Proposed syntax
change on slice header
parseAPS(viewIdx){ | Desc.
… | 
if (viewIdx==0){ | 
aps_sao_interleaving_flag | ae(v)
if (!aps_sao_interleaving_flag){ | 
aps_sao_flag | ae(v)
if (aps_sao_flag) | 
aps_sao_param() | 
} | 
} | 
… | 
} | 
Proposed syntax
change on SPS

## Slide 8: Proposed Method (2)
Inter-view SAO Process w/ Global Disp.
View 0
View 1
View 2
SAO Parameters
Derive
Codec

## Slide 9: Proposed Method (2)
Inter-view SAO Process w/ Global Disp.
View 0
View 1
View 2
SAO Parameters
Derive
Codec
w/ global disparity
between view 0 & 1
w/ global disparity
between view 0 & 2

## Slide 10: Proposed Method (2)
Inter-view SAO Process w/ Global Disp.
  Dependent views
Base View
Dependent View
Global
Disparity

## Slide 11: Proposed Method (2)
Global
Disparity
Inter-view SAO Process w/ Global Disp.
  Dependent views
Base View
Dependent View
① Align dependent view to base view
For dependent views,

## Slide 12: Proposed Method (2)
Global
Disparity
Inter-view SAO Process w/ Global Disp.
  Dependent views
Base View
Dependent View
① Align dependent view to base view
② Apply SAO process with base view’s ffffSAO parameters
(only over overlapped regions)
For dependent views,

## Slide 13: Proposed Method (2)
Inter-view SAO Process w/ Global Disp.
  Dependent views
Base View
Dependent View
Global
Disparity
parseSliceHeader(){ | Desc.
… | 
if (viewIdx==0){ | 
sao_interleaving_flag | u(1)
sao_flag | u(1)
if (sao_interleaving_flag && sao_flag){ | 
sao_flag_cb | u(1)
sao_flag_cr | u(1)
} | 
}else if (viewIdx!=0){ | 
delta_global_disparity | se(v)
} | 
… | 
} | 
Proposed syntax
change on slice header

## Slide 14: Simulation Results
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | -1.5% | -1.6% | -0.5% | -0.5% | -0.5%
Kendo | 0.0% | -1.8% | -1.4% | -0.5% | -0.5% | -0.5%
Newspapercc | 0.0% | -1.4% | -1.1% | -0.3% | -0.4% | -0.3%
GhostTownFly | 0.0% | -2.5% | -2.3% | -0.4% | 0.0% | -0.1%
PoznanHall2 | 0.0% | -1.4% | -2.4% | -0.6% | -0.7% | -0.6%
PoznanStreet | 0.0% | -2.1% | -1.1% | -0.1% | -0.4% | -0.3%
UndoDancer | 0.0% | -1.2% | -1.2% | -0.1% | -0.3% | -0.2%
1024x768 | 0.0% | -1.6% | -1.4% | -0.4% | -0.5% | -0.4%
1920x1088 | 0.0% | -1.8% | -1.8% | -0.3% | -0.3% | -0.3%
average | 0.0% | -1.7% | -1.6% | -0.4% | -0.4% | -0.4%
Rate-distortion results of proposed method (1)
‘Simple Inter-view SAO Process’

## Slide 15: Simulation Results
 | enc time | dec time | ren time
Balloons | 100.1% | 92.1% | 101.5%
Kendo | 100.1% | 101.2% | 98.8%
Newspapercc | 100.4% | 95.1% | 99.0%
GhostTownFly | 99.6% | 97.8% | 105.0%
PoznanHall2 | 99.9% | 108.9% | 105.4%
PoznanStreet | 99.9% | 98.1% | 105.6%
UndoDancer | 99.5% | 96.1% | 107.2%
1024x768 | 100.2% | 96.1% | 99.8%
1920x1088 | 99.7% | 100.1% | 105.8%
average | 99.9% | 98.4% | 103.2%
Running time ratio of proposed method (1)
‘Simple Inter-view SAO Process’

## Slide 16: Simulation Results
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized
Balloons | 0.0% | -1.5% | -1.4% | -0.4% | -0.4% | -0.4%
Kendo | 0.0% | -1.7% | -1.3% | -0.5% | -0.5% | -0.4%
Newspapercc | 0.0% | -1.3% | -0.9% | -0.2% | -0.3% | -0.2%
GhostTownFly | 0.0% | -2.2% | -2.2% | -0.4% | 0.0% | -0.1%
PoznanHall2 | 0.0% | -1.8% | -2.6% | -0.7% | -0.7% | -0.7%
PoznanStreet | 0.0% | -1.8% | -0.8% | 0.0% | -0.3% | -0.2%
UndoDancer | 0.0% | -1.4% | -1.3% | -0.2% | -0.2% | -0.2%
1024x768 | 0.0% | -1.5% | -1.2% | -0.4% | -0.4% | -0.3%
1920x1088 | 0.0% | -1.8% | -1.7% | -0.3% | -0.3% | -0.3%
average | 0.0% | -1.7% | -1.5% | -0.3% | -0.3% | -0.3%
Rate-distortion results of proposed method (2)
‘Inter-view SAO Process w/ Global Disp.’

## Slide 17: Simulation Results
 | enc time | dec time | ren time
Balloons | 101.4% | 104.1% | 103.7%
Kendo | 101.3% | 104.1% | 102.0%
Newspapercc | 101.5% | 97.1% | 100.0%
GhostTownFly | 101.8% | 102.0% | 109.0%
PoznanHall2 | 102.1% | 105.9% | 103.7%
PoznanStreet | 102.1% | 104.9% | 98.7%
UndoDancer | 102.1% | 102.0% | 106.8%
1024x768 | 101.4% | 101.7% | 101.9%
1920x1088 | 102.0% | 103.7% | 104.5%
average | 101.8% | 102.8% | 103.4%
Running time ratio of proposed method (2)
‘Inter-view SAO Process w/ Global Disp.’

## Slide 18: Conclusion
Report about 1.5% gains on all dependent views (both proposed methods)
  No complexity impact, removal of SAO parameter parsing & line-memory reduction for dependent views for LCU decoding, simplification of SAO encoding process
  Orthogonal to migrational changes (to HM8.X)
Recommend that ‘inter-view SAO process’ be adopted into 3DV-HEVC

## Slide 19: Q&A #1/2
Change of signalling of SAO parameters: In HM8.2 SAO parameter is signalled on CTU level, while in HM6.1 SAO parameters were signalled on picture level. This may be relevant for the contribution.
One expert expressed, that the encoder behaviour is completely changed.
There was a question, whether the gains will still be maintained with newer HM-version.
  This migrational changes are orthogonal to the proposal (“migration-proof”)

## Slide 20: Q&A #2/2
There were concerns about seeing this proposal for the first time and imposing significant changes.
Changes are limited (does not touch upon SAO process itself, nor does it SE parsing process, it just proposes to copy the stored filter data from the base view and use it without having to parse & derive the filter parameter).
In fact, we will copy SAO parameters from the exactly same data-structure (or memory area) used for decoding LCUs in both cases.
Gains are big, no complexity impact, reduction of parsing & line-memory for dependent views for LCU decoding, simplification of SAO encoding process .

## Slide 21: Sample Adaptive Offset (SAO)
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode

## Slide 22: Sample Adaptive Offset (SAO)
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode

## Slide 23: Sample Adaptive Offset (SAO)
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode
parseSliceData(){ | Desc.
do { | 
// for each LCU | 
… | 
if (slice_sao_interleaving_flag){ | 
parseSaoOneLcuInterleaving(x,y) | 
} | 
… | 
} while( !end_of_slice_flag ) | 
} | 
parseAPS(viewIdx){ | Desc.
… | 
aps_sao_interleaving_flag | ae(v)
if (!aps_sao_interleaving_flag){ | 
aps_sao_flag | ae(v)
if (aps_sao_flag) | 
aps_sao_param() | 
} | 
… | 
} | 

## Slide 24: Sample Adaptive Offset (SAO)
parseSliceData(){ | Desc.
do { | 
// for each LCU | 
… | 
if (slice_sao_interleaving_flag){ | 
parseSaoOneLcuInterleaving() | 
} | 
… | 
} while( !end_of_slice_flag ) | 
} | 
parseAPS(viewIdx){ | Desc.
… | 
aps_sao_interleaving_flag | ae(v)
if (!aps_sao_interleaving_flag){ | 
aps_sao_flag | ae(v)
if (aps_sao_flag) | 
aps_sao_param() | 
} | 
… | 
} | 
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode

## Slide 25: Sample Adaptive Offset (SAO)
Current
LCU
Up
LCU
Left
LCU
Merge Left Flag
Merge Up Flag
Offset Type,
Offset Values
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode

## Slide 26: Sample Adaptive Offset (SAO)
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode
LCU-based
Process

## Slide 27: Sample Adaptive Offset (SAO)
Proposed Method
Quadtree-based RD-opt.
3DV-HEVC CTC mode
LCU-based RD-opt.
Current HEVC mode