## Slide 1
3D-CE5.h Software fix of disparity derivation
LG Electronics
Convergence Lab.

## Slide 2: Current implementation
To indicate a block is DV-MCP block, a flag is used: DvMcpFlag
The flag is saved with other motion parameters (motion vector, reference index)
Therefore, the flag can be copied to neighbor blocks by AMVP and MERGE candidate
  the motion parameters of the DVMCP block including the flag are copied to the motion parameter candidate for a neighbor block
To prevent from propagation of the flag, the flag in each candidate is explicitly set to false after the candidate list construction.
However, the flag of temporal candidate of AMVP is not handled.
Current
block
MV
RefIdx
DvMcpFlag
Spatial
MV
DvMcpFlag
Temporal
MV
DvMcpFlag
Inter-view
MV
DvMcpFlag
Candidate list for AMVP
false
Spatial
MV
DvMcpFlag

## Slide 3: Effect of the bug and experiment results
Some inter-coded (not SKIP coded) blocks are wrongly marked as DV-MCP blocks
This bug does not affect the coding gain:
  The disparity derivation process uses only SKIP coded DV-MCP block
  No other coding tools use the DV-MCP flag
Software fix was provided to the participants of CE5.h
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | Enc time | Dec time | Ren Time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 101.2% | 108.2%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.1% | 101.8% | 104.3%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.8% | 95.7% | 96.0%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.7% | 103.3% | 112.9%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.2% | 101.0% | 103.4% | 102.5%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.8% | 102.9% | 98.8%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.9% | 103.9% | 109.2%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.1% | 99.5% | 102.7%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.8% | 103.4% | 105.7%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.5% | 101.7% | 104.4%