## Slide 1: Subjective Test Results on QuadTree Limitation and Predictive Coding (JCT3V-B0068)
JCT3V-B0222, Shanghai, October 2012
Joel Jung, Elie Mora

## Slide 2: Introduction
Quadtree limitation + predictive coding was proposed in JCT3V-B0068.
Experimental results exhibit some losses on synthetized views (PSNR losses)
The goal of this subjective session is to verify if any new visual artifact is introduced
The goal of this subjective session is not to show a quality improvement (encoder runtime = 68%)
Two viewing sessions were organized
9 people involved from 6 different companies or universities
It has been verified by a non-proponent that the results reported match with the scoring sheets.
Context:
Viewing session:

## Slide 3: Test Settings (1/2)
TEST NUMBER | Seq A | Display Seq A | Seq B | Display Seq B | Seq A | Display Seq A | Seq B | Display Seq B | Vote
Sequence A is | +3: largely better than +2: better than +1: slightly better than 0: same as -1: slightly worse than -2 worse than -3: largely worse than | Sequence B
Sequences:
Viewing session:
Reference and proposed method presented as sequences A and B (as a blind test)
A score between -3 and +3 is requested, using the following scale:
Newspaper and Balloons selected: highest objective losses on synthesized views
QP 25 selected: highest objective loss among other QPs
QP 35 selected: to provide the viewers with a more degraded version

## Slide 4: Test Settings (2/2)
3D test:
Stereo view constructed from 2 synthesized views corresponding to the two views that are the closest to the center view
Closest synthesized view on the left of the center view selected
2D test designed in case the 3D test does not allow seeing any new artifact.
2D test:

## Slide 5: 3D Test Results
Test | AVG | Viewer |  |  |  |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Balloons 25 | -0,6 | 0 | -1 | -1 | -1 | 0 | 0 | -1 | -1 | 0
Newspaper 25 | 0,1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
Balloons 35 | 0,4 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0
Newspaper 35 | -0,2 | 0 | 0 | -1 | 0 | 0 | 0 | 0 | -1 | 0
AVG | -0,1 |  |  |  |  |  |  |  |  | 
Observations:
No score above 1 or below -1 is reported.
Results are consistent (no +1 / -1 simultaneously)
Average score: -0.1 indicates a slight subjective improvement
(negative values indicate improvement resulting from the proposed method)

## Slide 6: 2D Test Results
Test | AVG | Viewer |  |  |  |  |  |  |  | 
 |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Balloons 25 | 0,2 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
Newspaper 25 | -0,7 | -1 | -1 | -1 | -1 | 0 | 0 | -1 | 0 | -1
Balloons 35 | 0 | 0 | 0 | 0 | 1 | -1 | -1 | 0 | 1 | 0
Newspaper 35 | -0,3 | 0 | -1 | 0 | -1 | -1 | 1 | 0 | -1 | 0
AVG | -0,2 |  |  |  |  |  |  |  |  | 
Observations:
No score above 1 or below -1 is reported.
Average score: -0.2 indicates a slight subjective improvement
(negative values indicate improvement resulting from the proposed method)

## Slide 7: Conclusion
2D and 3D subjective testings confirm that no new artifact is introduced by the quadtree limitation + predictive coding as proposed in JCT3V-B0068, experiment H3
Thanks again to the subjective viewers