## Slide 1: JCT3v-C0043/M27777: report on the relation of global view and depth format and 3DV standardization tracks
January 17, 2013
Takanori Senoh, et al. (NICT)
Masayuki tanimoto, et al.(NISRI)
Nicolce Stefanoski

## Slide 2
Introduction
This contribution reports on the AHG8 mandate:
Explore the relation of GVD (Global View and Depth) format with current 3D video standardization tracks (MVC+D, 3D-AVC, 3D-HEVC).
Core codec
(HEVC)
Global depth generator
Global depth
Residual view
View synthesizer
Depth maps
(D1,D2,D3)
Multi-views
(V1,V2,V3)
Decoded base view (V2)
Synthesized
views
Residual view generator
Decoded depth
Base view (V2)
Decoded
residual view
Decoded
global depth
Core codec
(HEVC)
Core codec
(HEVC)
Base view
(V1,V3)
Camera parameters
+Residual depth
+Residual depth

## Slide 3
Feature of GVD (fast)
Fast encoding/decoding time (Low complexity)
Comparing
to ATM
(M24984)
Comparing
to HTM
(M26013/
JCT2-A0071)
14.3%
17.4%
50%
7%
Decoding Time
Encoding Time
(view synthesis time is comparable.)

## Slide 4
Feature of GVD (reasonable quality)
Subjectively comparable quality (Reasonable coding efficiency)
Comparing to ATM
(M25242)
Comparing to HTM
(M26320/JCT2-A0172)

## Slide 5
Relationb
GVD and 3DV tracks are compensating each other as a low complexity profile and a high coding efficiency profile (JCT3V-B0058/M26750).
A harmonized bit stream syntax must be defined.
GVD
format
3DV
tracks
Low complexity profile
High coding efficiency profile
Core codec
(AVC, HEVC)

## Slide 6
Bitstream syntax (opt.1)
start_code_prefix_one_3bytes (24)
nal_unit( NumBytesInNALunit ) {
forbidden_zero_bit (1)
nal_ref_idc (2)
nal_unit_type (5)
for(i<NumBytesInNALunit) {
rbsp_byte (8)
}
}
AVC(H.264) stream syntax
start_code_prefix_one_3bytes (24)
forbidden_zero_bit (1)
nal_ref_idc (2)
new nal_unit_type (5) /* =24 */
Alternative 3D Flag (1)
gvd flag (2)
reserved_5bits (5)
nal_unit( NumBytesInNALunit ) {
forbidden_zero_bit (1)
nal_ref_idc (2)
nal_unit_type (5)
for(i<NumBytesInNALunit) {
rbsp_byte
}
}
Alternative 3D Format stream syntax
Insert 2 bytes
No change
2 byte header Insertion keeps the consistency with existing streams.
Define a new NAL unit Type when AVC, MVC, MVC+D, 3D-AVC, HEVC, MV-HEVC and 3D-HEVC codecs are used. (JCT3V-B0059/M26751)

## Slide 7
Bitstream syntax (opt.2)
Define a new VUI parameter of depth type for MVC+D, 3D-AVC, 3D-HEVC. (JCT3V-B0227/M27270)
start_code_prefix_one_3bytes(24)
nal_unit( NumBytesInNALunit ) {
forbidden_zero_bit(1)
nal_ref_idc(2)
nal_unit_type(5)=7 (Subset_SPS)
for(i<NumBytesInNALunit) {
rbsp_byte(8) (Subset_SPS)
}
}
AVC(H.264) stream syntax
subset seq_parameter_set_rbsp( ) {
seq_parameter_set_data()
bit_equal_to_one
seq_parameter_set_mvc_extension()
mvc_vui_parameter_present_flag
……
depth_type_info_present_flag
depth_type
bit_equal_to_one
seq_parameter_set_3dvc_extension()
rbps_trailing_bits()
Depth_type VUI signaling for
Alternative 3D Format

## Slide 8
Bitstream syntax (opt.3)
start_code_prefix_one_3bytes(24)
nal_unit( NumBytesInNALunit ) {
forbidden_zero_bit(1)
nal_ref_idc(2)
nal_unit_type(5)=6 (SEI)
for(i<NumBytesInNALunit) {
rbsp_byte(8) (SEI message)
}
}
AVC(H.264) stream syntax
sei_message(){
payloadType(8)=54 (depth type)
payloadSize(8)=1
depth_type (3)
rbps_trailing_bits(5)
Depth_type SEI signaling for
Alternative 3D Format
Define a new SEI message for depth type which signals view synthesis method for MVC+D, 3D-AVC and 3D-HEVC. (JCT3V-B0227/M27270)

## Slide 9: Depth Type
depth_type | interpretation
0 | Global depth for 2 view
1 | Global depth and residual depth for 2 view
2 | Global depth for 3 view
3 | Global depth and residual depth for 3 view
4 | Reserved for Warp
5…6 | Unspecified
7 | Reserved for future extension

## Slide 10
Bitstream syntax (opt.4)
start_code_prefix_one_3bytes(24)
nal_unit( NumBytesInNALunit ) {
forbidden_zero_bit(1)
nal_ref_idc(2)
nal_unit_type(5)=1,5,7,8,14,15,20
for(i<NumBytesInNALunit) {
rbsp_byte(8)
}
}
MVC(H.264) stream syntax
Depth stream using MVC syntax
When MVC or MV-HEVC is used, insert zero_byte=00 after the start code of depth streams to identify the depth streams.
In this case, depth type signaling is also necessary.
start_code_prefix_one_3bytes(24)
zero_byte(8)=00
nal_unit( NumBytesInNALunit ) {
forbidden_zero_bit(1)
nal_ref_idc(2)
nal_unit_type(5)=1,5,7,8,14,15,20
for(i<NumBytesInNALunit) {
rbsp_byte(8)
}
}
Insert 1 byte

## Slide 11
Summary
Four signaling methods are compared with their applicability and the feature.
AHG8 recommends to adopt SEI message approach.
 |  | core codec |  |  |  |  |  |  |  | 
No | signaling method | AVC (H.264) | MVC | MVC +D | 3D- AVC | HEVC | MV- HEVC | 3D- HEVC | merit | demerit
1 | new NAL unit type | ○ | ○ | ○ | ○ | ○ | ○ | ○ | no codec modification | different from 3DV extensions
2 | VUI for depth type |  |  | ○ | ○ |  |  | ○ | *** | user confusion
3 | SEI for depth type |  |  | ○ | ○ |  |  | ○ | consistent | ***
4 | SEI + byte0 insertion |  | ○ |  |  |  | ○ |  | now applicable | different from 3DV extensions