## Slide 1
1. Summary
2. Proposed Method
3. Experimental Results
4. Conclusion
Contents
CE6.h results on Simplification of Depth Modeling Mode 3 (JCT3V-C0044)
2013-01-xx
LG Electronics / Peking University
Shiqi Wang, Hongbin Liu, Siwei Ma,
Jie Jia

## Slide 2: Summary
Proposed method
  Simplification of Depth Modeling Mode (DMM) 3 by avoiding Wedgelet pattern search at decoder
Performance
Compared with HTM-5.0.1
  Solution 1
    AI : BD-rate: 0.0%, Decoding time: 98.9%
    CTC: BD-rate: 0.0%, Decoding time: 100.3%
  Solution 2
    AI : BD-rate: 0.0%, Decoding time: 98.0%
    CTC: BD-rate: 0.1%, Decoding time: 99.9%
  Solution 3
    AI : BD-rate: 0.0%, Decoding time: 98.0%
    CTC: BD-rate: 0.1%, Decoding time: 101.5%
Crosscheck
  JCT3V-C0109 (by GIST)
  JCT3V-C0191 (by Intel)
JCT3V-C0044

## Slide 3: Proposed Scheme
Background
  Wedgelet pattern search is required at decoder for DMM3, which increases decoder complexity.
  Proposed Scheme
  Solution 1
    When co-located texture luma block (CTLB) is intra coded with mode 2~34, signal index of the best Wedgelet pattern in the predefined candidate Wedgelet pattern set.
  Solution 2
    When co-located texture luma block (CTLB) is intra coded with mode 2~34, apply same method with solution 1
    When co-located texture luma block (CTLB) is not intra coded or the intra mode is 0 or 1,
      signal index of the best Wedgelet pattern in the coarse candidate Wedgelet pattern set
      Then, perform fine search as in HTM-5.0.1
JCT3V-C0044

## Slide 4: Proposed Scheme
  Proposed Scheme
  Solution 3
    When co-located texture luma block (CTLB) is intra coded with mode 2~34, apply same method with solution 1
    When co-located texture luma block (CTLB) is not intra coded or the intra mode is 0 or 1,
      signal index of the best Wedgelet pattern in the coarse candidate Wedgelet pattern set
      Disable fine search in HTM-5.0.1
JCT3V-C0044

## Slide 5
JCT3V-B0064
Experimental Results-Solution 1
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.6% | 100.6%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 103.3% | 100.4%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 100.5%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.3% | 100.6%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 103.6% | 100.7%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 103.6% | 100.4%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.1% | 99.1%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.4% | 100.5%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.9% | 100.2%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.7% | 100.3%
Table 1: comparison of HTM-5.0.1 with proposed method (CTC)

## Slide 6
JCT3V-B0064
Experimental Results-Solution 1
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.5% | 99.3%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.5% | 99.8%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 98.6%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 99.1% | 98.0%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 102.1% | 99.4%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 102.6% | 98.6%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.3% | 98.5%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 99.3%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.8% | 98.6%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.3% | 98.9%
Table 2: comparison of HTM-5.0.1 with proposed method (all intra)

## Slide 7
JCT3V-B0064
Experimental Results-Solution 2
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.2% | 100.0%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 103.4% | 99.9%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 99.8%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.3% | 100.1%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.7% | 100.2%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.6% | 100.2%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.6% | 0.4% | 101.3% | 98.8%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.6% | 99.9%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 101.0% | 99.8%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 100.8% | 99.9%
Table 3: comparison of HTM-5.0.1 with proposed method (CTC)

## Slide 8
JCT3V-B0064
Experimental Results-Solution 2
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 102.5% | 98.8%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.0% | 99.2%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.3% | 97.4%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 101.1% | 96.8%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 102.2% | 99.5%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.1% | 97.4%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.2% | 97.2%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.6% | 98.4%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | 100.9% | 97.7%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.8% | 98.0%
Table 4: comparison of HTM-5.0.1 with proposed method (all intra)

## Slide 9
JCT3V-B0064
Experimental Results-Solution 3
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | #NUM! | 101.5%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | #NUM! | 101.7%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | #NUM! | 101.7%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | #NUM! | 101.6%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | #NUM! | 102.1%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | #NUM! | 101.1%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.6% | 0.4% | #NUM! | 101.0%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | #NUM! | 101.6%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | #NUM! | 101.4%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.0% | #NUM! | 101.5%
Table 5: comparison of HTM-5.0.1 with proposed method (CTC)

## Slide 10
JCT3V-B0064
Experimental Results-Solution 3
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.5% | 98.9%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.1% | 98.8%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 103.4% | 97.4%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.1% | 0.1% | 98.2% | 97.0%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.5% | 99.6%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 101.0% | 97.3%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.6% | 97.1%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 98.3%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.8% | 97.7%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.7% | 98.0%
Table 6: comparison of HTM-5.0.1 with proposed method (all intra)

## Slide 11: Conclusion
Propose method
  Simplify Depth Modeling Mode (DMM) 3 by avoiding Wedgelet pattern search at decoder
  Performance
  Negligible influence on BD-rate when compared with HTM-5.0.1
  The Wedgelet pattern search at decoder is avoided at different extent.
It is recommended to adopt the proposed method into 3D-HEVC
JCT3V-B0064