## Slide 1
1. Summary
2. Bug Fix and Extension
3. Experimental Results
4. Conclusion
Contents
CE5.h related : Bug Fix and Extension of Illumination Compensation (JCT3V-C0046)
2013-01-17
China TV Lab. / Media Part
Hongbin Liu, Jiwook Jung, Jaewon Sung, Jie Jia, Sehoon Yea
(LG Electronics)

## Slide 2: Summary
Bug Fix
  Minor inconsistency between working draft and software for chroma component (T1)
    No influence on compression performance
  Encoder only bug – illumination compensation maybe disabled unintentionally for some inter modes at encoder (T2) .
    -0.3% and -0.3% (at most -1.0% and -0.9%) gain on two side views, -0.1% (-0.3% at most) gain on coded and synthesized view.
    Negligible encoding/decoding time increase.
Extension
  Apply idea of illumination compensation to depth coding (T3)
    T2+T3: -0.2% (at most -0.5%) gain on coded and synthesized view, 2.8% encoding time increase and negligible decoding time increase
Crosscheck
  JCT3V-CXXXX (by Hisilicon)
JCT3V-B0045

## Slide 3: Bug Fix and Extension
Bugs
  Minor inconsistency for chroma component between working draft and software (T1)
    Working draft
    xRX = xC + ( mvLX[ 0 ] >> (2 + (cIdx ? 1 : 0)) ),
    yRX = yC + ( mvLX[ 1 ] >> (2 + (cIdx ? 1 : 0)) ),
    Software
    xRX = xC + ( mvLX[ 0 ] >> (2 + (cIdx ? 2 : 0)) ),
    yRX = yC + ( mvLX[ 1 ] >> (2 + (cIdx ? 2 : 0)) ),
  Encoder only bug
    Illumination compensation maybe disabled unintentionally for all inter modes except Merge mode and SIZE_NxN mode
    Solution:
    Enable illumination compensation for all inter modes.
Extension
  Apply illumination compensation idea to depth coding
JCT3V-B0045

## Slide 4: Experimental Results
JCT3V-B0045
Three simulation sets
  Set 1: Fix inconsistency between working draft and software
  Set 2: Encoder only bug fix
  Set 3: Encoder only bug fix + apply illumination compensation to depth coding

## Slide 5: Set1: Fix inconsistency between working draft and software
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.1% | 0.0% | 0.0% | 0.0% | 0.0% | 97.5% | 100.1%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.9% | 99.9%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 100.2% | 100.1%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.7% | 100.3%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.0% | 99.7%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.9% | 100.2%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 95.1% | 98.7%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.6% | 100.0%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.9% | 99.7%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 98.6% | 99.9%

## Slide 6: Set2: Encoder only bug fix
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | -0.4% | -0.3% | -0.2% | 0.0% | -0.1% | 101.8% | 100.0%
Kendo | 0.0% | -1.0% | -0.9% | -0.5% | -0.3% | -0.3% | 101.4% | 99.8%
Newspapercc | 0.0% | -0.5% | -0.6% | -0.2% | -0.2% | -0.2% | 101.0% | 99.9%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 97.9% | 100.2%
PoznanHall2 | 0.0% | -0.1% | -0.2% | -0.1% | 0.1% | 0.0% | 101.4% | 99.9%
PoznanStreet | 0.0% | -0.2% | -0.2% | -0.1% | -0.1% | -0.1% | 104.5% | 99.9%
UndoDancer | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | -0.1% | 98.0% | 98.5%
1024x768 | 0.0% | -0.6% | -0.6% | -0.3% | -0.2% | -0.2% | 101.4% | 99.9%
1920x1088 | 0.0% | -0.1% | -0.1% | -0.1% | 0.0% | 0.0% | 100.4% | 99.6%
average | 0.0% | -0.3% | -0.3% | -0.2% | -0.1% | -0.1% | 100.8% | 99.8%

## Slide 7: Set3: Encoder only bug fix + apply IC to depth coding (comparison with Anchor)
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | -0.4% | -0.3% | -0.2% | -0.2% | -0.1% | 103.9% | 100.2%
Kendo | 0.0% | -1.0% | -0.9% | -0.5% | -0.4% | -0.4% | 103.4% | 100.3%
Newspapercc | 0.0% | -0.5% | -0.6% | -0.2% | -0.5% | -0.5% | 103.5% | 100.5%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 101.2% | 100.2%
PoznanHall2 | 0.0% | -0.1% | -0.2% | -0.1% | -0.2% | -0.1% | 102.7% | 100.3%
PoznanStreet | 0.0% | -0.2% | -0.2% | -0.1% | -0.4% | -0.2% | 102.7% | 100.2%
UndoDancer | 0.0% | -0.1% | 0.0% | 0.0% | -0.1% | -0.1% | 101.9% | 98.6%
1024x768 | 0.0% | -0.6% | -0.6% | -0.3% | -0.4% | -0.3% | 103.6% | 100.3%
1920x1088 | 0.0% | -0.1% | -0.1% | -0.1% | -0.2% | -0.1% | 102.1% | 99.8%
average | 0.0% | -0.3% | -0.3% | -0.2% | -0.3% | -0.2% | 102.8% | 100.0%

## Slide 8: Set3: Encoder only bug fix + apply IC to depth coding (comparison with set2)
JCT3V-B0045
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time
Balloons | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | -0.1% | 102.1% | 100.2%
Kendo | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 102.0% | 100.5%
Newspapercc | 0.0% | 0.0% | 0.0% | 0.0% | -0.4% | -0.3% | 102.5% | 100.5%
GhostTownFly | 0.0% | 0.0% | 0.0% | 0.0% | -0.1% | 0.0% | 103.4% | 100.0%
PoznanHall2 | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.1% | 101.2% | 100.4%
PoznanStreet | 0.0% | 0.0% | 0.0% | 0.0% | -0.3% | -0.2% | 98.2% | 100.2%
UndoDancer | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 104.0% | 100.1%
1024x768 | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.1% | 102.2% | 100.4%
1920x1088 | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.1% | 101.7% | 100.2%
average | 0.0% | 0.0% | 0.0% | 0.0% | -0.2% | -0.1% | 101.9% | 100.3%

## Slide 9: Conclusion
Propose method
  Minor inconsistency between working draft and software (T1)
    Negligible influence on compression efficiency and encoding/decoding time
  Encoder only bug – illumination compensation maybe disabled unintentionally for some inter modes at encoder (T2) .
    -0.3% and -0.3% (at most -1.0% and -0.9%) gain on two side views, -0.1% (-0.3% at most) gain on coded and synthesized view.
    Negligible encoding/decoding time increase.
  Apply idea of illumination compensation to depth coding (T3)
    T2+T3: -0.2% (at most -0.5%) gain on coded and synthesized view, 2.8% encoding time increase and negligible decoding time increase
It is recommended to adopt proposed T1, T2 and T3 into 3D-HEVC
JCT3V-B0045