## Slide 1: AHG13: On disparity vector constraints
JCT3V-C0078
O. Nakagami and T. Suzuki
Sony Corporation
Joint Collaborative Team on 3D Video Coding Extension Development of ITU-T SG 16 WP 3 and ISO/IEC JTC 1/SC 29/WG 11
3rd Meeting: Geneva, CH, 17–23 Jan. 2013

## Slide 2: Summary
Background
  Coding efficiency impact of disparity vector constraint is studied for input video having vertical offset as AHG13 activity.
Results
  If the offset of input is smaller than the constraint, BD-rate difference is 0.0% in total.
  Otherwise, the difference is more than about 40%.
Proposal
  To define two profiles as MVC; Stereo-profile and Multi-view profile, where the disparity vector constraint is mandated in the former but not mandated in the latter.
  Regarding the constraint value, fixed value 56 in pixel is proposed.
  Add a 1-bit sequence level flag in SPS extension to clarify the constraint.
Base view
Dep.view
DV Constraint

## Slide 3: Background: Disparity vector constraint
In order to enable parallel decoding of base and dependent views, it is proposed to constrain vertical component of disparity vector.
In the last meeting, coding efficiency impact for input having vertical offset was questioned.
The impact of the constraint is tested on HTM5.1 by changing following configuration parameters.
  DisparitySearchRangeRestriction and VerticalDisparitySearchRange
Related documents: JCT3V-B0037 and B0112.
Base view
Dep.view
DV Constraint

## Slide 4: DV constraint and parallel decode functionality
This contribution proposes 56 in pixel as DV constraint.
For a disparity vector DV=(DVx, DVy)
ABS(DVy) ≦ 56
, where 56 comes from 64 (max LCU size) – 8 (interpolation & loop filter).
Then, it is possible to decode a dependent view in
  2 LCU line delay for LCU size = 64
  3 LCU line delay for LCU size = 32
  4 LCU line delay for LCU size = 16
Base view
Dep.view
DV Constraint

## Slide 5: Test for MVC sequence
View
2
View
1
View
0
View
4
View
3
View
27
View
28
View
29
View
30
View
26
View
47
View
48
View
49
View
50
View
46
View
67
View
68
View
69
View
70
View
66
View
1
View
2
View
3
View
4
View
0
View
5
View
6
View
7
Flamenco2
(non-rectified)
Akko&Kayo
Breakdancers
(non-rectified)
pattern1
pattern2
pattern1
pattern2

## Slide 6: AHG13 software
It is based on HTM5.1 and has a functionality to shift input image of dependent view in a vertical direction before encode.
  The shift parameter can be set from configuration file. (VerticalShiftValueinPixel : X
It was released in the JCT3V reflector on 13th Dec 2012.
  Sharp, MediaTek and Sony did a cross check for the software before release.
CTC sequence with artificial offset is studied using the software.
View 0
View1
View2
View1
View2
X pixel
X pixel
When VerticalShiftValueinPixel = X,

## Slide 7: Summary of VerticalDisparitySearchRange=56 on AHG13 software
Sequence | MV-HEVC | 3D-HEVC
CTC Seq. with Shift 0 | 0.0% | 0.0%
CTC Seq. with Shift 16 | 0.0% | 0.0%
CTC Seq. with Shift 32 | 0.0% | 0.0%
CTC Seq. with Shift 64 | 39.9% | 68.3%
MVC Seq. Horizontal camera position (pattern1) | 0.0% | 0.0%
MVC Seq. Vertical camera position (pattern2) | 0.0% for Flamenco2_2_1_3 11.1% for Akko&Kayo_48_26_70 | 0.0% for Flamenco2_2_1_3 14.0% for Akko&Kayo_48_26_70

## Slide 8: Proposal: Two profiles as MVC
Stereo profile and Multi-view profile
Fixed DV constraint value
  1-bit sequence level flag to clarify the constraint.
 | Stereo profile | Multi-view profile
DV constraint | 56 pixel (fixed) | None
Parallel decode functionality | Always | Optional (Parallel decode SEI)
Supposed input | Aligned | Aligned/Not aligned, multi-view, Camera arrays, etc.

## Slide 9: Draft text

## Slide 10: SPS flag for bitstream level transcoding from Multiview to Stereo profile
base view0
dep.
view1
dep.
view2
dep.
view3
Multiview profile
base view0
dep.
view1
Stereo profile
Bitstream level transcode is possible
if disparity_vector_constraint_flag is equal to 1
Without the flag, only encoders know the constraint
in Multiview profile.