## Slide 1: AHG13: Disparity vector restrictions
JCT-3V 3rd Meeting: Geneva, CH, 17–23 Jan. 2013
Tomohiro Ikai
Yoshiya Yamamoto
SHARP Corporation
JCTVC-C0083:

## Slide 2: Motivation
View parallelism
  Enable parallel decoding capability of base-view and dependent-view
  Currently impossible due to disparity vector is not restricted (whole base view may be used in dependent-view decoding)
Assertion

## Slide 3: Assertion
  Mandatory constraints are required to encourage hardware/farmware design. If no mandatory constraint, designers cannot pick the parallelism as the design condition.
  Proposed parallelism scheme is the easiest way
    There are no loss
We miss the chance of very effective design if no mandatory restriction
This is not for Application but for Decoder. Thus restrict should be included in fundamental level)

## Slide 4: Proposal
Inter-view motion derivation process
  Vertical componnt of DV is always zero
MC stage
  Vertical range of DV is restricted within 56 pixel
xRef = Clip3( 0, PicWidthInSamplesL – 1, xP + ( ( nPSW – 1 ) >> 1 ) + ( ( mvDisp[ 0 ] + 2 ) >> 2 ) ) (G 127)
When dv_constraint_enabled is equal to 0, the following applies.
yRef = Clip3( 0, PicHeightInSamplesL – 1, yP + ( ( nPSH – 1 ) >> 1 ) + ( ( mvDisp[ 1 ] + 2 ) >> 2 )) (G 128)
Otherwise (dv_constraint_enabled is equal to 1) the following applies.
yRef = Clip3( 0, PicHeightInSamplesL – 1, yP)) (G 128)
When dv_constraint_enabled is equal to 1 and predFlagL0 is equal to 1 and ViewIdx is not equal to the view order index of RefPicListL0[ refIdxL0 ], the following applies.
mvL0[1] = Clip3(-56*4, 56*4, mvL0[1])
mvCL0[1] = mvL0[1]
When dv_constraint_enabled is equal to 1 and predFlagL1 is equal to 1 and ViewIdx is not equal to the view order index of RefPicListL1[ refIdxL1 ], the following applies.
mvL1[1] = Clip3(-56*4, 56*4, mvL1[1])
mvCL1[1] = mvL1[1]
If restriction is imposed in MC stage, there can’t be any evil bitstreams. Because MC stage is commonly used in decoder and encoder.
Easy data access
ref _addr = cur_addr + offset * y + x
only a few vertical offset means huge difference(offset) in address

## Slide 5: Proposal
SPS extension flag
Profiles
sps_extension( ) { | Descriptor
disparity_vector_constraint_flag | u(1)
} | 
F.1.1 Stereo profile
Bitstreams conforming to the Stereo profile shall obey the following constraints:
Sequence parameter set extensions shall have disparity_vector_constraint_flag equal to 1 only.
F.1.2 Multiview profile
Bitstreams conforming to the Multiview profile shall obey the following constraints:

## Slide 6: Experimental results in CTC
 | video 0 | video 1 | video 2 | video only | synthesized only | coded & synthesized | enc time | dec time | ren time
Balloons | 0.0% | -0.1% | 0.2% | 0.0% | 0.0% | 0.0% | 100.1% | 99.0% | 100.4%
Kendo | 0.0% | -0.3% | -0.1% | -0.1% | -0.1% | -0.1% | 99.9% | 100.2% | 99.4%
Newspapercc | 0.0% | 0.1% | 0.0% | 0.0% | -0.1% | -0.1% | 100.1% | 100.7% | 100.0%
GhostTownFly | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 99.8% | 99.6% | 99.7%
PoznanHall2 | 0.0% | 0.2% | -0.2% | 0.0% | 0.0% | 0.0% | 99.9% | 100.8% | 100.1%
PoznanStreet | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 99.8% | 100.8% | 100.3%
UndoDancer | 0.0% | 0.0% | 0.1% | 0.0% | 0.1% | 0.0% | 99.7% | 100.6% | 100.2%
1024x768 | 0.0% | -0.1% | 0.1% | 0.0% | -0.1% | -0.1% | 100.0% | 100.0% | 100.0%
1920x1088 | 0.0% | 0.1% | -0.1% | 0.0% | 0.0% | 0.0% | 99.8% | 100.4% | 100.1%
average | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 99.9% | 100.2% | 100.0%

## Slide 7: Experimental results in MVC
 | video 0 | video 1 | video 2 | video PSNR / video bitrate | video PSNR / total bitrate | synth PSNR / total bitrate | enc time | dec time | ren time
Flamenco2_0_1_3 | 0.0% | 6.8% | 6.1% | 3.4% | 3.4% |  | 100.9% | 98.2% | 
Flamenco2_2_1_3 | 0.0% | 6.6% | 4.7% | 2.2% | 2.2% |  | 100.9% | 97.5% | 
Akko&Kayo_48_46_50 | 0.0% | 0.1% | 0.1% | 0.0% | 0.0% |  | 100.0% | 100.5% | 
Akko&Kayo_48_26_70 | 0.0% | 28.1% | 29.8% | 14.7% | 14.5% |  | 97.7% | 97.2% | 
Breakdancers_4_1_7 | 0.0% | 0.4% | 0.1% | 0.2% | 0.2% |  | 99.5% | 98.5% | 
average | 0.0% | 8.4% | 8.2% | 4.1% | 4.1% |  | 99.8% | 98.4% | 

## Slide 8: Experimental results on artificially shifted CTC
 | shift = 16 | shift = 32 | shift = 64
Balloons | 2.19% | 3.64% | 48.97%
Kendo | 1.50% | 2.49% | 41.41%
Newspaper_CC | 0.91% | 1.42% | 47.13%
GT_Fly | 0.82% | 1.59% | 112.06%

## Slide 9: Conclusion
Proposal
  SPS extension flag – dv_constraint_flag
  Profiles
    stereo profile in which impose dv_constraint_flag shall be true
  Easy access
    Vertical componnt of DV is always zero in IV motion derivation
  No evil bitstream DV restriction
    DV is clipped in MC stage
Results
  No loss in CTC
  Small loss in some non-reftified video
  Significant loss in 2D array setting and large artificially shifted CTC
Recommendation
  Adopt this proposal in the next HTM and WD.
Many thanks to Sony for cross-checking this contribution (JCT3V-C0080)